## Slide 2: Present limitations and future performance for the accelerators of the CERN complex
Giovanni Rumolo, CERN, Genève, Switzerland
Accelerator Performance and Concept Workshop
10-12 December 2018, Flemings Hotel, Frankfurt am Main (Germany)
Special thanks to H. Bartosik, G. Iadarola and R. Tomás.
Acknowledgements: S. Albright, R. Alemany, D. Amorim, S. Antipov, F. Antoniou, G. Arduini, M. Barnes, M. Beck, E. Benedetto, N. Biancacci, C. Bracco, R. Bruce, O. Brüning, X. Buffat, M. Carlà, P. Costa Pinto, J. Coupard, H. Damerau, G.P. Di Giovanni, R. Di Maria, S. Fartoukh, V. Forte, M. Fraser, B. Goddard, K. Hanke, A. Huschauer, V. Kain, I. Karpov, A. Lasheen, K. Li, M. Meddahi, L. Mether, E. Métral, B. Mikulec, N. Nasresfahani, Y. Papaphilippou, T. Pieloni, D. Quartullo, S. Redaelli, J. Repond, A. Romano, L. Rossi, B. Salvant, M. Schenk, R. Scrivens, E. Shaposhnikova, G. Skripka, M. Taborelli, H. Timko, M. Van Gompel, F. Velotti, C. Vollinger, C. Zannini.

## Slide 3
Why upgrades and what are the upgrades for LHC and its injector chain?
Present limitations and future performance of the LHC injectors
  Present performance limitations  beam dynamics challenges
  How far we can go with the upgrades
Beam dynamics challenges for LHC

## Slide 4
Why upgrades and what are the upgrades for LHC and its injector chain?
Present limitations and future performance of the LHC injectors
  Present performance limitations  beam dynamics challenges
  How far we can go with the upgrades
Beam dynamics challenges for LHC

## Slide 5: Goals of upgrades in a nutshell (HL-LHC)
The High Luminosity LHC (HL-LHC) upgrade
Aims at 3000 (4000) fb-1 total integrated luminosity over HL-LHC run (2026 – 2037)
Based on operation at levelled luminosity of 5 (7.5) x1034 cm-2s-1 by lowering b*
 | Nb (x 1011 p/b) | ex,y, (mm) | Bunch spacing | Bunches
HL-LHC beam | 2.3 | 2.1 | 25 ns | 4x72 per injection
Beam properties @LHC injection
Notes: Both the consideration of energy deposition by collision debris in the interaction region magnets, and the necessity to limit the peak pile-up in the experimental detector, impose an a priori limitation upon peak luminosity. The consequence is that HL-LHC operation will have to rely on luminosity levelling.

## Slide 6: Goals of upgrades in a nutshell (LIU)
The High Luminosity LHC (HL-LHC) upgrade
Aims at 3000 (4000) fb-1 total integrated luminosity over HL-LHC run (2026 – 2037)
Based on operation at levelled luminosity of 5 (7.5) x1034 cm-2s-1 by lowering b*
The LHC Injectors Upgrade (LIU)
Aims at matching the beam parameters at LHC injection with HL-LHC target
Needs to deploy means to overcome performance limitations in all injectors!
 | Nb (x 1011 p/b) | ex,y, (mm) | Bunch spacing | Bunches
HL-LHC target | 2.3 | 2.1 | 25 ns | 4x72 per injection
Present | 1.3 | 2.7 | 25 ns | 4x72 per injection
Beam properties @LHC injection
Notes: Invest on improved shielding, ventilation, etc to make accesses possible when needed

## Slide 7: A view on LHC Injectors and LIU
Linac4
160 MeV H- charge exchange injection
Acceleration to 2 GeV with new main power supply and new RF systems
Main RF system (200 MHz) upgrade
Longitudinal impedance reduction & anti-ecloud coating
New beam dump and protection devices
Acceleration of H- to 160 MeV
Nominal 40 mA within 0.4 mm
2 GeV injection
New RF equipment including broad-band feedback
Notes: PSB
  Connection to Linac4  New H- charge exchange injection at 160 MeV from Linac4 to double brightness of LHC beams
  Acceleration to 2 GeV
    New main power supply POPS-B
    Replacement of C02-C04-C16 RF systems by Finemet based RF system
PS
  New injection at 2 GeV for protons to mitigate space charge
  RF improvements to improve beam quality and increase longitudinal coupled bunch instability threshold
    Impedance reduction of the RF systems
    Installation of new Finemet RF system as longitudinal feedback
  Operational deployment of transverse feedback system
SPS
  200 MHz RF system upgrade
    Rearrangement of cavities and power upgrade
    New LLRF including slip stacking capability
  Electron cloud mitigation and impedance reduction to increase intensity reach
    a-C coating of QFs + one full arc
    QF-type flange shielding and HOM damping in 200 MHz cavities
  New beam dump system in LSS5 and new design of protection devices to comply with the target HL-LHC beam parameter values

## Slide 8: A view on LHC and HL-LHC

## Slide 9
Why upgrades and what are the upgrades for LHC and its injector chain?
Present limitations and future performance of the LHC injectors
  Present performance limitations  beam dynamics challenges
  How far we can go with the upgrades
Beam dynamics challenges for LHC

## Slide 10: Present performance limitations
PSB injection: Brightness limited by efficiency of multi-turn injection process and space charge effects
PS and SPS injection: Brightness limited by space charge – DQ<0.31 (PS) and 0.21 (SPS), to limit beam degradation
PS cycle: Bunch intensity limited by longitudinal coupled bunch dipolar instability
SPS cycle: Bunch intensity limited by RF power, longitudinal coupled bunch instability
 | Nb (x 1011 p/b) | ex,y, (mm)
HL-LHC target | 2.3 | 2.1
Present | 1.3 | 2.7

## Slide 11: Present performance limitations
PSB injection: Brightness limited by efficiency of multi-turn injection process and space charge effects
PS and SPS injection: Brightness limited by space charge – DQ<0.31 (PS) and 0.21 (SPS), to limit beam degradation (H. Bartosik’s talk)
PS cycle: Bunch intensity limited by longitudinal coupled bunch dipolar instability
SPS cycle: Bunch intensity limited by RF power, longitudinal coupled bunch instability
 | Nb (x 1011 p/b) | ex,y, (mm)
HL-LHC target | 2.3 | 2.1
Present | 1.3 | 2.7

## Slide 12: Lifting the brightness limitations
Halve the slope of the PSB brightness line
  160 MeV H- charge exchange injection from Linac4 replacing 50 MeV multiturn injection from Linac2
Measured points (2012 – 2017)
PyORBIT simulations

## Slide 13: Lifting the brightness limitations
Halve the slope of the PSB brightness line
  160 MeV H- charge exchange injection from Linac4 replacing 50 MeV multiturn injection from Linac2
Reduce space charge at PS injection to accommodate same tune spread as current LHC beam (DQy=-0.31)
  Increase of PS injection energy from 1.4 GeV to 2 GeV
  Increase of longitudinal emittance (compatibly with other constraints) at transfer in order to gain from decreasing lmax and increasing d=(dp/p0)

## Slide 14: Lifting the PS intensity limitation
Instability
Bunch current limited to 1.6e11 p/b at extraction
Above 1.6e11 p/b longitudinal coupled bunch instabilities appear on the ramp and at flat top for nominal longitudinal emittance
  Dipolar oscillation, caused by 10 MHz RF system impedance (as found also in simulations)

## Slide 15: Lifting the PS intensity limitation
Longitudinal feedback based on broad-band Finemet cavity as kicker installed and deployed over the last three years
Feedback off (Nb = 1.8 · 1011 ppb)
Feedback on (Nb = 1.8 · 1011 ppb)

## Slide 16: Lifting the PS intensity limitation
Longitudinal feedback based on broad-band Finemet cavity as kicker installed and deployed over the last three years
With transverse optimisation, beam is now stable up to 2.6e11 p/b
Nb = 2.6 ∙ 1011 ppb, DN/N < 5%

## Slide 17: Lifting the PS intensity limitation
Longitudinal feedback based on broad-band Finemet cavity as kicker installed and deployed over the last three years
With transverse optimisation, beam is now stable up to 2.6e11 p/b
Goal in terms of intensity out of the PS reached!

## Slide 18: Lifting the SPS intensity limitation
Beam loading in the present 200 MHz TW RF system – intensity limited to about 1.3e11 p/b
Longitudinal instabilities during ramp with very low threshold currently cured by
  800 MHz RF system in bunch shortening mode
  Controlled emittance blow-up (with constraint of 1.7 ns bunch length at extraction)
Bunch length spread
Only RF power upgrade
Still lagging 20% below target …
Notes: (2x4 & 2x5 section cavities)
Bunch length variation due to controlled emittance blow-up in presence of beam loading
More 800 MHz voltage is available but it is kept at 10% level of 200 MHz voltage to avoid region with ω’(J)=0 during ramp

## Slide 19: Lifting the SPS intensity limitation
Impedance reduction needed in addition
  Shielding of a subset of vacuum flanges
  Enhanced damping of HOMs of 200 MHz (factor 3 desired)  baseline for LIU
  Serigraphy on the injection kickers MKP
new HOM coupler

## Slide 20: Other SPS intensity limitations?
Transverse Mode Coupling Instability (TMCI) threshold was raised from 1.6e11 p/b to 4e11 p/b when switching to a low gamma transition (gt) optics
original SPS optics
1.6e11
low gt SPS optics
x2.5
measurements confirm 2.5 times higher threshold!
4.0e11

## Slide 21: Other SPS intensity limitations?
Electron cloud mitigation relies mainly on
  Beam induced scrubbing (it worked, it still works!)
  Coating with a-C the chambers of the focusing quadrupoles and adjacent drift chambers

## Slide 22: Summary: Future LIU performance
PSB injection: from Linac4
PS injection: 2 GeV, larger longitudinal emittance
PS cycle: Longitudinal coupled bunch feedback system, impedance reduction
SPS cycle: RF power upgrade, longitudinal impedance reduction, beam scrubbing & partial a-C coating, low gt optics
 | Nb (x 1011 p/b) | ex,y, (mm)
HL-LHC target | 2.3 | 2.1
Present | 1.3 | 2.7
LIU matches HL-LHC

## Slide 23
Why upgrades and what are the upgrades for LHC and its injector chain?
Performance of the LHC injectors
  Present performance limitations  beam dynamics challenges
  How far we can go with the upgrades
Beam dynamics challenges for LHC

## Slide 24: LHC beam stability
LHC transverse beam instabilities observed with different types of beams and at different stages of the LHC cycle
2010, single bunch
during the ramp
2011-12, 50 ns beam
during b* squeeze or while adjusting the beams to collide
2015-18, 25 ns beam
at injection

## Slide 25: LHC beam stability
LHC transverse beam instabilities observed with different types of beams and at different stages of the LHC cycle
Sources are mainly transverse impedance (loss of Landau damping) and, at least with 25 ns beams, electron cloud
Controlled through “extreme” machine settings, e.g. at 6.5 TeV Q’=+15, octupole strength close to maximum, maximum damper gain and bandwidth
Need to gain some margin with stabilisation knobs for operation with HL-HLC beam parameters (double intensity)  Impedance reduction

## Slide 26: LHC beam stability
Due to the small gaps, at 6.5 TeV the most critical impedance contributor (80%) is collimators
Within HL-LHC secondary collimators replaced by new ones with Mo-Gr jaws having same robustness and higher conductivity  One order of magnitude lower RW impedance
Secondary collimators in IR-7
Primary collimators
Everything else
Geometric
Resistive wall
Present
Upgrade
Impedance reduction
secondary collimators

## Slide 27: LHC beam stability
Example: Effect of impedance reduction on TMCI threshold
Present LHC impedance model
Instability
HL-LHC impedance
(after collimator impedance reduction)
Instability

## Slide 28: Beam induced heat load in LHC
High heat load on beam screen in cold regions (cryo limit 160 W/hc in the arcs)
  With 25 ns beams
  Much higher than calculation from impedance + synchrotron radiation
  Different among arcs (factor ~3)
Most observations compatible with electron cloud, probably localised in some magnets
  Spread of Secondary Electron Yield between 1.15 and 1.35
S12
S81
S23
S78
S34
S67
S45
S56
ATLAS
CMS
LHCb
ALICE
SEY < 1.25
SEY > 1.30
Notes: Only 25 ns, scaling with bunch intensity (linear, threshold at just below 4e10 p/b), power loss localised in last bunches of trains from RF measurements of stable phase, at least partly scrubbable, behaviour in dipoles and quadrupoles

## Slide 29: Beam induced heat load in LHC
We can sum up contributions to e-cloud from all parts of the arc assuming SEY from heat load measurements (SEY=1.25 – 1.35)
  HL-LHC
e-cloud in quadrupoles
e-cloud in dipoles
e-cloud in drifts
Impedance
Synchrotron radiation
  HL-LHC
Heat load [kW/arc]
Bunch intensity [1011 p/bunch]
Heat load [kW/arc]
Bunch intensity [1011 p/bunch]
SEY=1.25
SEY=1.35
  8 kW/arc (~160W/hcell)
Low-load sectors ok with HL-LHC
High-load sectors above capacity for HL-LHC

## Slide 30: Beam induced heat load in LHC
We can sum up contributions to e-cloud from all parts of the arc assuming SEY from heat load measurements (SEY=1.25 – 1.35)
Although high-load sectors might be not fully compatible with HL-LHC operation, a safety net is the filling scheme …
25 ns (2760b)
25 ns slot
72b
25 ns slot
8b
4e
8b
4e
8b
4e
8b
8b+4e (1972b)
 Pure 25 ns and 8b+4e can be combined to reach the maximum heat load

## Slide 31: To wrap up and conclude
LHC and its injectors set to major upgrades: LIU, HL-LHC
  Injectors upgraded in 2019-2020, LIU beam commissioning in 2021-2024
  LHC upgraded in 2024-2025 and HL-LHC era >2026
Overcoming performance limitations in the LHC injectors
  Produce/preserve higher brightness  Linac4, mitigation of space charge, optimised transfers
  Produce more intense beams  Impedance reduction, electron cloud mitigation, active feedback, longitudinal emittance blow up, enhanced Landau damping, optics change
Beam dynamics challenges for upgrade of LHC
  Preservation of beam stability  Landau damping & impedance reduction, electron cloud build up & instability scaling
  Beam induced heat load  Low e-cloud filling pattern

## Slide 32
THANK YOU FOR YOUR ATTENTION

## Slide 33: Timeline of the projects
Proton Runs
Technical Stops
Long Shutdowns
Beam Commissioning
Run 2
LS2
Mainly LIU work
LS3
Mainly HL-LHC work
Run 3
Run 4
Run 3: LIU beam commissioning through the injector chain
Run 4: HL-LHC run with a period of ‘luminosity learning’
We are here

## Slide 34: Lifting the PS intensity limitation
Longitudinal feedback based on broad-band Finemet cavity as kicker installed and deployed over the last three years
With transverse optimisation, beam is now stable up to 2.6e11 p/b
Goal in terms of intensity out of the PS reached!
Brightness still pending Linac4 and space charge mitigation in PS
2.6e11 p/b, 5 mm

## Slide 35: HL-LHC single particle dynamics
Strong effect of linear and nonlinear errors in IRs due to large b  Low Dynamic Aperture in absence of correction
Pre-computed corrections from magnetic measurements needed even for basic optics measurements
b∗ levelling will require commissioning of a large number of optical configurations  Challenge for efficiency of the optics measurement and correction tools
Simulated evolution of an HL-LHC physics fill with baseline parameters
Notes: needed to fulfil the tight tolerances coming from DA or coherent stability constraints

## Slide 36: Luminosity projection

## Slide 37: LHC beam stability
Strong instabilities observed at 450 GeV with 25 ns beams, in both x and y
  Stabilized with high chroma (Q’=20), high octupole strength (DQ=1.5e-3)
  Caused mainly by electron cloud in quadrupoles
Simulations predict more stability for HL-LHC (thanks to lower electron cloud)
Instability simulations (450 GeV)
(e-cloud in the arc quadrupoles - SEY 1.3)
arc quadrupoles
e-cloud buildup simulations

## Slide 38: Beam induced heat load in LHC
High heat load on beam screen in cold regions (cryo limit 160 W/hc in the arcs)
  With 25 ns beams
  Much higher than calculation from impedance + synchrotron radiation
  Different among arcs
Most observations compatible with electron cloud, probably localised in some magnets (or even some parts of magnets)
  Coating with a-C for triplet quadrupoles to decrease SEY
Heat load
per half cell
8 Aug 2017
Notes: Only 25 ns, scaling with bunch intensity (linear, threshold at just below 4e10 p/b), power loss localised in last bunches of trains from RF measurements of stable phase, at least partly scrubbable, behaviour in dipoles and quadrupoles

## Slide 39: E-cloud build up with intensity
Underlying mechanism:
When the SEY decreases the energy window for multipacting becomes narrower
For high bunch intensity the e- spectrum drifts to higher energies and can move outside the most efficient region

## Slide 40: Inferring the average SEY
6.5 TeV
Simulations
450 GeV
6.5 TeV
Measurements
High-load
Low-load

## Slide 41: Inferring the average SEY
450 GeV
Simulations
450 GeV
6.5 TeV
Measurements
High-load
Low-load

## Slide 42: Beam induced heat load in LHC
Two fold issue for HL-LHC
  Less margin for cryostat with HL-LHC parameters (three-fold contribution from impedance and synchrotron radiation)
  How does the additional load scale with bunch intensity?  We can make a prediction only if we assume it is caused by electron cloud
Maximum allowed by cryogenics
Margin
~7 kW
e-cloud S12
(2017)
~6 kW
Margin
~4 kW
2556b
1.15e11 p/bunch
6.5 TeV
2760b
2.2e11 p/bunch
7 TeV
e-cloud S34
(2017)
~2kW

## Slide 43: Some other challenges in LHC
Beam-beam interaction
  Head-on beam-beam tune shift limit (based on past experience) currently surpassed
  Effect of the long-range  6s DA comfortably achieved during the whole levelling process, even including the chromaticity and octupole settings necessary for beam stability
Incoherent emittance growth along the cycle
  Larger than expected from Intra Beam Scattering (with margin), but impact de-facto mitigated by b* levelling
  Influence of noise  minimise sources by careful design of power converters, crab cavity controls, transverse damper upgrade (it might also benefit coherent instabilities)
Beam halo active control for machine protection
  Potentially large halo generation with HL-LHC beams, especially during commissioning
  Cleaning techniques under study, option for Hollow Electron Lens
Notes:  adjust crossing angle during levelling process to reduce the pile-up density and the radiation on the inner triplets

## Slide 44: Some other challenges in LHC
Beam-beam interaction
  Head-on and long range (dynamic aperture during leveling), compensation techniques
Incoherent emittance growth along the cycle
  Sources to be understood, influence of noise
Large beam halo generation with future beams
  Halo active control for machine protection, cleaning techniques under consideration
RF power and longitudinal stability
  Power consumption for future injection voltage, transient beam loading, instabilities at flat bottom, longitudinal emittance blow up
Notes:  adjust crossing angle during levelling process to reduce the pile-up density and the radiation on the inner triplets