## Slide 1: FCC RF beam dynamics and HOM power challenges
Ivan Karpov, CERN
Acknowledgments: P. Baudrenghien, O. Brunner, A. Butterworth, R. Calaga, E. Shaposhnikova, D. Teytelman

## Slide 2: Future circular electron-positron collider FCC-ee
Tunnel circumference, km
Experimental program has 4 energy stages
Maximum acceptable power loss per beam due to synchrotron radiation is 50 MW
 | Z | W | H | 
Energy/beam [GeV] | 45.6 | 80 | 120 | 182.5
Energy loss/turn [GeV] | 0.036 | 0.34 | 1.72 | 9.21
RF voltage/beam [GV] | 0.1 | 0.75 | 2.0 | 10.93
Beam current [mA] | 1390 | 147 | 29 | 5.4
 | Z | W | H | 
 | 45.6 | 80 | 120 | 182.5
 | 0.036 | 0.34 | 1.72 | 9.21
 | 0.1 | 0.75 | 2.0 | 10.93
 | 1390 | 147 | 29 | 5.4

## Slide 3: Beam-cavity interaction challenges in FCC-ee Z
Power losses due to high order modes (HOM) must be extracted by HOM couplers (maximum 1 kW/coupler in SC RF)
Transient beam loading leads to bunch length spread or/and to shift of collision point, therefore to possible reduction of luminosity
The Z machine has the highest beam current and the lowest total RF voltage

## Slide 4: HOM power loss
Simulated cavity
impedance
Normalized Fourier harmonics
of beam current
– average beam current
– revolution frequency
– revolution harmonic number
Power losses depend on HOM impedance and beam spectrum (ring filling schemes)

## Slide 5: Possible beam filling schemes
Abort gap,
= 2 μs
Bunch trains
Train spacing,
Beam spectrum is dominated by:
lines (always present)
lines (depending on number of trains)
Bunch spacing,
2.5 ÷ 17.5 ns
Number of trains,
Number of bunches
per train,

## Slide 6: Possible beam filling schemes
Beam spectrum is dominated by:
lines (always present)
lines (depending on number of trains)
Defined by train spacing
Defined by bunch spacing

## Slide 7: LHC-like superconducting single-cell cavity
“Continuous” spectrum
Cut-off frequency
HOM
Fundamental mode
ABCI* and CST** results:
Fundamental mode at 400.79 MHz with = 42.3 Ω
HOM below cut-off frequency at 694 MHz,
1/e – decrease of the beam
power spectrum,
Collisions on
ps
Collisions off
ps
*Azimuthal Beam Cavity Interaction code, http://abci.kek.jp/abci.htm
**CST EM STUDIO, https://www.cst.com/products/cstems
Contributions of impedance below and above cut-off frequency are important for power loss calculations

## Slide 8: Power loss above cut-off frequency
Power loss is moderate for the present cavity design for bunches in collisions ( kW)
There is a weak dependence on train spacing and bunch spacing
Collisions on
Assumptions: total current ≤ 1.4 A, number of bunches ≤ 16640, abort gap 2 μs, bunch population 1.7e11
Variable parameters: number of bunches in the train, number of trains, train spacing
Collisions on
Collisions off
Train spacing (RF buckets)

## Slide 9: Power loss for HOM below cut-off frequency
Power losses of about 1 kW are for small + “resonant” cases with high
Damping of the mode for longitudinal stability should be moderate
Resonant cases should be identified
Longitudinal coupled-bunch instability growth rate due to HOM
If stability
– growth time
– radiation damping time
– slip factor
– beam energy
– synchrotron tune
Stability threshold
MHz,
Quality factor, Q
Train spacing (RF buckets)

## Slide 10: Power losses for different filling schemes
Some filling schemes should be avoided in machine operation (restrictions for train and bunch spacings)
Resonant case when the beam spectral line overlaps with HOM*
Rounded off value
*I.Karpov, R. Calaga, E. Shaposhnikova, Phys. Rev. Accel. Beams 21, 071001 (2018)
Train spacing (RF buckets)
Overlap with spectral lines defined by bunch spacing

## Slide 11: More “general” case
Operation settings define recommendations for the cavity geometry
Safe
Dangerous
Present design
Resonant frequency scan,

## Slide 12: Transient beam loading
*D. Boussard, CERN-SPS-ARF-DB-GW-NOTE-84-9, 1984 **J. Tückmantel, CERN-ATS-Note-2011-002, 2011
Model of superconducting RF cavity linked to generator via circulator*
Generator current**
Reflected current
Transmission line
Generator
Load
Cavity detuning is , ,
Circulator

## Slide 13: Beam induced transients
Cavity voltage
amplitude and phase modulations
Beam current
Average synchronous phase
amplitude and phase modulations
System of equations for can be obtained
Solution depends on the choice of and
Generator current
Synchronous phase

## Slide 14: Optimal parameters
Optimal detuning
for superconducting cavities
Generator power*
It can be minimized for given:
average beam current , with - bunch form factor
average cavity voltage
Optimal loaded quality factor
*J. Tückmantel, CERN-ATS-Note-2011-002, 2011
**K. W. Robinson, Stability of beam in radiofrequency system, Rep. CEAL-1010 (1964)
Beam is unstable for optimal parameters because the second Robinson limit** is reached if there are no loops around cavity

## Slide 15: Small-signal Pedersen model
Transfer functions* from beam current amplitude
cavity voltage amplitude
beam phase
cavity voltage phase
For “magic” detuning**
*F. Pedersen, Beam loading effects in the CERN PS Booster, IEEE Trans. Nucl. Sci. 22, 1906 (1975)
**F. Pedersen, RF cavity feedback, CERN-PS-92-59-RF, 17 (1992)
- cavity filling time, – complex variable
Magic detuning can be used for transient beam loading calculations
Small modulations: ,

## Slide 16: Transient beam loading in FCC-ee Z
There is a strong modulation due to the abort gap and a fine structure due to the gaps between trains
Reasonable agreement between time-domain and frequency-domain calculations
,

## Slide 17: Results for FCC-ee Z
Phase modulations can result in collision point shift, but It can be compensated by proper matching of abort gap transients (for example in the LHC*)
Bunch length modulations can still affect luminosity
Bunch length
Synchrotron tune
– harmonic number
– energy spread
For baseline parameters, the abort gap length < 2 µs and bunch length spread can be neglected
Time domain
Frequency domain
*T. Mastoridis, P. Baudrenghien, and J. Molendijk, Phys. Rev. Accel. Beams 20, 101003 (2017)

## Slide 18: Conclusions
HOM power loss contributions:
  From impedance above cutoff frequency is about 3 kW,
  From overlap of HOM below cutoff frequency with beam spectral line is below 1 kW for train spacing larger than 100 RF buckets, if 10 ns and 17.5 ns bunch spacing are excluded from operation.
HOM frequency ranges for new cavity designs which are “safe” for given bunch spacings were identified.
Beam induced transient are dominated by abort gap:
  collision point shift still can be eliminated by matching abort gap transients,
  for < 2 µs bunch length spread < 2%.

## Slide 19: Thank you for your attention!

## Slide 20: Second Robinson limit
Second Robinson limit above transition (no loops around cavity)*
for optimal parameters ( and )
*K. W. Robinson, Stability of beam in radiofrequency system, Rep. CEAL-1010 (1964)

## Slide 21: Shift of the resonant frequency
→ There are many cases when the spectrum line hits the resonant line → Not all of them are dangerous
“Resonant” condition*
Rounded off value
*I.Karpov et al., CERN-ACC-NOTE-2018-0005 (2018)

## Slide 22
Dependence on the train spacing for bunch spacing of 17.5 ns

## Slide 23: Beam current for different filling schemes

## Slide 24: Beam-cavity interaction challenges in FCC-ee Z
→ Power losses due to high
order modes (HOM)
→ Transient beam loading
→ Longitudinal coupled-bunch
instability
Parameter | Value
Beam current, | 1.39 A
Number of bunches, | 16640
Minimum abort gap, | 2 µs
RF frequency, | 400.79 MHz
of fundamental mode | 42.3 Ω
Cavity voltage, | 1.91 MV
Number of cavities, | 52
Harmonic number, | 130680
Radiation damping time, | 414 ms
Parameter | Value
 | 1.39 A
 | 16640
 | 2 µs
 | 400.79 MHz
 | 42.3 Ω
 | 1.91 MV
 | 52
 | 130680
 | 414 ms

## Slide 25: Impedance of LHC-like single-cell cavity
“Continuous” spectrum
Cut-off frequency
HOM
Fundamental mode
Only one mode below cut-off frequency with parameters:
MHz, (CST EMS simulations), quality factor= ?
1/e – decrease of the beam
power spectrum,
With BS* ps
Without BS ps
*Beamstrahlung effect
Impedance calculation using ABCI
Axisymmetric structure
+
Gaussian bunch
Wake potential
Impedance
MHz

## Slide 26: Transient beam loading
*D. Boussard, CERN-SPS-ARF-DB-GW-NOTE-84-9, 1984 **J. Tückmantel, CERN-ATS-Note-2011-002, 2011
Model of superconducting RF cavity linked to generator via circulator*
Generator current**
Reflected current
Transmission line
Generator
Load
From circuit equations:
Assumptions:
all dynamic variables are proportional to with varying amplitude
Slow change of the complex voltage amplitude,
Cavity detuning is , ,

## Slide 27: Fundamental impedance driven instability
Synchrotron radiation damping
The growth rate of the longitudinal coupled-bunch mode m*
*For example in A. Chao, Physics of Collective Beam Instabilities in High Energy Accelerators, 1993
For magic detuning (about )
the most unstable mode is -4
Fundamental cavity impedance

## Slide 28: Mitigation by direct RF feedback*
*D. Boussard, Control of cavities with high beam loading, IEEE NS-32 (1985)
The flat response is achieved for , loop delay ns (similar to LHC)
Growth rates of all unstable modes are smaller than synchrotron radiation damping rate
To increase stability margins one-turn delay feedback (similar to SPS, LHC) or more sophisticated double peaked comb filter (PEP II) can be used