## Slide 1: FCC-hh (single beam) collective effects
O. Boine-Frankenheim
S. Arsenyev, D. Schulte (CERN)
D. Astapovych, U. Niedermayer (TU Darmstadt)
V. Kornilov (GSI)
B. Riemann (TU Dortmund)
L. Mether, T. Pieloni, C. Tambasco (EPFL, Lausanne)

## Slide 2: Future Circular Collider Study GOAL: CDR and cost review until 2019
International FCC collaboration (CERN as host lab) to study:
pp-collider (FCC-hh)  main emphasis, defining infrastructure requirements
80-100 km tunnel infrastructure in Geneva area
e+e- collider (FCC-ee) as potential first step
p-e (FCC-he) option
HE-LHC with FCC-hh technology

## Slide 3: FCC-hh reference parameters (for beam stability)
Circumference [km] | 100
Energy [TeV] | 3-50
Bunch charge | 1011
Bunch spacing [ns] | 25
Bunch length [cm] | 8
Number of bunches | ≈ 10000
Qx / Qy | 108.28 / 107.31
Qs | 10-3-5 x 10-3
Normalized emittance | 2.2 μm
Luminosity [cm-2s-1] | 5 x 1034
FCC vs. LHC
Larger circumference, lower frequency of 1 kHz (5:1)
screen temperature: 50 K (5:2)
Smaller screen diameter (2:3), thicker (4:1) Cu coating
Smaller beam (1:3)
LHC-like bunches (1:1)
Larger average β-function (2:1)
Aim of the studies: Predict instability thresholds
-> Use LHC results together with numerical tools.

## Slide 4: Beam stability: LHC vs FCC
Larger circumference (5:1) -> lower frequency: 1 kHz vs 8 kHz
Smaller screen diameter (2:3) -> larger impedance (factor 3)
screen temperature: 50 K (5:2), maximum field 16 T (2:1) -> changed conductivites
Larger average β-function (2:1) -> growth rates
Smaller beams (1:3) -> weaker Landau damping, e-cloud thresholds
LHC-like bunches and 25 ns spacing (1:1)
Growth rate for transverse coupled bunch instabilities:
TMCI single bunch threshold bunch intensity:

## Slide 5: FCC-hh beam pipe design and coatings
or AC
LHC vs FCC:
20 W/m synchrotron radiation (100:1)
FCC beam pipe (right) optimized for
synchrotron radiation and suppression
of photo electrons
LHC
FCC
(old
design)
or a-C for e-cloud
Cu coating
for impedance
Laser treated beam screen (option)
FCC
(new)

## Slide 6: Collective effects in FCC and codes
e-
Electron clouds:
created wall emission and other mechanisms.
-> heat loads, emittance growth and instabilities
OpenCloud (O. Haas, F. Petrov)
PyCloud (G. Iaderola, CERN)
beam pipe
Bunch
Beam-beam interaction:
Can cause coherent instabilities.
Challenge for simulations:
Interplay of different mechanisms !
Wake fields and impedances:
-> heat loads and instabilities
Image current
(lab system)
Time-domain:
CST particle studio (3D)
Frequency domain:
BI2D (U. Niedermayer)
„Vlasov solvers“:
DELPHI (N.Monet), NHT (A. Burov)
Tracking codes:
PATRIC (V. Kornilov)

## Slide 7: Resistive wall impedance: LHC and FCC-hh
b=0.012 m
b=0.02 m
(Thick) resistive wall impedance
Coupled bunch growth rate:
FCC
LHC
LHC:
few kHz
FCC: kHz
(chromatic phase shift)
(Sacherer 1974)
Transverse impedances (vertical real part)
growth time at 3.3 TeV:
approx. 50 turns
at 50 TeV:
approx. 500 turns
LHC at 7 TeV:
approx. 2000 turns
(lowest sideband)
Remark: difference between injection and top energy due to magnetoresistance.

## Slide 8: Single bunch TMCI threshold: Effect of coating
„Full“ Cu coated:
Partially Cu coated:
TMCI threshold bunch intensity:
(synchrotron tune)
(tune shift)
Design Cu coating
(d=0.3/0.1 mm)
‚Full‘ Cu
coating

## Slide 9: HTS coated FCC screen (R&D)
P. Krkotic,
U. Niedermayer
“depinning frequency“
B=16T
Hybrid coating
Hybrid coating (HTS stripes):
Possible reduction of the resistive wall instability growth rates by factor 5-6.
TMCI thresholds !
P. Krkotic et al., High-temperature superconductor coating for coupling impedance reduction in the FCC-hh beam screen, Nucl. Instr. Meth. A, (2018)

## Slide 10: Landau damping with octupoles
actions variables )
Tune shifts from octupoles:
From LHC to FCC-hh:
72 x 168 octupoles
length of octupole
# of magnets
Scaling with energy:
2D dispersion relation:
Landau octupoles
k=0: transverse feedback system

## Slide 11: Landau damping of head-tail modes
k=0 k=1 k=2
LD of non-rigid head-tail modes:
PATRIC:
Particle tracking with octupoles and resistive wall wake.
V.Kornilov

## Slide 12: Coupled bunch mode coupling
„Vlasov solvers“: DELPHI (N. Monet), Nested Head-Tail (NHT) (A. Burov)
S. Arsenyev, H. Klinkenberg (2018)

## Slide 13: „Advanced“ Landau damping: Electron lenses
Similar to the beam-beam force !
Tune shift induced by a
counter-propagating electron beam:
Electron lenses
Example: One lens (l=2 m, Ie <1 A) in FCC would provide a tune spread larger than the LHC-like octupoles octupoles.
V. Shiltsev et al., PRL (2017)
Tune shift:
Remark: Octupoles will also stabilize unstable beams, at the cost of a larger emittance.

## Slide 14: Electron cloud in FCC
Example from openECLOUD:
Saturated e-cloud density in FCC
drift section without any coating
In dipole magnet:
The coating should cover the full top and bottom of the chamber
(pyCloud, L. Mether).
Pipe with a-C coating
If the the FCC screen will be (partly) a-C coated (with SEY lower/equal 1) and the screen design avoids photoelectron entering in the pipe, electron could induced instabilities should be absent in the FCC.

## Slide 15: Conclusions
FCC-hh beam stability: Benefit from LHC experience and models. Understand scaling and „error bars“ of simulation predictions.
Impedances studies:
Pipe and coatings: Cu and HTS (option) for impedance , aC or Laser (option) for SEY
Impedance library
Beam stability and limits (remark: head loads dominated by synchrotron radiation).
Coupled bunch damped by Octupoles (k>=0) and Feedback (k=0)
Single bunch TMCI (might be an issue with laser coating and collimators)
Coupled bunch TMCI
Electron lenses and RF Quadrupoles for Landau damping
Electron cloud:
(Minimum) coating for e-cloud suppression
Role of residual photo electrons

## Slide 16
Backup

## Slide 17: Landau damping at very high energies
The good news:
The OK news:
The bad news:
(tune spread required for LD)
(tune spread provided by octupoles)
(instability growth rate)
circumference
length of magnet
normalized emittance
# of magnets
From LHC to FCC-hh: 72 x 168 octupoles
FCC transverse beam stability:
k=0 coupled bunch modes: Feedback (50 turns)
k>1 modes: Landau damping (octupoles)

## Slide 18: 2D impedance code in frequency space
U. Niedermayer et al., Space charge and resistive wall impedance computation in the frequency domain using the finite element method, Phys. Rev. ST-AB 18, 032001, 2015
BeamImpedance2D (PYTHON): https://bitbucket.org/uniederm/beamimpedance2d.git
Open source package FEniCS (A. Logg, K. Mardal, G. Wells et al.)
Mesh from GMSH (C. Geuzaine, J. Remacle)
Dipolar current source term
Frequency domain
impedance solver:
More accurate at low
frequencies (kHz)

## Slide 19: Impedance contributions and database
Example: Coupled bunch instability
S. Arsenyev (IPAC 18)
Example: TMCI
: Spectrum of head-tail modes

## Slide 20: Octupoles and Landau damping
actions variables )
Tune shifts from octupoles:
2D beam distribution:
[1] H. G. Hereward, CERN 65-20 (1965)
[2] J. S. Berg, F. Ruggiero, CERN SL-AP-96-71 (1996)
[3] J. Gareyte, CERN-LHC-Project-Report-91 (1997)
2D dispersion relation [1-3]:
rms tune spread:
Very approximate stability condition
From LHC to FCC-hh:
72 x 168 octupoles
length of magnet
# of magnets
Scaling with energy:

## Slide 21: Finite chromaticity
Example case Q‘=15: the growth rates for the k=0 coupled bunch mode would be lower by a factor 0.6, but the k=1 mode would be present in addition (growth rate corresponding to 650 turns at injection).
(Sacherer 1974)
Form factor for different k

## Slide 22: Landau damping: Possible alternative schemes
Shiltsev et al PRL (2017)
Tune spread induced by a
counter-propagating electron beam:
Electron lenses
FCC-hh: Active feedback for k=0 modes, Landau damping for k>1.
Still, additional Landau damping concepts are helpful !
Grudiev PRAB 2014
Schenk et al, IPAC17
Radio-Frequency
Quadrupole (RFQ)
No local spread (in z) !
Dispersion relation and Landau damping ?
(longitudinal action)
Detailed particle tracking studies are ongoing (see also V. Kornilov).
Shiltsev et al
PRL 2017
LHC: 10 x larger stability area then with octupoles