## Slide 1: Beam dynamics studies for transverse feedback systems - modelling
J. Komppula (CERN)
Acknowledgements:
W. Hofle, G. Kotzian, K. Li, D. Valuch

## Slide 2: Outline
What are transverse feedback systems?
How to model
PyHEADTAIL simulation tools
Recent studies
  FCC-hh feedback performance
  LHC ADT induced coupled bunch instability
  SPS and LHC FIR filter tests
Discussion

## Slide 3: Why transverse feedback systems?
Beam quality
  Injection dipole errors cause emittance growth without damping
Beam stability
  Stabilization against transverse coherent instabilities
Multipurpose tool for machine development studies and operations
  Excitations, tune shift measurements, abort gap cleaning…
Future accelerators rely increasingly on the transverse feedback systems!

## Slide 4: What are transverse feedback systems?
Turns
Bunches
Digital signal processing
  FIR filters to calculated pickup to kicker phase advances (weighted sum over multiple turns)
  FIR filters for correcting analog signal distortions (weighted sum over consecutive bunches)
Analog signal processing
  Front end: Pickup signal processing for the ADCs
  Back end: Bandwidth limitations of power amplifiers and kickers

## Slide 5: History
Used in every synchrotron at CERN
  First systems in the 1970s
All proton injectors upgraded to digital signal processing during the LIU program
The SPS and LHC systems are closest to the FCC-hh requirements
  Used during all operation phases from injection to collision/extraction
  Single system for both injection oscillations and instabilities
Reliable and robust systems
Photo: D. Valuch

## Slide 6: Outline
What is a transverse feedback system?
How to model
PyHEADTAIL simulation tools
Recent studies
  FCC-hh feedback performance
  LHC ADT induced coupled bunch instability
  SPS and LHC FIR filter tests
Discussion

## Slide 7: Modelling - engineering point of view
Transverse feedback system is a controller
  Control theory is a powerful tool for linear systems
Pickups, transmission lines
Digital signal processing
Power amplifiers, kickers

## Slide 8: Modelling - beam dynamics point of view
Beam dynamics is complex… keep the models as simple as possible!
  Most of the simulation codes include an ideal transverse feedback model
    Direct correction
    Resistive vs. reactive feedback
  Coupled bunch instabilities from theory
    Modes where growth rate is lower than damping rate are stable
Recently more detailed models developed by several authors

## Slide 9: Do we need better feedback models?
Accelerators will be operated and designed closer the ultimate stability and performance limits
  Transverse feedback is one of the key systems
Modelling becomes more challenging
  Theories assume linear systems and/or weak kicks
    Strong kicks from the wake fields
    Strong kicks from the transverse feedback system
  Filling scheme
  Possible interplay between the beam (chroma, wakes, etc) and the feedback system
  Noise propagation
Reliable feedback performance estimates are needed
  Where are the limits of the used models?
  What happens when the models break?
Macroparticle simulations allow flexible studies for the performance limits and challenges

## Slide 10: Outline
What is a transverse feedback system?
How to model
PyHEADTAIL simulation tools
Recent studies
  FCC-hh feedback performance
  LHC ADT induced coupled bunch instability
  SPS and LHC FIR filter tests
Discussion

## Slide 11: PyHEADTAIL
A python library of macroparticle beam dynamic tools
  Developed 2014-> at CERN
    K. Li, A. Oeftiger, M. Schenk at al
  Based on HEADTAIL code
Modular design allows easily customized simulations
  Transverse and longitudinal tracking, wakes, space charge, e-cloud, etc.
  Recently optimized for multibunch beams and new feedback module developed
  Full FCC-hh beam simulations including wakes and feedback models possible
Transverse
tracking
Longitudinal
tracking
Wakes
Transverse
feedback
one_turn_map = [... +
wake_map +
transverse_segm_map_5 +
feedback_map +
transverse_segm_map_6 +
ecloud_dipole +
space_charge + ...]
for i in range(nturns):
for m in one_turn_map:
m.track(beam)
Transverse
tracking
Allows also models for multi pickup – multi kicker systems

## Slide 12: PyHEADTAIL feedback module
Allows detailed feedback models into beam dynamic simulations
  Link between the beam dynamics and the real feedback systems
Beam dynamics:
-good models for
beam dynamics
-ideal models for
feedback system
Engineering:
-good models for signal processing
-ideal models for beam
Detailed PyHT feedback model
-Every model step has equivalent signal processing step in the real system
- Beam dynamic effects from the feedback system design choices
- Deeper understanding of the performance limits and challenges
-Model can be simplified by commenting or replacing lines

## Slide 13: Example: PyHEADTAIL LHC ADT model
Power amplifier/kicker
phase correction
Close orbit offset and betatron phase
advance corrections
Gain and bandwidth
corrections
Power amplifier/kicker frequency response
Impulse response

## Slide 14: Outline
What is a transverse feedback system?
How to model
PyHEADTAIL simulation tools
Recent studies
  FCC-hh feedback performance
  LHC ADT induced coupled bunch instability
  SPS and LHC FIR filter tests
Discussion

## Slide 15: FCC-hh feedback performance
Challenges
  Fast coupled bunch instabilities
  Rigid beam (3.3 TeV injection energy)
Baseline feedback system based on the LHC ADT
Performance studied with PyHEADTAIL simulations
  Up to full beam (>10 000 bunches) simulations including filling scheme, chromaticity, wakes and LHC ADT feedback model
  Injection emittance growth
  Coupled bunch instability damping
Injected batch

## Slide 16: Outline
What is a transverse feedback system?
How to model
PyHEADTAIL simulation tools
Recent studies
  FCC-hh feedback performance
  LHC ADT induced coupled bunch instability
  SPS and LHC FIR filter tests
Discussion

## Slide 17: Analysis of the LHC ADT induced instability
FIR filter normalization issue during the machine development test
  Damper loop became unstable due to too high gain
  Induced fast coupled bunch instability
Simulations reproduce well the observed beam behavior
  Growth rate pattern along the batches
  ~100 turns growth time and ~0.05 coherent tune shifts
Simulation
Measurements

## Slide 18: Analysis of the LHC ADT induced instability
Beam was operated with the nominal ”standard bandwidth ” bunch-by-bunch filter
100 kHz filter with (as thought) equal gain was enabled, this moved the stability map
Further 30% increase of gain moved the operation point to the unstable region
Coherent beam-oscillations triggered the loop instability causing fast growth rate and strong real tune shift
Test simulation: What happens when the damper is turned on in the different operation points
Damper OFF
Damper ON
τ = 95 turns
ΔQ = 0.048
τ = 3000 turns
ΔQ = -5e-5
3)
4)
Operation point
2)

## Slide 19: Outline
What is a transverse feedback system?
How to model
PyHEADTAIL simulation tools
Recent studies
  FCC-hh feedback performance
  LHC ADT induced coupled bunch instability
  SPS and LHC FIR filter tests
Discussion

## Slide 20: LHC and SPS FIR filter tests
Turn by turn FIR filters of the transverse feedback system
  Determines operational gain and tune acceptance margins
  Currently used FIR filter scheme utilizes Notch+Hilbert filters (8-taps)
  3-tap filter allows larger margins and induces less tune shift
Filters tested in the LHC and SPS
  Good agreement between the LHC measurements and the PyHEADTAIL simulations

## Slide 21: Outline
What is a transverse feedback system?
How to model
PyHEADTAIL simulation tools
Recent studies
  FCC-hh feedback performance
  LHC ADT induced coupled bunch instability
  SPS and LHC FIR filter tests
Discussion

## Slide 22: Future possibilities and challenges
  Injection oscillations
    High energy accelerators (e.g. FCC-hh) require strong kicker systems
      Replacement technology for the tetrode amplifiers
      Smarter ways than the proportional damping?
  Instabilities
    Technology feasible for <10 turns coupled bunch instability damping times
    Possibilities of the intra bunch feedback systems
    How much margin can the FB systems give, where are the hard limits?
      Technology, beam dynamics or interplay between them?
  Noise
    Induces emittance growth and instabilities
    Best ways to mitigate
  Machine protection
    Accelerators will be operated with fast growing instabilities
    Is the feedback system a guardian angel or a concern?

## Slide 23: Summary
Transverse feedback systems are robust and reliable
  Allow performance increases in the existing and future accelerators
Technological and beam dynamics limits must be studied carefully
Feedback systems and beam dynamics can be simulated together
  Up to full beam simulations possible
  Good agreement with experimental data

## Slide 24: Thank you!