## Slide 1: RF feedback and dynamic tuning in CSNS/RCS
Li Xiao
Institute of High Energy Physics, CAS
2018.12.11 @ APEC workshop

## Slide 2: Outline
Introduction
CSNS/RCS RF system
Beam commissioning issue
RF feedback
Dynamic tuning system
Future plan

## Slide 3
Introduction

## Slide 4: Introduction
China Spallation Neutron Source (CSNS)
80MeV H- Linac
1.6GeV
25Hz
RCS
Target

## Slide 5: Introduction
Milestones
Feb. 2001 | Idea of CSNS discussed
Jun. 2005 | Proposal approved in principle by the central government
Sep. 2011 | Construction started, component fabrication started
Apr. 2017 | Linac commissioning 60MeV
May 2017 | RCS commissioning start
Aug. 2017 | first beam on target, first neutron beam
Nov. 2017 | Increase beam power to 10kW
Jan. 2018 | Linac/RCS commissioning 80MeV
Mar. 2018 | Passed National Acceptance Test, pre-open to users
Apr. 2018 | First Experiment Results Published in Nano Energy
Aug. 2018 | Passed National Acceptance
 | 6.5 years in total

## Slide 6: Introduction

## Slide 7
RF system

## Slide 8: RF system
Parameter | Value
Beam power (kW) | 100
Energy (GeV) | 0.08~1.6
Intensity (ppp) | 1.56E13
RCS circumference (m) | 228
Circulating dc current (A) | 1.5/ 3.5
Repetition rate (Hz) | 25
Harmonic number | 2
RF frequency (MHz) | 1.02~2.44
Peak RF voltage (kV) | 165 (h=2)
CSNS/RCS
8 fundamental harmonic cav.
h=2
3 second harmonic cav.
h=4

## Slide 9: RF system
RF pattern

## Slide 10: RF system

## Slide 11: RF system
Ferrite loaded cavity
RF power source
Bus bar
Cooling plates and ferrite rings
Cables for bias current
Two gaps of the cavity

## Slide 12: RF system
The RF power source
  500W wide-band solid-state preamplifier.
  800W feedback amplifier for direct RF feedback.
  500kW final stage amplifier (TH558).

## Slide 13: RF system
Bias supply
  3300A switch type plus 180A linear type.
  20kHz small signal bandwidth.
  Without beam, about 200~3000A corresponding to 1.022~2.444MHz.

## Slide 14: RF system
LLRF
CPU board (CPCI6200)
4 FPGA boards
Beam signal processing
8 FPGA boards
Control function for 8 RF systems
6U/21slots CPCI crate

## Slide 15: RF system
RCS tunnel

## Slide 16: RF system
Equipment hall

## Slide 17: RF system
Local station

## Slide 18
Beam commissioning issues

## Slide 19: Beam commissioning issues
60MeV injection
67 days to reach 10% of design beam power！
RCS/AC (13 days)
RCS/DC
(10 days)
Linac
(10 days)
2017.04.15~04.24
2017.05.26~06.07
2017.06.30~07.12
First beam on target, first neutron beam
RCS/AC (18 days)
2017.07.21~07.28
2017.08.11~08.28
2017.08.28
RCS/AC (8 days)
RCS/DC (8 days)
2017.07.13~07.20
2017.11.01~11.09
Increase beam power to 10 kW

## Slide 20: Beam commissioning issues
DC mode
  To control the beam loss during the beam commissioning, the single shot mode is adopted. In the first step, the beam commissioning was started in DC mode without acceleration.
  In May 31st, the first beam was injected into the RCS, and successfully accumulated in the RCS. The maximum accumulated particle number is about 1/3 of the design target.
  In June 5th/ 6 days, the first beam was extracted to RCS dump.

## Slide 21: Beam commissioning issues
AC mode
Beam life time was 4ms in the first shot.
On the same day, via shifting timing between RF and B field, the major part of beam was accelerated to 1.6GeV and extracted.
July 7th, the first beam was accelerated from 60MeV to 1.6 GeV.

## Slide 22: Beam commissioning issues
AC mode
Tuning RF amplitude, frequency, injection phase…
July 9th, the 99% beam transmission rate was achieved with the RF frequency pattern form 0.9018 to 2.444MHz.

## Slide 23: Beam commissioning issues
Interface
  Timing
    10MHz master clock/120MHz digital working clock
    Cycle start pre-trigger
  Trigger
    LEBT chopper
    Extraction kicker
    BPM
  Interlock
    Local equipment interlock
    MPS/FPS/PPS
  EPICS
    Standard EPICS interface
    Real time control data display and storage

## Slide 24: Beam commissioning issues
Beam signal processing
  Beam position
  Beam phase
  Beam amplitude / fundamental harmonic component

## Slide 25: Beam commissioning issues
Control architecture

## Slide 26: Beam commissioning issues
Control loops
  Cavity voltage control
  Cavity phase control
  Cavity tune control
  Grid tune control
  Direct RF control
  Beam loading compensation
  Synchrotron oscillation damping
  RF frequency correction
Cavity control module
Now in used
Beam control module

## Slide 27: Beam commissioning issues
Cavity voltage control

## Slide 28: Beam commissioning issues
Cavity phase control

## Slide 29: Beam commissioning issues
System tuning control

## Slide 30: Beam commissioning issues
Running statistics
2017.5 ~ 2018.7
Beam time 2400 hours
Fault time 14 hours
2018.9.30 ~ 2018.11.28
Beam time 1025 hours
Fault time 2.65 hours
99.4%
99.74%

## Slide 31
RF feedback

## Slide 32: RF feedback
To increase the dynamic performance of control system.
To compensate beam loading effect.
Cavity voltage signal from pickup

## Slide 33: RF feedback
Implement of RF feedback
  Tetrode grid tune control
  Feedback amplifier

## Slide 34: RF feedback
Feedback amplifier
  Specifically designed for direct RF feedback.
  Located in front of final stage amplifier adjacent to the cavity.
  High reliability

## Slide 35: RF feedback
Feedback amplifier
  Prototype adopted AGS scheme.
  2 stages, 4 push 4.

## Slide 36: RF feedback
Feedback amplifier
  Output power was not enough (AGS TH537/300kW)
  Low reliability in impedance mismatch condition
  High broken probability for long running

## Slide 37: RF feedback
Feedback amplifier
  2 stages, 2 push 6
  Output power was solved
  High broken probability still remained
  Impedance increase between stages leads to big phase shift

## Slide 38: RF feedback
Feedback amplifier
  2 stages, 1 push 2
  A matching network between stages is used to increase gain
  Stable working condition and very low broken probability

## Slide 39: RF feedback
The principle is very simple.
Major problem is to deal with the rapid sweeping working condition.
  The phase shift is guaranteed by the two stage of tuning loops.
  The feedback gain is set about 20dB.
Detuning may cause self-oscillation
  should be interlocked with bias supply.
Very effective for cavity voltage and cavity tuning.
30 kW operation without beam loading compensation loop.

## Slide 40
Dynamic tuning system

## Slide 41: Dynamic tuning system
In general, the load voltage should be in anti-phase to the grid voltage.
The resonant frequency is adjusted by bias supply.

## Slide 42: Dynamic tuning system
CSNS/RCS RF tuning system configuration

## Slide 43: Dynamic tuning system
Tetrode tuning system
  Similar principle with cavity tuning system
  Compensate the parasitic capacitance of tetrode grid
  Ensure the gain and stability of RF power source
  Ensure the phase shift for the RF feedback control

## Slide 44: Dynamic tuning system
Cavity tuning system
  Equivalent circuit of the bias supply load
  Resistance and capacitance of bypass is used to damp the oscillation

## Slide 45: Dynamic tuning system
Typical current curve in one cycle
  The maximum current is about 3000A
  Rapidly decreases to a low value (~150A) in about 1ms.

## Slide 46: Dynamic tuning system
Requirement of dynamic performance
  Nonlinear characteristic of ferrite
  Transient beam loading compensation
Limit of tuning system
  Control system ～ level of dozens of kHz
  Bias supply ～ several kHz
3 prototypes were developed
  Switch type
    4 IGBT modules
    High efficiency / low bandwidth / voltage ripple
  Linear type
    1392 transistors in parallel
    Low efficiency / high bandwidth / stability
  Combined type

## Slide 47: Dynamic tuning system
Combined type bias supply
  3300A switch type bias supply
  180A linear type modulator

## Slide 48: Dynamic tuning system
Small signal bandwidth (SSWB) comparison

## Slide 49: Dynamic tuning system
Detuning phase in 1 cycle

## Slide 50: Dynamic tuning system
Amplitude and Phase error in 1 cycle

## Slide 51: Dynamic tuning system
In practice, SSWB is the most important technical indicator.
Not like the power supply used in magnet system, the requirement of tracking precision could be relaxed due to the existence of tuning control system.
The voltage ripple doesn’t seem to affect the cavity voltage.

## Slide 52
Future plan

## Slide 53: Future plan
System running and beam commissioning
  20～25kW running
  50～100kW
  Beam control loops
    Beam loading compensation
    Synchrotron oscillation damping
Second harmonic system-500kW
  Manufacture of MA ring
  Cavity design
  High power test
LLRF
  New digital platform based on OpenVPX

## Slide 54
Thank you for your attention!