## Slide 1
RFQ Reliability Optimization for MYRRHA
H. Podlech
Institut für Angewandte Physik
Goethe Universität Frankfurt
Accelerator Performance and Concept Workshop
Frankfurt
December 12th 2018

## Slide 2
MYRRHA: Multi purpose hYbrid Research Reactor for High tech Applications
Subcritical reactor
with spallation target
Proton accelerator (cw)
4=mA, E=600 MeV (P=2.4 MW)
Keff 0.95-0.98
Spallation neutrons create fissions
Additional neutron by fission
2-5% external neutrons required
Reactor power 20-50 times higher compared to beam power

## Slide 3
Schematic Layout of the MYRRHA Project
Parallel redundancy
Serial redundancy
Construction has started
3 gap ESS Spoke 352 MHz
5 cell elliptical 704 MHz

## Slide 4
Courtesy J.-L. Biarrotte
Lay-Out of the MYRRHA-Linac

## Slide 5
Courtesy SCK • CEN

## Slide 6
17 MeV MYRRHA Injector
Design driven by emittance conservation (especially longitudinally)
Conservative beam dynamics design
Cw Solid state amplifiers as RF sources (up to 200 kW)
32 m
ECR
LEBT
RFQ
MEBT-1
CH-cavities
MEBT-2
CH-cavities

## Slide 7
Proton energy | 600 MeV
Beam current | 0.1 to 4.0 mA
Beam power | 2.4 MW
Beam duty cycle | 100%
Beam power stability | < ± 2% on a time scale of 100ms
Beam footprint on reactor window | Circular 85mm
Beam footprint stability | < ± 10% on a time scale of 1s
# of allowed beam trips on reactor longer than 3 sec | 10 maximum per 3-month operation period
# of allowed beam trips on reactor longer than 0.1 sec | 100 maximum per day
# of allowed beam trips on reactor shorter than 0.1 sec | unlimited
J-L. Biarrotte, MYRTE TEC meeting, Brussels, 29 October 2015.
Extreme reliability level
Parameter MYRRHA Linac

## Slide 8
Reliability Issues
Conservative design & redundancy
Beam trips longer than 3 sec must be very rare:
 To minimize thermal stress & fatigue on the target window, reactor structures & fuel assemblies
 To ensure an 80% availability – given the foreseen reactor start-up procedures

## Slide 9
Reliability Issues
Conservative design: All components will be operated well below their design parameters
Low energy part: Parallel redundancy
Main Linac: Serial redundancy
Injector is most critical part, especially the RFQ

## Slide 10
Parameter | Value | Unit
RF Structure | 4.Rod | ---
Frequency | 176.1 | MHz
Beam current | 4 | mA
Duty factor | 100 | %
Eout | 1.5 | MeV
Rp | 73 | kWm
RF Power | 107 | kW
Specific power | 26.5 | kW/m
Voltage | 44 | kV
Length | 4 | m
MYRRHA RFQ

## Slide 11
Cooling Issue of 4-Rod RFQs (MYRRHA, FRANZ, HLI, HBS)
Cw operation major concern
Conservative design
Research program to optimize cooling
New fabrication technologies have been developed
Pth=130 kW/m
U=100 kV
Ep=33 MV/m
Result prototype high power test

## Slide 12
Cooling System on Main Parts of the RFQ
copper electro forming
Tuning plates

## Slide 13
Dipole Compensation
A 4-Rod RFQ has an intrinsic dipole component
Upper electrode is on higher potential
Corresponds to a shift of beam axis
Can create non-linearities close to electrodes

## Slide 14: Dipole Compensation
Dipole compensation by shifting the stems

## Slide 15
MYRRHA RFQ

## Slide 16
MYRRHA RFQ

## Slide 17
MYRRHA RFQ

## Slide 18: 192 kW cw Solid State Amplifier
SSA for RFQ delivered on the 9th of May
September, 9th:
190 kW on dummy load!

## Slide 19: Event Prediction Systems
Implement diagnostics to predict failures in advance
Example: Signature of breaking power coupler

## Slide 20
Temperature Acquisition System
Continous data logging of 180 water outlets
Connected with an interlock system

## Slide 21: Summary
RFQ reliability
Optimized cooling
Relative low rod voltage (44 kV) and power losses
Solid state amplifier
Diagnostic and event prediction systems to prevent severe damage
(T-Sensors, Vacuum measurement)
For MYRRHA a very reliable Linac is required
Injector: Parallel redundancy
Main-Linac: Serial redundancy
Every component designed very conservatively
Operated well below design parameters

## Slide 22
MYRRHA RFQ@LLN

## Slide 23
Thank you