## Slide 1: Micro Vertex Detector
15.2.2018 Tobias Stockmanns
Tracking

## Slide 2: Mean dE/dx
Bethe-Bloch Formula
electronic stopping power ~ 
non-ionizing interactions
bremsstrahlung
(Fermi-)Plateau
Rise: Tmax ~ 22
const
~ ln 
~ 1/2
Minimum at   3.0 – 3.5  minimum ionizing particle (MIP)

## Slide 3: Energy loss distribution (straggling)
Energy loss is a statistical process
Distribution function is asymmetric for small absorbers
For thick absorbers the distribution becomes Gaussian
Collisions with small dE more probable
large dE rare  electrons with large energy (keV) are called -electrons (or –rays)
-electrons have enough energy for their own ionization trace
Parameterized via asymmetric Landau(-Vavilov) distribution

## Slide 4: pn - junction
p
n

## Slide 5: pn junction as particle detector
Space charge
region
Electric field
Potential
!!
thin, highly doped p+ (~1019 cm-3) layer
on lightly doped n- (~1012 cm-3) substrate
p+
n-
neutrality cond.
Maxwell

## Slide 6: pn junction under reverse bias (Vext)
1. Vbi  Vbi + Vext 2. no thermal equilibrium => EF(n)  EF(p)
p n
Hole Electron
current current
p n
Depletion
region
no bias
forward bias
reverse bias
Depl.  I 
Depl.  I 

## Slide 7: Single sided processing

## Slide 8: Double sided microstrip detector
top side
bottom side
bias strips
p-type insulation
read-out strips

## Slide 9: Capacitive charge division
incoming particle
incoming particle
intermed. strip
read Q
collected Q

## Slide 10:  - distribution for position-interpolation
 = QL/(QR+QL)
simple expectation:
x = η*d
not quite correct, use more complex function:

## Slide 11:  - distribution for position-interpolation
ideally  symmetric but: parasitic capacitances and r/o specifics
intermediate strips  intermediate “structure” in η

## Slide 12: MVD
Barrel:
  2 pixel layers
  2 strip layers
Forward:
  4 pixel layers
  2 mixed layers
Thickness:
  100 µm pixel
  280 µm strips

## Slide 13
MVD Pixel Part

## Slide 14: Pixel Modules
6.8 cm

## Slide 15: Pixel Sensors
Epitaxial Silicon Sensor
100 µm thickness
Pixel dimensions 100 µm x 100 µm

## Slide 16: Pixel Front End Electronics – ToPix
Floorplan ToPix 4
Reduced Size Prototype
leading edge
trailing edge
threshold
ToT
ToPix – Torino Pixel ASIC
Charge measurement: time over threshold (ToT)
CMOS 130 nm technology
Recent prototype (reduced size): ToPix 4 (640 pixels)
Input charge range | 50 fC
Input channels | 12,760 pixels
Max event rate | 6.1 x 106 Hits/s/cm2
Power consumption | < 800 mW/cm2
Charge resolution | 12 bit
Radiation dose | < 100 kGy (goal)
preamplifier-output

## Slide 17: ToPix 4 Measurements: Lab
ToT-Linearity
S-Curve Sigma
Power consumption
Radiation Hardness

## Slide 18: ToPix 4 Measurements: Testbeam
Test beam measurement with ToPix beam telescope with protons @ COSY
pbeam = 2.95 GeV/c
Successful measurements with ToPix 4 prototype
Readout
Board
ToPix 4
Beam
Hitmap
Leading vs. Trailing Edge
Hit distribution over time

## Slide 19
MVD Strip Part

## Slide 20: Strip Part – Design Concept

## Slide 21: Strip Part – Module Design
Sensors
Cooling Pipe
Carbon foam: POCOFoam® or HTC
for thermal management
2mm
Front-end chip
31.3 cm
Cable channel
Hybrid flexible PCB
  Sensor
  Chip support: carbon foam
  Cooling pipe
  Flex PCB
  Sensor Frame: CFRP
  Readout chips

## Slide 22: Strip Sensors
6 cm
3.5 cm
2.2 cm
3.7 cm
5.7 cm
Barrel Sensor
Thickness 285 µm
896 x 512 strips
65 µm pitch
Readout every 2nd strip
90° stereo angle
Wedge Sensor
Thickness 285 µm
768 strips per side
45 µm pitch
Readout every 2nd strip
15° stereo angle
Notes: final wedge sensor pith 45 mu m jeder zweite wird gelesen
bei 67,5 wird jeder streifen gelesen
barrel sensor final 65 mu m aber jeder zweite wird gelesen

## Slide 23: Measurements Disk Prototype
Lab measurements
Test beam, pbeam = 0.8 GeV/c Protons
APV25 Front End
Prototype successfully tested
Notes: ! APV 25 messungen!

## Slide 24: Barrel Prototype
Flex-PA and squared sensor assembled on a test board and successfully tested at SPS, CERN
(September 2012)
3.5 x 3.5 cm2 PANDA fullsize sensor S2 (@130 µm r/o)
Hitmap

## Slide 25: Geometry
Full geometry description of all components
Slightly outdated
Contains all materials in a (semi)realistic manner
CAD design of MVD not finished

## Slide 26: Angular Coverage
Notes: A minimum amount of hits is required to obtain a good tracking of particles.
the detector geometry was optimizes to aim a minimum of 4 hits per track.
For this simulation particles with fixed momentum where isotropically emitted in the detector.
The goal of four hits per track is acheived in a large range of the solid angle.

## Slide 27: Radiation Length
< 10 % for most Θ angles
Main contributions from cables and support

## Slide 28: Digitization
Parameterizes charge cloud effect
Splits charge to adjacent pixels / strips according to path of particle and diffusion
Data format matches with electronics
Pixel digitization matches with ASIC (ToPix)
Strip digitization works like pixel digitization. Adoption to strip ASIC (PASTA) still has to be done
  Strip ASIC has a much higher time resolution but not clear if it can be used in combination with silicon sensor
  Pile-up behavior different

## Slide 29: Reconstruction
Pixel and Strip Clusterization: Search for nearest neighbors
Strip matching of top and bottom cluster taking charge information into account
Space point reconstruction based on different algorithms:
  Geometrical mean
  Eta distribution
Noise reduction by cutting on charge measurement
Comparison with test beam data done

## Slide 30: Time-Based Simulation
MVD fully supports time based simulation
Pile-up is handled in a parametric way in the pixel part matching with the ToPix ASIC
  first hit is measured
  ToT is enlarged (wrong charge measurement)
  second hit is lost
TOAST features are not implemented (Strips behave as pixel)
Reconstruction steps
  Hit sorting by time stamps
  Time-gap event building
  Event based reconstruction steps

## Slide 31: Test Beam Analysis
Different test beam analysis software exist
  Stand alone pixel and strip software
  PandaRoot based reconstruction for pixel and strip
  FairMQ based online reconstruction of pixel
Cross-check between simulation and measured data still missing

## Slide 32: General points
Open issues in MVD:
  Update of geometry (medium)
  Implementation of TOAST features (high)
  Comparison of test beam data with simulated data in PandaRoot
  Refactoring and clean up of code
  Manpower needed: 2 FTE years (depending on skill)
  Manpower available: 0.2 FTE per year