Suggestion for design and movement of the
Forward platform

---
Task:
- It has to carry the forward-detectors
- the Forward-platform has to move from the maintenance position to the experimental area
- the total weight of the platform with detectors and components will be approximately 110 tons
- the precision regarding to the final position should be in the range of 2-4mm

---
Design of the platform:
The following pictures show a revised Design of the platform

---
Design of the platform:
The platform is divided into a welded main platform and several screwed segments
main platform

---
Design of the platform:
The detectors in this presentation are only shown as placeholders, the exact dimensions of the platform have to be adjusted when the designs of the detectors are final
Shashlic
TOF
RHICH
Myon Range System
FT5 u. FT6
LUMI
Racks

---
1.	Concept
Suggested solution for moving:
Moving the platform by a hydraulic skidding system, for example from the Company Holmatro

---
In the first step, four hydraulic cylinder are positioned under the platform and lift it up by
some cm

---
In the first step, four hydraulic cylinder are positioned under the platform and lift it up by
some cm

---
After that the stacks of the skidding system will be placed under the platform and the cylinders
lower the platform on the teflon-plates of the skidding system

---
Then, two hydraulic cylinder will be attached to the platform

---
The movement itself takes place via teflon plates on the stacks and sliding plates made
of polished stainless steel
main platform
bolt
hydraulic cylinder
teflon plates
slide plate
(sliding surface made of polished stainless steel)

---
For the movement, the cylinders push the platform 500mm forward, while they are locked to the
stacks

---
For the movement, the cylinders push the platform 500mm forward, while they are locked to the
stacks

---
In the next step the cylinders act in the other direction and draw themself to the platform
while the wings on the cylinder swing up and lock the cylinder to the stacks in 500mm again

---
In the next step the cylinders act in the other direction and draw themself to the platform
while the wings on the cylinder swing up and lock the cylinder to the stacks in 500mm again

---
So it goes on, step by step until the final position is almost reached

---
Then a reference plate is attached to the platform, which will be positioned in relation
to a mark on the floor

---
Then a reference plate is attached to the platform, which will be positioned in relation
to a mark on the floor

---
When the final position perpendicular to the beam axis is reached, the four lifting cylinders
are positioned under the platform again and release the platform from the stacks

---
When the final position perpendicular to the beam axis is reached, the four lifting cylinders
are positioned under the platform again and release the platform from the stacks

---
When the final position perpendicular to the beam axis is reached, the four lifting cylinders
are positioned under the platform again and release the platform from the stacks

---
Then, four special stacks will be put under the platform, an the cylinders lowers the
Platform onto the teflon plates

---
Then, four special stacks will be put under the platform, an the cylinders lowers the
Platform onto the teflon plates

---
Then, four special stacks will be put under the platform, an the cylinders lowers the
Platform onto the teflon plates

---
Then two fasteners and two cylinders are attached to the platform

---
Then two fasteners and two cylinders are attached to the platform

---
After that, the two cylinders push the platform to the final position in beam direction

---
After that, the two cylinders push the platform to the final position in beam direction

---
After that, the two cylinders push the platform to the final position in beam direction

---
In the last step the four lifting cylinders raise the platform and lower it on
the floor after the stacks and the polished sliding plates are removed

---
In the last step the four lifting cylinders raise the platform and lower it on
the floor after the stacks and the polished sliding plates are removed

---
In the last step the four lifting cylinders raise the platform and lower it on
the floor after the stacks and the polished sliding plates are removed

---
In the last step the four lifting cylinders raise the platform and lower it on
the floor after the stacks and the polished sliding plates are removed

---
In the last step the four lifting cylinders raise the platform and lower it on
the floor after the stacks and the polished sliding plates are removed

---
In the last step the four lifting cylinders raise the platform and lower it on
the floor after the stacks and the polished sliding plates are removed

---
The following links show the principal process of skidding systems in various
videos:
https://www.youtube.com/watch?v=FEnxTs0_jnk
https://www.youtube.com/watch?v=RQQEZ1K0KIM
https://www.youtube.com/watch?v=uvmbPQ-HImc

---
2. Conclusion
Conclusions:
Advantages of the skidding system:
- the complete system is removable, so there is more space on the floor
  for maintenance
- there are several companies that sell complete systems
- such systems are practically proven
- there is no need for any anchoring on the hall floor
-there exists a system designed for 400 tons, so we could use the system for
 moving and positioning of the target spectrometer as well