## Slide 1: EMC Feature extraction for time-based simulation
Viktor Rodin
Myroslav Kavatsyuk, Peter Schakel

## Slide 2: EMC readout
Hardware trigger
Main features
Continuous data flow
No physical triggers
Intelligent FEE
?????
????

## Slide 3: EMC readout
Feature extraction stages of digitized signals.

## Slide 4: Pile-up happens…
Integrated single-crystal hit rate as a function of X and Y for the Forward Endcap EMC obtained from simulations with full interaction rate.
EMC TDR

## Slide 5: Pile-up recovery

## Slide 6: MWD and MA
Moving Window Deconvolution
x(i) – value of sample,
m – length of window in samples,
– inverted index of exponential tail of the pulse.
Moving Averaging
L – number of samples for averaging.
(differentiation with exponential tail recovery)
(integration, low pass efficient filter)

## Slide 7: Feature Extraction on FPGA
SADC
MWD I
MWD II
FE
FE
Base-line
MA
E
CFT
Time
Tr
long
short
I/A

## Slide 8: Waveform after filter
Raw waveform
MWD waveform
Samples
This waveform was measured with latest ADC version
(weaker shaping)

## Slide 9: Energy resolution
C.Tsolanta (Bachelor thesis)
Energy = Pulse Integral over threshold
The longer filter length  better resolution

## Slide 10: Disadvantages of dynamic integration
C.Tsolanta (Bachelor thesis)
Using of MWD filter improves but does not fix the non-linear dependency
of integral and amplitude(energy). Before it was working with old filter.

## Slide 11: Possible solutions
Fixed window for the integration including
area below thresholds
( hard to implement)
Definition of energy with help of amplitude
( sensitive to noise effects )
Integrate the flat area after MWD filter
Using MA filter
(Energy is defined by amplitude
but noise effects are small)

## Slide 12: PandaRoot implementation
Old vs New pulse shape:
Old  shape of the pulse with ADC prototype
New  shape of the pulse produced by the final ADC version

## Slide 13: Implementation of pile-up identification&recovery
Aim of investigation
Pile-up treatment
Implementation of new waveform
(implemented but not optimized)

## Slide 14: Timebased Simulation
Input parameters
G4generator – Box Generator Particle – photon
Number – 10000 Energy – 0.5 GeV Hit rate – 100kHz
Shooting in one point
Clustering algorithm – online clustering

## Slide 15: Simulation results
New waveform w/o pile-up
recovery
New waveform + pile-up
recovery
Raw wf
MWD+MA(16,25, 8) MWD II(10,24,5)
Photon energy

## Slide 16: Summary
Pile-up identification and pile-up recovery algorithms have been added and tested in the Pandaroot timebased simulations
A new shape of pulse is implemented. It corresponds the real shape
The scrutiny of the pile-up issues is ongoing and possible adjustments in the cluster reconstruction and noise adding will be implemented

## Slide 17
Thank you for attention!

## Slide 18: EM Calorimeter
Subunit of 16 crystals
Internal structure of subunit
Our prototype: 9 crystals + dummies
Each crystal has 2 LAAPDs

## Slide 19: FE with old filter
G.Tambave(PhD thesis)