## Slide 1: Simulation of cooling system for PANDA electromagnetic calorimeter using CFD
Ing. Michal VOLF
volfm@kke.zcu.cz
+420 608 282 562
PANDA Collaboration Meeting
Darmstadt, November 2018
FACULTY OF MECHANICAL
ENGINEERING
UNIVERSITY
OF WEST BOHEMIA

## Slide 2
Department of Power System Engineering - CFD
Ammonia-water solution-based heat exchangers
Cogeneration units
1D & 3D analysis (Nuclear Power Plant)
Complex geometries (valves)
Complex geometries (reduction cages)
Electrostatic precipitators of flue dust
Turbomachinery

## Slide 3: Introduction
PbWO4 light yield ↑↓ temperature
within a single crystal ≈ 0.1 K
among all crystals ≈ 1 K
lower temperature is better
temperature stability
How can this be achieved?
! limited space for cooling circuits
! crystals cannot be cooled down directly
! homogenous temperature field
! different pressure losses in each cooling circuit
? number of cooling tubes
? shape of cooling tubes
? mass flow rate of cooling medium
? inlet temperature of cooling medium

## Slide 4: First approach
partial geometry is used for simulation in order to:
  decrease pre-processing time
  decrease computational time
MODULE 10
MODULE 11
FOAM
COOLING TUBES
SUPERMODULE7
numerical error
influence of fluid flow turning
influence of fluid flow turning
„representative“ crystals
computational domain should be extended to increase the number of „representative“ crystals

## Slide 5: Computational domain
ccomputational domain has been divided to two parts: base domain (crystals etc.) and cooling system
  simplifies the procedure of testing multiple cooling systems
  ensures the base domain is not influenced by changes in computational mesh
BASE DOMAIN
COOLING SYSTEMS
SUPERMODULE 6 & 7 (modules 8 – 11)
  domain consists of 150 crystals
  100 of them are considered as representative for the rest of SLICE
rectangular tubes
inner dim. 8 x 8 mm
two separate circuits
round tubes
inner diam. 8 mm
two separate circuits
connection

## Slide 6: Numerical simulation setup
inlet 2
inlet 1
outlet
outlet
1D simulation
3D simulation
heat source from the chip (≈150 mW)
heat conduction in cables (≈200 mW)
Heat sources: ambient temperature 25 °C
read-out electronics
heat conduction in cables
heat transfer from ambient air
fixed temperature of -25 °C
symmetry specified on side walls
adiabatic wall
back wall is considered to be adiabatic
applied as ambient temperature + heat transfer coefficient (≈50 W/m2)
Cooling fluid: -28 °C, 0.4 kg/s at inlet
pressure of 1 atm at outlet
mixture of water/methanol (40/60)

## Slide 7: Material properties
Component | Material | Specific heat capacity [J kg-1 K-1] | Thermal conductivity [W m-1 K-1] | Density [kg m-3] | Other
Crystals | PbWO4 | 262 | 3.22 | 8280 | Ref. temp. 30 °C
Crystal casings | Carbon fibres | 1100 | 78.8 | NaN | Ref. temp. 120 °C
Crystal connections | Duralum | 920 | 147 | 2900 | Ref. temp. 25 °C
APFEL asics | Aluminium | 903 | 237 | 2702 | Ref. temp. 25 °C
Electronic board holders | Duralum | 920 | 147 | 2900 | Ref. temp. 25 °C
Intermediate plates | Duralum | 920 | 147 | 2900 | Ref. temp. 25 °C
Supermodule plate | Duralum | 920 | 147 | 2900 | Ref. temp. 25 °C
Foam | HOCOTOL | 880 | 154 | 2830 | Ref. temp. 25 °C
Cooling tubes | Copper | 385 | 401 | 8933 | Ref. temp. 25 °C
Cooling medium | Water/methanol (40/60) | 3151 | 0.341 | 930 | Ref. temp. 25 °C Ref. pressure 1 atm
Ambient medium | Ideal gas | - | - | - | -
Material properties are NOT defined for operating temperature
General values are taken since we do not have specific material sheets available
needs to be reviewed

## Slide 8: Material properties
crystal connections
the connection was modeled since there was no direct connection in the default geometry

## Slide 9: Preliminary results
Temperature field – surface of the domain (without foam)
Temperature field – surface of the crystals

## Slide 10: Preliminary results – cooling system failures
Temperature field – surface of the whole domain
Temperature field – surface of the crystals
it is assumed that mass flow rate in the second circuits is only 5% of the mass flow rate in the first one

## Slide 11: Conclusion
Goal: cool down crystals to approx. - 25 °C
ensure stability of temperature & homogenous temperature field
Difficulties: complex geometry with lots of connections between components that are simulated as ideal ones
lack of free space for proper cooling system
1D simplification of supermodules
high accuracy of simulations
sensitivity to boundary conditions
difficulties with material properties at working temperature
Follow-up research: result comparison between various cooling system designs
propose cooling design modifications
simulate cooling system failures
VALIDATION OF PARTIAL RESULTS

## Slide 12: Thank you
Ing. Michal VOLF
+420 608 282 562
volfm@kke.zcu.cz
FACULTY OF MECHANICAL
ENGINEERING
UNIVERSITY
OF WEST BOHEMIA