## Slide 1: Preliminary results of the structural analysis of the Bucharest TRD Module Type 1 (Buch-TRD)
CBM-TRD Retreat, 27-29 March, 2019
Laura Radulescu for CBM-TRD Bucharest team

## Slide 2
Motivation and Outlook
Simplified
Frame behavior under the wires tensions
Wires tensions variation
Entrance window deformation under the wires tensions
Based on ALICE-TRD experience (see Mariana’s presentation)
chamber frames suffer a deformation induced by wires tension
pad plane (and entrance window) could suffer deformation during operation/construction
Studying static chamber deformation based on ANSYS

## Slide 3
ONLY Frame behavior under the wires tensions
No entrance window (toy model) !
The ANSYS Simulation Model – hypothesis
1. Modelling tension distribution on wires rods

## Slide 5
The ANSYS Simulation Model – hypothesis
2. Modelling the supports: type and position

## Slide 7
Dx [mm] | Window type_15mm
4.8 x 2 | 15_full fill
93.4 x 2 | 15_without Cfibber in
11.1 x 2 | 15_without Cfibber out
Dz [mm] | Window type_15mm
22 | 15_full fill
346 | 15_without Cfibber in
59 | 15_without Cfibber out
The ANSYS Simulation Model – results for Chamber Deformations
1. Entrance Window Thickness = 15 mm

## Slide 8
Dx [mm] | Window type_12mm
4.6 x 2 | 12_full fill
88.6 x 2 | 12_without Cfibber in
12.6 x 2 | 12_without Cfibber out
Dz [mm] | Window type_12mm
30.3 | 12_full fill
347 | 12_without Cfibber in
102 | 12_without Cfibber out
The ANSYS Simulation Model – results for Chamber Deformations
2. Entrance Window Thickness = 12 mm

## Slide 9
Dx [mm] | Window type_9mm
5.8 x 2 | 12_full fill
90 x 2 | 12_without Cfibber in
16.6x 2 | 12_without Cfibber out
Dz [mm] | Window type_9mm
44 | 12_full fill
449 | 12_without Cfibber in
159.5 | 12_without Cfibber out
The ANSYS Simulation Model – results for Chamber Deformations
3. Entrance Window Thickness = 9 mm

## Slide 10
The ANSYS Simulation Model – Wire tension variations
Realistic simulation of the cathode wire geometry
F(x) agrees with elastic deformations
Elastic constant found to be 1.9e-3 N/mm

## Slide 11
Very preliminary results for the variation of the wires tensions taking into account the rods and entrance window deformations
The ANSYS Simulation Model – results Cathode Wire Tension
4. Systematics with Entrance Window Structure

## Slide 12
Nominal Cathode tension (CT) ~ 100 cN
Wire elasticity limits 80 cN< CT <120 cN
Observed DTmax = 20 cN
Model sustain by measured deformations
Comparison between ALICE-TRD measured deformation (Tension variation) agrees qualitatively with ANSYS simulations

## Slide 13
Entrance window deformations may also affect the pad plane planarity and gain uniformity! To be followed!
The ANSYS Simulation Model – results Entrance Window Concavity
5. Systematics with Entrance Window Structure

## Slide 14
Current gas flow geometry relies on 2 inlet and 2 outlets
Possible gas flow patterns in TRD12
Ways to obtain an uniform flow
Optimal solution - in progress
The ANSYS Simulation Model – Gas Flow Studies
Studying Inlet/Outlet geometry

## Slide 15
CBM-TRD HPD Bucharest team
Alexandru Bercuci, Valerica Aprodu, Daniel Bartos, Gheorghe Caragheorgeopol, Vasile Catanescu, Viorel Duta, Mariana Petris, Mihai Petrovici, Lucia Prodan, Andrei Radu, Claudiu Schiaua, Victor Simion
Thank you!