## Slide 1: The Collector Ring @ FAIR
Oleksii Gorda
21 January 2019
GSI/FAIR Workshop on Stochastic Cooling

## Slide 2: Tasks of the Collector Ring (CR)
HESR
CR
SIS-100
Rare Isotope
Beam (RIB)
production target
Antiproton
production
target
Existing facilities
Planned facilities
 | Operation mode | Kin. Energy | Nmax | Cycle Time
1 | cooling | 3 GeV | 108 | 10 s *
2 | RIB cooling | 740 MeV/u | 108 | 1.5 s
3 | RIB isochronous mass-measurements | 400-790 MeV/u | 1-108 | few turns
4 | Delivery of primary stable beams from SIS-18 to HESR ** | On demand, (with pre-cooling if necessary) |  | 
 | Operation mode | Kin. Energy | Nmax | Cycle Time
1 |  | 3 GeV | 108 | 10 s *
2 | RIB cooling | 740 MeV/u | 108 | 1.5 s
3 | RIB isochronous mass-measurements | 400-790 MeV/u | 1-108 | few turns
4 | Delivery of primary stable beams from SIS-18 to HESR ** | On demand, (with pre-cooling if necessary) |  | 
extraction to HESR *
extraction to HESR *
in-ring
* within the Modularized Start Version (MSV) of the FAIR project
** option presently under consideration
extraction to HESR **
SIS-18

## Slide 3: CR general overview
Circumference 221.45 m
Max. magnetic rigidity 13 Tm
Dipole
Quadrupole
Sextupole
Antiprotons
εx,y = 240 mm mrad
δp/p = ± 3%
from -separator
from Super-FRS
RIBs
εx,y = 200 mm mrad
δp/p = ± 1.5%
to HESR
Designed specially for stochastic cooling of antiproton or rare isotope beams
Flexibility in ion-optical settings for the different operation modes essential
Large transverse/momentum acceptance to accommodate hot beams coming directly from separators
Bunch rotation by the RF-system to reduce the momentum spread prior to stochastic cooling
Matching of the beam parameters between CR and HESR

## Slide 4: CR cooling cycle
Injection
single-turn
Bunch rotation & de-bunching
Max. RF voltage of 200 kV required for bunch rotation.
Stochastic cooling
Re-bunching
Extraction
Re-excite RF voltage for re-bunching
Simultaneous 3D cooling by Filter, TOF or Palmer method
to HESR
injected bunch length σb ~ 50 ns.
Schematic RF pattern for antiprotons **
* CR Technical Design Report, v.7.6.1 (2016)
*
** not true to scale

## Slide 5: RF system
Two inductively loaded coaxial quarter wavelength resonators working on a common ceramic gap
Ring core of cobalt-based magnetic alloy
Max. voltage 40 kV/unit
Number of units 5
Frequency range 1.1 – 1.5 MHz
Inner pipe diameter 150 mm
First of Series CR debuncher during commissioning at GSI.
First of series accepted in 2017
FAT/SAT of series cavities ongoing

## Slide 6: Stochastic cooling system
3D cooling by Filter, Palmer or TOF method
System bandwidth 1-2 GHz
Slot-line pick-ups with movable (plunging) electrode modules at cryogenic temperature (20-30 K) to improve signal-to-noise ratio for antiprotons
Palmer pick-up for pre-cooling of hot radioactive ion beams
Palmer Pick-Up
Slot-line double Pick-Up
Kickers

## Slide 7: Magnets
Num. of magnets 24
Max. field 1.6 T
Bending radius 8.125 m
Useful aperture 380140 mm2
Field uniformity ±1·10-4
Weight 59.8 t
Embedded horizontal correction coils
Dipole
Num. of magnets 40
Num. of types 4
Number of families 15
Max. ramping rate 1 T/m/s
Useful aperture 380140 mm2
Field homogeneity ±5·10-4
Num. of magnets 24
Number of families 6
Yoke length 50 cm
Pole inscribed radius 201 mm
Max. field 0.067 T
Correction angle ±1.5 mrad
Length with coils 39 cm
CR magnet polarity change within 60 s
Quadrupole
Sextupole
Orbit corrector
dipole
quadrupole
sextupole

## Slide 8: Injection/Extraction
Injected beam
Single turn injection by 3 pulsed septum magnets and 6 fast kicker magnets
Same kickers and 1 extraction septum magnet for fast extraction
Max. field 0.6 T
Magnet length 0.952 m
Pulse duration 3 ms
Ceramic vacuum chamber
Num. of kicker units 6
Max. field 0.054 T
Kicker unit length 0.47 m
Rise/fall time 318 ns
Flat top length 0.05 - 1.5 µs
Inner diameter 150 mm

## Slide 9: Vacuum system
Beam lifetime requested in CR
Measured outgassing rates included
Ceramic tubes for microwave damping of the stochastic cooling system:
Ferrites in injection/extraction kickers:
Total ferrite surface in the stochastic cooling pick-up and kicker tanks:
Required average dynamic pressure (N2 equivalent)
Component | Quantity | Remark
Roughing pumps | 2 | Mobile in the Ring
Ion/getter pumps | 75 | Hydrogen pumping speed of 1000 l/s; DN 100 CF
Sector / Gate valves | 6 | DN 200 CF
Angle valves | 8 | DN 160 CF for roughing stations
Cold cathode gauges | 12 | Two gauges in each vacuum sector
Pirani gauges | 12 | Two gauges in each vacuum sector
Residual gas analyzers | 2 | Installed either temporarily or permanently, connected via a DN 40 CF angle valve.
1.4

## Slide 10: Beam diagnostics
Schottky
pick-up
BTF
BPM
Cryogenic
current
comparator
Residual gas monitor
Scintillation
screen

## Slide 11: Ion-optical design
Driven by requirements for the most efficient stochastic cooling
Compromise between desired mixing (KI→PU) and undesired mixing (PU→KI)
Flexibility in setting the slip factor and PU-KI to an optimal value for different ion-optical settings (, RIB)
with
transition energy defined as
Optimum betatron phase advance between PU and KI for the transverse cooling
Accommodation of SC hor/vert. pick-ups, kickers and RF-cavities in regions of zero dispersion D=0
Palmer pick-up → in a dispersive region
Efficient chromatic corrections for all ion-optical settings
Palmer PU
PUx
PUy
KIy
KIx
Beam
RF
cavities
Mirror-symmetry plane
Circumference 221.45 m
Max. magnetic rigidity 13 Tm
Super-periodicity 1
24 dipoles
40 quadrupoles
24 sextupoles

## Slide 12: Antiproton optics (I)
Optimal local slip factor which eliminates the undesired mixing PU→KI
Ring has to be small enough to reach sufficient momentum acceptance for Notch filter cooling.
Ring has to be sufficient for a good desired mixing KI→PU
- mode 1 | 
Kinetic energy | 3 GeV
Revolution frequency | 1.315 MHz
Velocity | 0.971 c
Lorentz factor γ | 4.2
Transition energy | 4.84
Ring slip factor | 0.014
Local slip factor | 0
Betatron tunes | 4.39 / 3.42
Momentum acceptance | ± 3%
Transverse acceptance | 240 mm mrad
Kinetic energy | 3 GeV
Revolution frequency | 1.315 MHz
Velocity | 0.971 c
Lorentz factor γ | 4.2
 | 4.84
 | 0.014
 | 0
 | 4.39 / 3.42
Momentum acceptance | ± 3%
Transverse acceptance | 240 mm mrad
PU/KI
Palmer PU
Average dispersion
in arcs
Beam size at slot-line PU:

## Slide 13: Antiproton optics (II)
Possible future upgrade of the stochastic cooling system to 2-4 GHz (additional PU and KI) aiming at cooling time of 5 s (beyond MSV)
Optimized setting which guarantees optimum momentum acceptance for both 1-2 GHz and 2-4 GHz bands operating simultaneously.
Local slip factor kept small but non-zero
- mode 2 | 
Kinetic energy | 3 GeV
Revolution frequency | 1.315 MHz
Velocity | 0.971 c
Lorentz factor γ | 4.2
Transition energy | 3.85
Ring slip factor | -0.011
Local slip factor | -0.033
Betatron tunes | 4.28 / 3.44
Momentum acceptance | ± 3%
Transverse acceptance | 240 mm mrad
Kinetic energy | 3 GeV
Revolution frequency | 1.315 MHz
Velocity | 0.971 c
Lorentz factor γ | 4.2
 | 3.85
 | -0.011
 | -0.033
 | 4.28 / 3.44
Momentum acceptance | ± 3%
Transverse acceptance | 240 mm mrad
Average dispersion
in arcs

## Slide 14: Eta-variation during cooling
Coherent term of the filter cooling system is proportional to the ring slip factor
Momentum cooling efficiency can be improved by a linear increase during the cooling process while momentum spread is shrinking.
Control of betatron tunes, phase advance between pick-ups and kickers during the quadrupole ramping
Keeping zero-dispersion in the straight sections
Variation of transition energy 3.85 ≥≥ 3.35 or 0.011 ≥ ≥ 0.033
Max. required gradient 0.24 T/m/s for eta-variation during 5 s

## Slide 15: RIB optics
Average dispersion
in arcs
Momentum acceptance for RIB filter cooling is limited by undesired mixing PU→KI
Transition energy must be chosen as small as possible by increasing dispersion in the arcs
Hot RIBs have to be cooled first by Palmer method which has a larger momentum acceptance
RIB mode | 
Kinetic energy | 740 MeV/u
Revolution frequency | 1.124 MHz
Velocity | 0.830 c
Lorentz factor γ | 1.79
Transition energy | 2.73
Ring slip factor | 0.178
Local slip factor | 0.134
Betatron tunes | 3.40 / 3.44
Momentum acceptance | ± 1.5%
Transverse acceptance | 200 mm mrad
RIB mode | 
Kinetic energy | 740 MeV/u
Revolution frequency | 1.124 MHz
Velocity | 0.830 c
Lorentz factor γ | 1.79
 | 2.73
 | 0.178
 | 0.134
 | 3.40 / 3.44
Momentum acceptance | ± 1.5%
Transverse acceptance | 200 mm mrad
Beam size at Palmer PU:

## Slide 16: Ion-optical optimizations
Orbit corrections
Correction of closed orbit distortions due to dipole field errors and magnet alignment tolerances
Dipole field error δB/B = 5·10-5 (rms)
Magnet displacement error Δx,Δy,Δz = 0.3 mm
Magnet rotational error Δφ,Δθ,Δψ = 0.3 mrad
29 horizontal and 19 vertical correctors available
Peak-to-peak (rms)
before correction: ~10 mm
Peak-to-peak (rms)
after correction: ~1.5 mm
Compensation of betatron tune Qx,y variation with momentum
Reduce tune spread to avoid crossing dangerous resonances
6 families of sextupoles are used
Chromaticity corrections
Dynamic aperture control
Impact of nonlinear field errors on beam stability, can be critical for beams with large momentum spread
Compensation schemes for improving dynamic aperture and reducing possible beam losses
Aim: preserve beam intensity &
prepare optimal pre-conditions for the most efficient stochastic cooling

## Slide 17
Thank you for
attention!