## Slide 1
RIB Production at Super-FRS
Helmut Weick, GSI Helmholtzzentrum
Stochastic Cooling Workshop, 21st Jan. 2019
Motivation
Production Reactions and Kinematics
Rare Ion Separation
Super-FRS System
Emittance Modification
Beam Diagnostics

## Slide 2: Rare Isotopes in Rings
Chart of nuclides has:
~ 2200 with t > 1 ms ~ 1100 with t > 1 min
some t = 10n years
 Lifetime long enough for
cooling and accumulation
Look at rare decays and transitions - ILIMA
When lifetime is years we need many ions in ring (e.g. 205Tl case)
or b-decay followed by neutron emission (trace mother and daughter ions in ring)
Reactions with gas jet target - EXL
Luminosities of 1024 – 1028 /(cm2. s) require 105 – 109 cooled ions in ring
Collider with electrons - ELISe

## Slide 3
How to produce Rare Isotopes ?
Fragmentation
Removal of nucleons in quasi-free nucleon-nucleon collisions
neutrons (N)
protons (Z)

## Slide 4
Distribution of Fragments
Uranium on Pb target
N
Z
at 1 GeV/u

## Slide 5: Production Cross sections
Projectile fragmentation
Projectile fission
Target
Projectile 129Xe
Main Fragment
238U
Fusion (only at lower velocity)
Tin isotopes by different methods

## Slide 6: Fission Kinematics
|q| < 10 mrad
in Uranium fission ~200 MeV are released
in Lab:
132Sn from
238U beam
at 1 GeV/u
in
CoM:
200 MeV
with angular acceptance
with thick target
MOCADI
simulation

## Slide 7: Momentum Distribution in Fragmentation Reaction
A. Bacquias, Phys.Rev.C 85, 024904 (2012)
exp. data V. Henzl, thesis 2005, U. Prague
Fermi momentum of bound nucleons
Mom. transfer by evaporated nucleons
Coulomb expansion in multi fragment.
Bacquias’ model
Experiment FRS@GSI
Morrissey

## Slide 8: Br-DE-Br Separation Method
78Ni
scheme of FRS @ GSI, L=72m
DE Z2

## Slide 9: Br-DE-Br Separation Method
78Ni
Dp/p1 = Dp/p2
with p1 > p2  cooling ?
Non-Liouvillean system.
Coupling of longitudinal and transverse emittance,
Dp  Dp / f (f>1), but ex  ex * f
In addition angular and energy-loss straggling.
Overall achromatic system,
keep achromatic with
shaped degrader.

## Slide 10
Super-FRS
target
degrader
Brmax = 20 Tm
Brmin = 2 Tm
Brmax = 13 Tm
Brmin ~ 9 Tm
beam spot on target
~ 1 – 20 mm2
initial acceptance:
DA = ± 40 mrad
DB = ± 20 mrad
Dp/p = ± 2.5%
after thick shaped degraders
DA, DB ~ 20 mrad, Dp/p = ±2.5%
but ex,y ~ 100-300 mm mrad
238U28+ 0.8 - 2 GeV/u
to CR
max. 1x108/spill
740 MeV/u

## Slide 11
Super-Conducting Magnets
+ High intensity Target
8 short + 25 long multiplets (triplets + sextupoles and octupoles)
first short ready, last installed 2024
SC-dipoles divided
into 3 parts -> 30
Graphite target wheel
energy deposited in 50-100 ns.
5x1011 U/s on 1 cm2
--> E/m = 1.4 kJ/g
Most materials melt, or thermal stress damage,
mm2 spot not possible
d=0.45m
7 m
≈60 ton
raperture = 19 cm
2.4 m

## Slide 12
Separation in Storage Rings
After cooling only |D(m/q)| < 10-3 should survive,
Worst case fission: No pure isotopes
even with small beam spot at the target.
combined with cut by Super-FRS good separation.
Problems only for low integer ratios, like m/q = 2 or 2.5
With large spot even more nuclides

## Slide 13: Emittance
Depends on:
initial spot size
target thickness
nuclear reaction
degrader thickness
Here 1.5 GeV/u 238U on
4 g/cm2 C target, fission to
132Sn with 740 MeV/u
at exit of Super-FRS.
Too large momentum spread
can be cut with slits in
dispersive focal plane of
Super-FRS.
Dp/p [%] = x at FMF2 [cm] / 5.8 cm/%

## Slide 14
Identification In-Flight
Br = m/q bg c0
Br from magnet setting and position detectors at dispersive focal planes (e.g. TPCs, MWPCs).
thesis V. Henzl, CTU Prague 2005.
238U on H target, FRS@GSI
Velocity (bg) from ToF over larger distance (20-100 m)
mostly by plastic scintillators
Z from DE in ionization chamber
= m [amu] / q [e]
But only with quasi DC beam !

## Slide 15: Diagnostics for RIBs
Super-FRS has particle detectors for full A, Z identification
(ionization chambers for DE, x position x, ToF -> velocity)
of each ion at rates up to MHz --> not useful for fast extraction.
Use Schottky diagnostics in CR (resonant Schottky by ILIMA).
Resolution only after cooling, only as good as cooling.
Mass number identification requires Dv/v < 10-3.
Fine differences to identify also within isobars require Dv/v < 10-5,
only possible in isochronous mode (uncooled).
Adjust separation with slowly extracted beam, afterwards only
beam profiles (sometimes with intense peaks for guidance).
Go in steps from stable beam to extreme RIBs.
No electron cooler, also not in HESR for beginning.

## Slide 16: Schottky Diagnostics in the Ring
Measure revolution
frequency from noise
of pick-up.
Very sensitive down to
single ions.
Example from ESR at GSI
(electron cooled beam)
relative mass difference
Dm/m = 2.6x10-5
Intensity changes with time
because of EC decay of
140Pr into 140Ce.
time after injection [min]

## Slide 17: Summary
RIBs are an essential part of FAIR physics program,
some experiments with cooled beam directly in CR others in HESR.
Separation by Super-FRS not sufficient due to large Dp/p of fragments,
worse than for slow extraction due to enlarged beam spot on target.
RI beam can contain ions with different D(m/q) up to few %.
Intensity ratio can be up to 1:10 in favor of others.
 Separation during cooling or with scrapers after cooling can help.
Primary beam 5x1011/spill  fragmentation or fission in flight,
production rates for cooling in range: 1000 – 108 /spill,
for many experiments accumulation will be needed.
Emittance at end of Super-FRS depends on case (100-300 mm mrad),
good Br collimation possible.

## Slide 18
The fate of accelerated ions
Yeah, I am an accelerated ion.
By the way, what
do you do with accelerated ions?
Aaarrgh !

## Slide 19
Emittance Growth with Targets
Momentum transfer by reaction in target increases transverse momentum spread,
but in a thin target x does not change much.
Interaction with Matter (Targets)
x
tan(a) =px/pz
x
tan(a)
primary particle
secondary particle
pz
pz
px
Make small beam spot to avoid large emittance for secondary beam
a

## Slide 20: Limits by Targets
Simple temperature and stress calculation
melting?
Example (FRS at GSI):
1010 U/spill at 125 MeV/u on 1mm2 spot,
 dQ/dm = 2 kJ/g, DT = 4000 K (in Cu)
Cu
Al
graphite
Super-FRS at FAIR 5x1011 U ions/spill
use graphite, but requires enlarged spot.
1mm thick plates
Cu diamond
20mm
pressure
Instantaneous energy deposition
Initial compressive pressure P, wave propagates
(vsound) to target boundary  tensile stress.
P > spall strength, plastic deformation, P > yield strength ? not exactly elastic, cyclic stress, cracks ?

## Slide 21: Two-Stage Separation
Problem: contamination from reactions in degrader
Example: 48Ni from 58Ni primary beam with two thick degraders (d/R=0.5)
Solution: two degrader stages.
2x107/s at
1012/s primary
Simple analytical transmission program verified by MOCADI simulation with 1400 input files and 5*108 ions.

## Slide 22: Why ?
Reactions with Rare Isotopes
Proton scattering is a technique to learn about matter distribution.
Like once Rutherford with a particles on gold foil,
with ~ 1 GeV proton beam on target made of material of interest.
Not possible for short lived radioactive nuclides.
 Reverse role of target and beam, shoot RIB on hydrogen target.
A very clean way and sensitive way is inside a storage ring.
Extremes of matter distribution inside nuclei
11Li 208Pb
Shape of nucleus follows from
shape of scattering distribution.

## Slide 23
Scattering of RIB on Hydrogen Target
measure position and energy with Si detectors

## Slide 24
56Ni(p,p) scattering distribution
Diffraction Pattern (like for a wave after a single slit).
Extract radius of nucleus by fitting theory with parameters.
EXL collaboration, first such investigation for RIBs.
 RMS radius of 56Ni = 3.76 ± 0.08 fm
Physica Scripta T116 (2015) 014005.

## Slide 25
EXL technical proposal 2008
Luminosity with gas jet target