## Slide 1: HESR/cosy hardware system of Stochastic Cooling
January 21 | R. Stassen
Cool19 GSI

## Slide 2: outline
Installation of HESR stochastic cooling tanks at COSY
Optical hardware, custom products
Experience with GaN amplifiers
cooling results of last two beam-times in 2018 with PANDA cluster target

## Slide 3: HESR Pu and kicker installation
1. HESR Pickup-tank
FCT
Space for
BPM tests
Rogowski
coils

## Slide 4: Status Installation HESR cooling system at cosy
Transfer-lines: two hollow fiber lines (horizontal and vertical cooling), one Coax-line (longitudinal cooling)
Five power amplifiers installed (two horizontal, two vertical and one longitudinal)
Two switchable delay-boxes installed at Kicker (needed to use up to 4 amplifiers for one cooling direction at different energies).
All needed delay-lines at pickup installed, but still not remote controllable.
Optical delay-lines installed to adjust system-delay
beam
horizontal
vertical
longitudinal

## Slide 5: Optical devices
JDSU MAP2000
Multiple application platform used for notch-filter
modules for laser, attenuators, power-meter, splitter etc.
External mach-zehnder modulator

## Slide 6: Optical devices
Miteq transmitter and receivers, General photonics delay-line, Agiltron delay-line
Transimpedance amplifier included
Receiver installed in JDSU system
1ns step
Very precise, but ‘zero-length’ about 20ns
Optimized version possible, but very expensive
Attenuator included

## Slide 7: Optical devices
ViaLite RF over fiber
Best performance with acceptable price
Gain adjustable
Tested at COSY with hollow fiber as transmission line between PU and KI

## Slide 8: Optical devices
Hollow fiber
Advantage:
High speed: 99% c0
Low temperature coefficient
But:
Sometimes amplitude and phase changes
High losses at transition to FC/APC
Zero-span
Sweep-time: 2 sec

## Slide 9: Programmable delay lines to cover the HESR momentum range
Custom product by IMST
3 different modules:
Module 1: 10mm, 20mm
Module 2: 20mm, 40mm
Module 3: 20mm, 40mm, 80mm, 160mm
equalizer to compensate frequency response of all modules
Concept: Switches optimized with changing reference-plane, advantage: equal number of switches, minimized numbers of switches

## Slide 10: Programmable delay lines to cover the HESR momentum range
Custom product by IMST

## Slide 11: GaN amplifier (100 Watt)
Custom product by Nanowave
Some amplifier running at COSY for more than 6000h without any problems
Cooling switched on during acceleration
16 amplifiers delivered, first amplifies with different absolute phase (under discussion)

## Slide 12: Longitudinal new measurement setup -> talk: Nikolay
All BTF measurements with new setup
Very short system set-up time
Measurement and cooling simultaneous
Control of parameters (e.g. system delay or notch-frequency) during cooling.
Switch
NWA
from PU
S
w
i
t
c
h
to KI
P1 P2
Notch-filter
2 : 1 combiner
2 : 1 combiner
2 : 1 combiner

## Slide 13: Vertical cooling: Beam profile measurements with IPM
Vertical cooling only
Coupling due to identical tune
Vertical cooling only
slightly change of tune

## Slide 14: PANDA Cluster Target meets HESR Stochastic Cooling at COSY
Only target: Target thickness: atoms/cm” ! Thickest cluster target ever in COSY
Fast energy loss and emittance growth immediately visible
High beam loss (more or less whole beam lost after 5 min cycle)
Change of local frequency slip factor (frequency change due to energy loss changed sign)
Schottky spectra at 2000th harmonic

## Slide 15: Target with Barrier-Bucket operation
BB-Voltage: +/- 200V
BCT and counting-rate
COSY-BB not high enough
(HESR-BB: +/- 2.5kV)

## Slide 16: Longitudinal cooling with barrier-bucket and full PANDA cluster target (1-2 ∙ 109 protons)
Beam loss significantly reduced
Fast cooling at beginning of cycle (~ factor 2)
Very stable equilibrium for the rest of the 5min cycle

## Slide 17: PANDA Cluster Target meets HESR Stochastic Cooling at COSY
Chart: PANDA Cluster-Target with Stochastic Cooling

## Slide 18: Beam-time with 2MeV E-Cooler
2.425 MeV/c with e-cooler magnets
Dispersion zero in straight sections
Only vertical cooling on
Horizontal cooling due to solenoid fields of 2MeV cooler.
3-D stochastic cooling with e-cooler magnets was prepared within two shifts.

## Slide 19: Electron Cooling, stochastic cooling & Cluster-Jet Target
Target (1015 atoms/cm-2) and Barrier Bucket (0.4kV Pk-Pk)

## Slide 20: Electron Cooling & Cluster-Jet Target
Reduced target thickness (2⋅1014 cm-2)

## Slide 21: Electron cooling with transverse stochastic pre-cooling
No target

## Slide 22: ToF cooling (Time of flight)
5 minutes
Best system delay
+ 10ps
180° phase shift realized by change of system-delay (not optimum)
Even with such low eta-value (η = -0.035), ToF cooling was visible
ToF Cooling performance strongly dependent on system-delay
Best system delay
+ 10ps

## Slide 23: Transverse cooling with different gains
betatron sidebands
Switching to lower gains
Higher gain shows faster cooling, but higher equilibrium.
Gain-control during cycle useful
Stochastic heating
by change of delay
Fast cooling
High gain
Gain adjusted in optical regime:
Works fine for both transverse systems but not for longitudinal cooling due to the limit dynamic range of the notch-filter
Transverse equilibrium limited by small beta-functions at PU:
βx ~ 8m
βy ~ 15m

## Slide 24: Automated Open/closed loop measurements
Signal reduction
Good and fast method for checking the system settings
…
…
…

## Slide 25: Preparation for next beam-time
Installation of additional amplifier for longitudinal cooling (increase of power)
Gain adjustment of longitudinal cooling outside the optic regime
Cooling at different energies:
  Lower momenta always possible (lowest momentum: 1.5GeV/c)
  Highest momentum for existing setup:
      Transverse: delay margin ~10ns -> 3.3 GeV/c
      Longitudinal: delay margin ~1.5ns -> 2.5 GeV/c -> use of hollow fibre line with shortest path will gain several meters, but additional noise -> cutting the feed lines of optical delay-lines

## Slide 26: summary
HESR stochastic cooling hardware successfully tested
Full 3-D stochastic cooling with original HESR pickup and kicker at COSY (up to )
Full compensation of energy loss and emittance growth by PANDA cluster target () with ‘light’ cooling version was achieved
Dynamic range of optical notch-filter limits use of optical gain control for longitudinal cooling
Transverse Stochastic pre-cooling improves electron cooling

## Slide 27: Ongoing production of cooling tanks
Begin of cooling
end of cooling

## Slide 28: Thanks for your attention and…….
Many thanks to
      Bernd
      Nikolay
      Peter
      Ralf (ZEA1)
HESR stochastic cooling system is well prepared for beam at HESR
We would like to invite everybody to join our next beam-time