## Slide 1: Marina Dolinska 22nd January, 2019
Time domain approach for
Stochastic cooling study

## Slide 2: Outline
Basic principle of stochastic cooling
Time domain method
Time domain approaches
Signal response on kickers
Noises
Example of cooling simulations at the CR

## Slide 3
Let us consider the basic principle of stochastic cooling
This principle happens in real cooling process
Time-domain method can reproduce this process very closely to reality.

## Slide 4: Stochastic cooling system
Pickup – detect the beam parameters
Electronics – transfer signal, filter, amplify
Kicker – correct
These devises are places in storage ring, which parameters are important for stochastic cooling system

## Slide 5: Basic principle of stochastic cooling
One particle consideration
Measure position and apply a correction.
One particle passing with maximal position at PU
Requirement: particle crossing the reference orbit at kicker with maximal angle
Trajectory of not ideal particle
Closed orbit of the ring
(trajectory of the ideal particle)
ΔX‘=gXs,
g – normalized gain
[0<g≤1]
Kicker eliminates angle deviation

## Slide 6
In the real process one has up to 1013 particles.
In ideal case it would be good to
recognize each particle and then
correct it. But one needs a very fast
(high speed) system with a frequency
1010-1020 Hz. This is practically
impossible.
In this case the system considers small groups (ensemble) of particles.
The number of particles in one group is defined by frequency characteristic
of SC system.
Basic principle of stochastic cooling

## Slide 7
Center of gravity of one sample Position with respect to the reference orbit. Pick-up detects the value of this displacement and forms the signal.
samples
Mean value of sample
Basic principle of stochastic cooling
The coasting beam is sampled. The number of samples and its time length
is defined by frequency range [f1 ; f2] of SC. Bandwidth W=f2-f1
Example: nominal value of W for the CR W=1 GHz
ts=1/(2W)
The number of samples is n=Trev/ts (for the CR it is about 1500).
The injected number of particles is around 108. This means, one sample contains of 6.7*104 particles.

## Slide 8: Basic principle of stochastic cooling
The sample of particles passing the kicker gets correction of the mean position. The individual particle coordinate is reduced by the mean value of ensemble.
After one turn one has not full cooling. “Stochastic” behavior of samples must be considered in the full time interval. The mean value of each sample is changed during one turn.

## Slide 9: Mixing
All particles migrate from one sample to another one because of energy deviation from reference energy. This particle migration is called “mixing”.
mean value evolution of one sample
mean value appears
Because of mixing the new mean value of sample is formed.
At the next turn the pick-up detects this value and then the kicker corrects it again
For quantitative description of this process the time domain consideration can be used.

## Slide 10: The time domain approaches
The beam dynamic is calculated particle by particle and turn by turn
Beam sampling (or binning) is applied in the timeline.
Mixing is calculated like in the real cooling process.
Pick-up and Kicker action (considering noises and kicker signal response)

## Slide 11: The computer code has been written The main ideas of this code: Several number of samples is taken to study cooling process.

## Slide 12: Approximation 1: number of samples
Example CR : The number of samples is 1500 (n=Trev/ts). One sample contains 6.7*104 particles.
It is not necessary to track all samples like in the real process.
One can consider only few samples (for example 5).

## Slide 13: Particle generation in longitudinal phase space
The particles are generated in a certain time-window: Tw=nsts
Number of samples can be ns = 5 - 10
The initial momentum deviation in the frame [–dp/p : dp/p] is defined for each particles.
The initial time in the frame [0 : Tw ] is defined for each particle.
The samples are structured (depending on time the particle is assigned
to certain samples)
The history (variation of coordinates x, x’, y, y’, dp/p, t) of this sample is
calculated turn by turn.
Revolution time
Tw
Tw
(Tw =2.5 -5 ns)

## Slide 14: Particle generation in transversal phase space
Finally the ensemble of N particles is generated in 6D phase space.
Each particle has the six coordinates (x, x‘, y, y‘, Δp/p, t)
transformed to normalized phase space
simulation becomes simpler

## Slide 15: Approximation 2: Mixing
We consider the “bunch” (several samples) with the time length from 0 to Tw
(x, x‘, y, y‘, Δp/p, t)
Mixing: the particle migration is performed inside this “bunch”.
Every turn the time of each particle is changed by value of
T0 revolution period
η – ring parameter
ti+1 =ti + Δti

## Slide 16
At the Pick-up the mean value of each sample is calculated
s - sample number (max ns)
Ns – number of particles in one sample
Approximation 3:
Pick-up action

## Slide 17: Mixing on the way from Pick-up to Kicker
On the way from Pick-up to Kicker mixing takes place.
The particles migrate from sample to sample, which means the time coordinate of each particle is changed by Δt
bad mixing
D(s) - dispersion function
ΔL – path length
ρ – bending radius of dipole
-0.011 (pbar optics)
0.18 (RIB optics)

## Slide 18: On the way from Pick-up to Kicker
Betatron oscillation
The particle coordinate in the transversal phase space is changed due
to betatron oscillation in the ring.
In the normalized transversal phase space it is simple rotation
The phase advance Pick-up→Kicker

## Slide 19: Kicker action
At the kicker correction is applied. All particles of sample get the kicker correction and energy change
g – is a normalized “gain” parameter
[0 < g ≤ 1]

## Slide 20: Mixing on the way from Kicker to Pick-up
Mixing takes place. The particles migrate from sample to sample, which means the time coordinate of each particle is changed by Δt
good mixing
Here Δµ can be any
In transverse plane the coordinates are recalculated
∆t >>0

## Slide 21: Time domain approach One turn
Lattice and SC system parameters
Particle generation
Analyses of distributions ( Δp/prms and εrms )
Pick-up action
Mixing on the way Pick-up – Kicker
Kicker action
Mixing on the way Kicker – Pick-up
Stop after N turns
one turn

## Slide 22: cooling effect in time domain treatment
cooling effect in ideal case is calculated by simple formulae:
In reality one has to take into consideration the electronic noises and
kicker signal response. Noises and kicker response are the specific
characteristics of all SC components.
Then the given formulas must be modified according to this SC system .
Let‘s look how the signal is proceed in the SC system.

## Slide 23: Noise of signal
δnoise
Noise in the time domain treatment
is still a subject of study :
how to calculate δnoise
Up to now the analytical approach is used

## Slide 24: Noise of signal
factor α is introduced in the formulae
D.Möhl, Stochastic Cooling of particle beams, Springer-Verlag 2013.

## Slide 25: noise-to-signal ratio
noise-to-signal ratio :

## Slide 26: Kicker response
inverse Laplace transformation

## Slide 27: Kicker Response
s(t)
1
the normalized gain is transformed according to shape of signal at the kicker.
s(t) – is normalized function (max is 1)
inverse Laplace transformation
signal shape at kicker

## Slide 28: Kicker response of CR SC System
inverse Laplace transformation
signal shape at kicker (Palmer)
In both cases we normalize the max. responses to unity. The used time signal (real part of the inverse Laplace transformation) is antisymmetric with respect to t=0
t=0 is the center of sample
in the code after Laplace transformation the obtained curves are represented by
simple formulas of polynomial of 4th order.
signal shape at kicker (notch filter)
0

## Slide 29
These formulae for calculation of cooling in time domain approach
cooling effect in time domain treatment

## Slide 30
Benchmarking of MPT-6D
Measured emmitance and Δp/p at ESR (PALMER cooling)
MPT-6D calculations
Argon beam : 36Ar18+,
E=400 MeV/u
W=0.8 GHz
η = 0.31
gain g and parameter of noise α are adjusted
F. Nolden, et. al. Proceedings of EPAC 2000,conference
calculated
measured

## Slide 31: Cooling of ions at CR
Palmer method
System bandwidth W= 1 GHz
Uranium beam 231U92+
Energy 740 MeV/u
η=0.17

## Slide 32: Cooling of ions at CR
N=104 macro-particles
ns=5 number of samples
MPT-6D and analytical calculation of cooling with Palmer method

## Slide 33: Cooling of antiprotons at CR
System bandwidth W= 1 GHz
Antiprotons
Energy 3000 MeV/u
η=0.011
Notch filter method

## Slide 34: Cooling of antiprotons at CR
Gain parameter is varied to find optimal value
2.5x10-4
1.2 mm*mrad

## Slide 35: Cooling of antiprotons at CR
N=104 macro-particles
ns=5 number of samples
MPT-6D code. Test of Kicker response, where
the given analytical formulae are used for calculation of cooling

## Slide 36: Conclusion
Time domain approach is more advanced method
(simpler, multi-dimension, mixing simulation close to reality, other effects can be easy integrated, simulation time is reasonable (10-30 min depending on N)
Next steps:
Frequency characteristic of electronics
Plunging of electrodes
Combination of different methods (Palmer + Filter for ions)
Other effects can be included (IBS, target effect, RF-cavity (bunch rotation, barrier bucket), other...?).