## Slide 1: the RFQs in IMP
Yuan He
On behalf of Linac Center
Institute of Modern Physics, CAS

## Slide 2: Outline
CW high-intensity RFQs activities in IMP
Structure and Conditioning of the RFQs
Problems happened to the RFQs
How to make a stable RFQ always?
Notes: This is the outline

## Slide 3: CW RFQs constructed in IMP
 | ADS RFQ injector II | CMIF-RFQ | D-RFQ-973 | LEAF | SSC-Linac
Project served | CiADS | CMIF | BisoL | HIAF | HIRFL
Freq. (MHz) | 162.5 | 162.5 | 162.5 | 81.25 | 53.67
Type | 4-vane | 4-vane | 4-vane | 4-vane | 4-rod
Dipole mode | PiMS | PiMS | window | PiMS | -
Species | Proton | Deuteron | Deuteron | HI A/q=7 | HI A/q=7
Vane V (kV) | 65 | 65 | 60 | 70 | 70
I (emA) | 10 | 10 | 50 | 2 | 0.5
Inj. E (keV) | 35 | 40 | 40 | 98 | 25
Ex. E (MeV) | 2.1 | 3.0 | 1 | 3.5 | 1
Kp | 1.2 | 1.4 | 1.68 | 1.5 | -
CW Op. (emA) | 11 | 2.5 (P) | 1.8 (H2+) | 0.5 (HI) | 0.2 (HI)
First beam | Jun. 2014 | Nov. 2017 | Jun. 2018 | Feb. 2018 | Jan. 2015
Institution | IMP/LBL | IMP | PKU/IMP | IMP | IMP/PKU

## Slide 4: Chinese ADS Front-end Demo linac (CAFe)
HEBT
DUMP
Beta=0.1
IMP
IHEP
Beta=0.21
Beta=0.15
IMP
162.5 MHz Taper HWR
Goal: to demonstrate the technology of 10 mA CW beam of superconducting front-end Linac for CiADS.
Design: 25 MeV, 10 mA, CW, 4.5K
IMP collaboration with IHEP 2011 ~ 2017
Supported by “Strategic Priority Research Program” of the Chinese Academy of Sciences.
ADS RFQ：2014-2017
CMIF RFQ：2018-
P, He

## Slide 5: RFQs for CAFe
Apr. 17 to Jun. 6 ’14, condition to 90 kW
June 6th, 2014，the first beam, 2.16 MeV
June 21st, the first CW beam @ 2 mA
June 30th，10 mA, CW, 21 kW, 4.5 hours, transmission >97%
CW RF Operation 5904 hours
Offline in Jan. 2018
15
2017.11.15, H +, 3.4 mA; H2+, 7.8mA
2018.12.17-19, 4He2+ , 46 hours
Nov. 2017, short pulse condition to 135 kW
Online in Oct. 2018
Operation from Nov. 2018, RF Operation time, pulse, 312 hours
Notes: 162.5MHz ADS RFQ从设计、加工到运行历时3年。2014年6月30日达到10mA连续束设计指标，7月通过中科院组织的专家测试，到目前已累计运行900小时以上，毫安级连续束约46小时，是国际上唯一稳定运行的连续波强流RFQ。陈佳洱院士评价其为“国内第一，国际先进”。除了组织项目实施和关键技术攻关以为，还在下面四个方面做出了创新性的贡献。

## Slide 6: RFQ for LEAF
Feb. 2018, condition to 1.1 nominated power in 44 hours; 200 uA CW 4He+ beam，100 uA CW 14N2+，energy is 0.5 MeV/u
Operation time, CW, 589 hours

## Slide 7: Outline
CW high-intensity RFQs activities in IMP
Structure and Conditioning of the RFQs
Problems happened to the RFQs
How to make a stable RFQ always?
Notes: This is the outline

## Slide 8: Structure of ADS RFQ
48 sensing
loop ports, Regularly spaced
2 RF input ports
Both in Module 2
One near side, one far side
80 Tuners
Equal spaced
20 per module
32 Pi-mode Rods
Equal space,
8 per module
Consists of four modules, each
module is 1050mm long

## Slide 9: Thermal analysis of the cavity body
Max. Temp.: 26oC
Number: 8
Number: 4
Max heat flux 28.92 W/cm2;
Max temp of cutbacks 48.0 oC
Cooling water 20oC
Velocity < 2.5 m/s
70~105 W for each
Max. Temp.: 41oC
Max. Temp.: 30oC

## Slide 10: Cooling Water Loops
Chiller 1 (for vanes)
Vane: 4 Channels
in Parallel
Wall：
8 Channels
in Parallel
Pi-mode rod：
8Channels
in parallel
Vane: 4 Channels
in Parallel
Vane: 4 Channels
in Parallel
Vane: 4 Channels
in Parallel
Wall：
8Channels
in Parallel
Pi-mode rod：
8Channels
in parallel
Wall：
8 Channels
in Parallel
Pi-mode rod：
8Channels
in parallel
Wall：
8 Channels
in Parallel
Pi-mode rod：
8Channels
in parallel
Chiller 2 (for wall &
pi-mode rods)
Pressure gauge
Temperature monitor
Flow meter
Flow monitor and temperature monitor are required to be installed at the exit of each channel
Valve

## Slide 11: Conditioning of ADS RFQ
Pulse/CW alternatively
Pulse Beam
CW Beam

## Slide 12: Operation Status
Chart: Trips @ Usage of Solid-State Amplifier（108）
| Power Source Error | Cavity | Human error
 | 31 | 75 | 1
Chart: Trips @ Useage of Tetrode Amplifier（288）
| Power Source Error | Cavity | Interrruption of Power Supply | Human Error
 | 256 | 26 | 3 | 3
AMP change
Alarm of flux meters
EMC of vacuum gauge
chiller
Chart: 
| 真空保护 | 腔体水冷 | 打火
 | 30 | 36 | 9
Vacuum
Cooling
Arc
3264 hours
2638 hours
MTBF:11.3 hours
MTBF:24.4 hours

## Slide 13: Structure of CMIF RFQ
Tmax=30℃
Tmax=26℃
Tmax=33℃

## Slide 14: Conditioning of CMIF-RFQ
RF Power
* RF Power when arcing (kW)

## Slide 15: Structure of LEAF RFQ
 Max. T: 22.7°C, rised 2.7 °C
max deform.: 21.4 μm
max. stress: 10.99 MPa
SEY < 1 at coupler

## Slide 16: Conditioning of LEAF RFQ
Keep CW power conditioning
44 hours to nominal voltage 70 kV
Arcing when power was higher than 70 kW

## Slide 17: Structure of D-RFQ-973
Parameters | CST | ANSYS
Water velocity /m/s | 2.3 | 2.3
Cooling water/℃ | 18 | 18
Room /℃ | 22 | 22
Power /kW | 46.5 | 52.5
Max dT /℃ | 31.39 | 32.56
Max deform/μm | 73.27 | 75.24
Cooling channel
Thermal analysis
Aperture 40 mm

## Slide 18: Conditioning of D-RFQ-973
50 kW = 61.7 kV
Jun. 12-14, 2018
Keep CW power conditioning
47 hours to nominal voltage 60 kV
Arcing when power was higher than 50 kW

## Slide 19: Outline
CW high-intensity RFQs activities in IMP
Structure and conditioning of the RFQs
Problems happened to the RFQs
How to make a stable RFQ always?
Notes: This is the outline

## Slide 20: Blue Marks at the Exit of ADS RFQ
Aug 12, 2014, after conditioning and cw beam commissioning.
Apr. , 2019, checking after 6000 hours operation.
E
B
T
Temp. Max 21 ℃

## Slide 21: Blue Marks at Entrance of ADS RFQ
End-plate of the entrance is near two times farer from electrodes than one of the exit.
Due to beam loss of H2+ and H3+ , and than gas releasing?
Due to worse vacuum (1E-4 Pa) at entrance?

## Slide 22: Beam Loss Simulation of H2+, H3+
corn
corn
5% of H2+ and H3+ are loss in the entrance of 1.5 m of RFQ, 0.1% is on the tips.

## Slide 23: Blue Marks at PiMS of CMIF RFQ
Aug 12, 2014, after conditioning and cw beam.
Apr. , 2019, checking after 6000 hours operation.
Can not achieve nominal field after long term conditioning.
The max CW power was 110 kW. 100 kW was relatively stable.
Heavy discharge hapend in PiMS hole.
Multipactor?
CMIF RFQ
ADS RFQ
ADS RFQ

## Slide 24: Multipactor in RFQs
Multipactor simulation in CMIF RFQ
Possible Multipactor in ADS-RFQ
3 ns
6 ns
120 ns

## Slide 25: Multipactor of Coupler of ADS RFQ

## Slide 26: Discharge w/o Arc (spark)
Discharge of LEAF-RFQ（1/2hours，60 kW）
LLRF detector
Arc detector

## Slide 27: Something Uncertainty
D-RFQ-973
ADS RFQ
Blue mark between sections

## Slide 28: Outline
CW high-intensity RFQs activities in IMP
Structure and conditioning of the RFQs
Problems happened to the RFQs
How to make a stable RFQ always?
Notes: This is the outline

## Slide 29: A little bit confuse!
 | radial matching gap （mm） | fringe-field gap （mm） | Aperture on end-plates | voltage （kV） | vendor
ADS | 10.040 | 5.987 | 10/15 | 65 | KJTJ(IMP)
CMIF | 9.704 | 5.295 | 10/15 | 65 | KJTJ(IMP)
LEAF | 11.019 | 5.579 |  | 70 | KeLin
973 | 8.011 | 7.988 | 40/40 | 60 | KJTJ(IMP)
 | R0 （mm） | a （mm） | max m | kp | vendor
ADS | 5.731 | 3.16 | 2.376 | 1.17 | KJTJ(IMP)
CMIF | 4.807 | 2.74 | 2.279 | 1.4 | KJTJ(IMP)
LEAF | 5.805 | 3.63 | 2.035 | 1.55 | KeLin
973 | 3.477-5.971 | 2.63 | 1.86 | 1.68 | KJTJ(IMP)

## Slide 30: Just thinking……
To optimize Bpeak/V(Eacc), Epeak/V(Eacc), especially at the corner of electrodes and end plates.
To optimize the multipactor, especially the coupler, PiMS, etc. Try to make SEY < 1.
To optimize structure of contact. RF fingers or springs will be burned due to bad contact.
To put “cleanness” on the “first” position. It is not only in the stage of assembly, tuning and installing, but also in the stage of fabrication from acid washing to brazing.
Any more……?
Lessons from the bad experience of ADS and especially CMIF RFQ:

## Slide 31: Assembly and tuning in cleanroom
The first ADS RFQ was in dirty surroundings.
CMIF and D-RFQ-973 were in clean room.

## Slide 32: Optimize Epeak and Bpeak
--- Varied voltage
--- Constant voltage
--- Varied voltage
--- Constant voltage

## Slide 33: Acknowledgement
LBL: Derun Li, Steve Virostek, Matt Hoff, John Staples
FNAL: Sergei Nagaitsev, Gennady Romanov
PKU: Kun Zhu, Yuanrong Lu, Pinpin Gan, Qi Fu
IMP: Chenxing Li, Weiping Dou, Liang Lu, Xuejun Yin, Bin Zhang, Xiaofeng Jin, Zhijun Wang, Wei Ma

## Slide 34
Thanks for your attention