## Slide 1: Beam dynamics issues in high-current RFQs
M. Comunian

## Slide 2: Index
IFMIF RFQ DESIGN
RFQ input conditions ->LEBT Effects (Simulation <-> Measurements)
RFQ beam transport -> Ideal vs Real RFQ (Simulation <-> Measurements)
RFQ beam output -> MEBT Effects (Simulation <-> Measurements)

## Slide 3: IFMIF RFQ design
The voltage is increased following an analytic law
The focusing in the Gentle Buncher is strong (B=7) so to keep the tune depression above 0.4 for the best control of space charge.
Main resonances are avoided in the accelerator section
The focusing in the shaper raises from 4 to 7 to allow an input with smaller divergence.
Modulation “m”, average aperture “r0” [cm], small aperture “a” [cm], Voltage/100 [kV] E0 [MV/m], Acceleration factor “A10”, Energy “W”, Focusing “B”,
-Sync. Phase/100 [deg], Pole tip “rho”, along the RFQ
Shaper GB Accelerator
Notes: Accelerator section design
Designed cell by cell
Voltage and R0 are given by an analytic law.
Surface fields Es as interpolation of PARI geometry file “V2TERM.txt”.
Synchronous phase was increased in linear way cell by cell from -60 to -32 deg.
Acceptance increased up to 4.2 mm mrad norm
Accelerator section design
Designed cell by cell
Voltage and R0 are given by an analytic law.
Surface fields Es as interpolation of PARI geometry file “V2TERM.txt”.
Synchronous phase was increased in linear way cell by cell from -60 to -32 deg.
Acceptance increased up to 4.2 mm mrad norm

## Slide 4: IFMIF RFQ design
Shaper GB Accelerator
Longitudinal and transverse Phase Advance along the RFQ
I=0 mA
I=130 mA
Tune depression
0.4
Notes: Accelerator section design
Designed cell by cell
Voltage and R0 are given by an analytic law.
Surface fields Es as interpolation of PARI geometry file “V2TERM.txt”.
Synchronous phase was increased in linear way cell by cell from -60 to -32 deg.
Acceptance increased up to 4.2 mm mrad norm
Accelerator section design
Designed cell by cell
Voltage and R0 are given by an analytic law.
Surface fields Es as interpolation of PARI geometry file “V2TERM.txt”.
Synchronous phase was increased in linear way cell by cell from -60 to -32 deg.
Acceptance increased up to 4.2 mm mrad norm

## Slide 5: Acceptance increase in the accelerator part
Shaper GB Accelerator
5 erms
IFMIF RFQ design

## Slide 6
Integral 0.96 mA
Integral 2.4 10^9 n/s
Integral 363 W
WB distribution 0.25 mm mrad rms norm
Beam losses
To achieve Beam losses concentrated in the low energy part is very important since neutron production is proportional to Energy2

## Slide 7: Error studies
The error study shows tolerances in beam alignment and electrode displacements of the order of 0.1 mm, while the RF field law has to be followed with an accuracy of 1-2%.
Example: displacement between two modules (9 modules)
Transmission and Power loss due to the segmentations applied with gaussian and waterbag input beam distribution.(TOUTATIS)

## Slide 8: RFQ construction and installation
SOFT 2016

## Slide 9: Real RFQ
Ideal Vane Shape
Real Vane Shape
The geometrical construction errors
has been introduced electrodes by electrodes
along the RFQ and the voltage tuning
-3%

## Slide 10
Ideal RFQ
Real RFQ
Power Lost=1482 W
0.2 mm
120 W
10 W
D+ 130 mA emit.=0.25 mmrad Gaussian dst

## Slide 11: Real RFQ: Final Phase Space
Very small impact on global losses (-0.4% Transmission) and beam behavior.
Ideal RFQ
Real RFQ
D+ 130 mA emit.=0.25 mmrad Gaussian dst
+10% emit. Long.

## Slide 12
Ion Source and LEBT

## Slide 13
IFMIF/EVEDA LEBT installation for beam commissioning

## Slide 14: LEBT behaviour for proton in pulsed mode at about 50 mA
Strong focusing
Weak focusing
Hyper
focusing
Hyper
weak
focusing
Focus before the cone hole
Focus after the cone hole
Smaller beam size
after the cone hole
Larger beam size
in the cone hole
Match zone
for the RFQ

## Slide 15
The neutralisation (99-90%, from FGA_H_50keV_20160324-1111.dat and trace-forward) implies after the extraction an emittance dominated beam.
The major part of the BD is dominated by the thermal term in the LEBT.
We are sensitive to a couple of percentage difference in the neutralisation, due to the fact that such difference is applied for almost 2 m.
From indirect calculation the exit of the extraction source seems to produce a too divergence beam at the first solenoid. Thus, the emittance growth is given mainly by the coupling from the solenoid nonlinearities (mainly) and space-charges. The emittance trend was confirmed experimentally (beam_report_23032016) and by simulations (COB20 presentation).
Therefore, the main objective is to reduce the beam dimensions at the first solenoid.
Generalised perveance,
=0
0.034
=0.01
=0
even less if emittance growth occurs
In the LEBT:
neutralisation factor
LEBT behaviour:
beam dynamics background

## Slide 16: Models for LEBT
Design models and simulations
Commissioning models and simulations
Generally should include as much as possible all the processes involved in BD (critical for LEBT part).
Large number of macro-particles
Normally not depending on measurements
Error studies, multi-species simulations, or space charge compensation processes could require order of weeks to be performed.
Generally should include just what is really necessary to describe the physics problem (e.g. the rms evolutions along the line).
It is mandatory to reduce the time needed for getting the results (half a day maximum)
Depends on measurements. This led to the development of ad hoc methods.
Field maps for strongly non linear elements (such as buncher and solenoids) and as built RFQ model.
Gives hints for initial tuning
Example of software: Tracewin error studies, WARP (3d simulations).
Approximations,
semi-empirical methods
Example of software: Tracewin (normal runs), Axcel and WARP (2d simulations), Toutatis
How to deal with S.C.C.?

## Slide 17: Commissioning model and trace forward method
Key points:
It takes the inputs from the measurements, trying to fix as many as possible parameters. If any error occurs in the measurement, it will be transported to the simulation
It needs the model from the simulation.
Estimate the beam input rms emittance and the Courant-Snyder parameters, via an iterative method.
Rms measured input @ output:
Rms simulated output @ input:
Model
Space charge compensation is normally a free parameter. However, the trend along z can be given by the design model simulations

## Slide 18: From the design model: example of residual potential of 135 mA deuteron beam at 100 keV
The RFQ cone and the emittancemter changes the s.c.c. pattern!
Copper RFQ injection cone
Wolframium EMU shield

## Slide 19: Example of results of the design model: Deuteron beam 135 mA, pulsed mode.
measurement
simulation
Phase spaces and x projection comparisons.

## Slide 20: LEBT behaviour: some points along the solenoid scan.
Sim.
Sim.
Sim.
Sim.
Meas.
Meas.
Meas.
Meas.
Beam_report_23032016

## Slide 21: Example of results of the commissioning models: 55 - 50 mA proton beam 50 keV.
in order to check the guess on the s.c.c. and on the initial Twiss, several emittance measurements were performed with different solenoid values and used in the trace forward cycle.
there is an overestimation of the tales, but the beam profile is respected (waterbag core + gaussian)
the best match parameters are retrieved at the RFQ input point.
Red experimental measurement
Blu simulation

## Slide 22: Comparing the studies and measurement we were able to give an empirical criteria* to accept or not the source+LEBT settings for injection into the RFQ
* Limit on RFQ input Emittance

## Slide 23
RFQ test bench

## Slide 24: Beam commissioning strategy
First step done: Beam at low current 6-22 mA proton @ 50 keV used as probe beam. The source PE was decreased down to 3 mm radius.
From simulation RFQ can transmit >99%(@6 mA) with up to 220% mismatch at this condition.
The proton fraction will be very low (down to 50%). Large fraction of needs to be taken into account in the experimental transmission measurement.
Pre RFQ emittance*
Emittance trans. and profiles.
Pre RFQ current
Currents and BPM
Current
Present step: Beam at high current 40-55 mA proton @ 50 keV used as probe beam. The source PE is 4.5 mm radius.
From simulation RFQ can transmit >95% with low mismatch at this condition.
The proton fraction is not bad (more than 70% ?). Same fraction of needs to be taken into account in the experimental transmission measurement.
Last Slide
Remaining part
of the talk

## Slide 25
MEBT has a relatively good energy selection. It separates the , the not accelerated particles from the main H+ beam at the D-plate. But a not negligible part of them will be transmitted through the RFQ.
LEBT
RFQ
MEBT
DPLATE
Almost all is lost
LPBD
10% Transmission

## Slide 26: The will affect the experimental transmission
Longitudinal position of the LEBT ACCT
Injection point of the RFQ, Theoretical transmission starts here
From the LEBT ACCT to the injection of the RFQ a not negligible amount of H2+ is lost. 4 cm.
RFQ cone
Repeller

## Slide 27: Expected trends at the LPBD
Voltage calibration curve with respect to the presence (or not) of contaminants
Expected reduction of about 5%
I_lebt=13 mA

## Slide 28: Transmission and current measurement vs RFQ Voltage
Not-removing contaminants
Removing contaminants
From Enrico Fagotti paper at LINAC2018
Good agreement
4 % losses
I_lebt=13 mA

## Slide 29
Due to contaminants
Due to emittance!
Transmission and current measurement vs RFQ Voltage

## Slide 30: RFQ Performances Due to emittance (40 mA working point)
Reducing the input beam emittance of 20% the losses reduces of a factor of 2.
From preliminary calculation, the Losses = 10% at LPBD. 2.5 times emittance growth after solenoid 1. Mismatched beam at RFQ.
RFQ
> 0.3 mm mrad + mismatch

## Slide 31
It was impossible to increase the transmission for the 40 mA point, confirming that the emittance was not suitable for the injection into the RFQ. It is needed to change the PE hole.
=30 mA
=40 mA
Low Emittance
High Emittance
Experimental Solenoid Scan

## Slide 32: Post RFQ emittance measurements
30 mA beam with different solenoids couples and = 62 – 70 kV. 1/3 of the full beam space charge effects. Different solenoids couples.
800 beam pulse length. Increased S/N ratio.
Bunchers OFF.
The simulation
Trace forward input beam from LEBT (4D-parabolic distribution). solenoid field maps. Tracewin+toutatis code.
Longitudinal space charge compensation profile from WARP code in the LEBT.
As – built RFQ model with voltage from bead pull measurement.
MEBT hard edge quadrupoles, buncher field maps.
The beam
3
2
1
96% +/- 6% of experimental transmission

## Slide 33
The RFQ is working as predicted
Point 3 will be investigated with simulations and post analysis.
Apart for point 3 , the emittance are in very good agreement.
There are same differences in the Twiss, but the trend is completely followed. When they decrease so that the simulation etc..
We have also explored indirectly the longitudinal RFQ dynamics (change in )
Ref. | Sol1 [A] | Sol2 [A] |  |  |  |  | 
1.1 | 135 | 160 | 66 | 0.26 | 0.24 | 6.0 / 7.5 | -4.1 / -5.5
1.2 | 135 | 160 | 62 | 0.25 | 0.24 | 7.2 / 8.1 | -4.8 / -6.0
2 | 135 | 162 | 70 | 0.23 | 0.23 | 5.5 / 6.3 | -3.6 / -4.3
3 | 131 | 162 | 70 | 0.2430.009 | 0.28 | 5.4 / 6.0 | -3.7 / -4.5
Ref. | Sol1 [A] | Sol2 [A] |  |  |  |  | 
1.1 | 135 | 160 | 66 |  | 0.24 | 6.0 / 7.5 | -4.1 / -5.5
1.2 | 135 | 160 | 62 |  | 0.24 | 7.2 / 8.1 | -4.8 / -6.0
2 | 135 | 162 | 70 |  | 0.23 | 5.5 / 6.3 | -3.6 / -4.3
3 | 131 | 162 | 70 |  | 0.28 | 5.4 / 6.0 | -3.7 / -4.5
!
Thank you to CEA and CIEMAT colleagues

## Slide 34: Recommendations
It is important to design the RFQ robust against input Twiss and mechanical /Voltage errors.
The losses cannot be completely avoid, so it is better to avoid them at high energy where they are more dangerous.
The major source of differences found up to now between the simulations and the measurements were due to wrong distances (electrodes, positions of detectors and optical elements). It absolutely mandatory to carefully check such distances in order to use the models fruitfully during commissioning.
If a difference is found between simulations or and measurements, a counter check should be made with care on BOTH sides.
Characterization of separate component is essential in order to decouple the problems: as a matter of fact, despite the physics at low current is easier with respect to high current, many complex effects can still occur (see contaminants and emittance growth). The result is a mess, or strange tuning of the machine.
The whole system proved to be quite reproducible in time. When something happens, strange results in emittance and currents, it is always advisable to check first the diagnostics.
It is important to fix the objective of the commissioning and design models: do they need to be able to predict at infinite precision the beam values? As soon as you are able to guide the commissioning and to predict the trend and with a certain error (10-20%) the quantitative values you should be happy. “It is important to be conscious of the approximations you are introducing in your model and their limits“

## Slide 35: Conclusions
The characterization of the beam dynamics of the RFQ requires a carful characterization and control of the systems which came before and after.
Development of models for the commissioning is highly advisable: it is not sufficient to design the machine, but, in order to make it work it is important to follow the commissioning.
They time spent in doing such goal allows to satisfactory characterize the RFQ beam dynamics.
One of the mission of the LIPAc beam dynamics team is to find the limits of the models above cited. This work is ongoing, and we are working to the possible upgrades which can improve the physics description even at higher currents, relying less as possible on measurements.
with respect to a pervance which is about 1/3 nominal perveance (i.e. 135 mA deuteron beam @ 100 kV):
The RFQ transverse dynamics was directly checked and work as expected.
The RFQ longitudinal dynamics was indirectly checked and it seems it is working as expected. It will be performed a longitudinal emittance measurement in future for a direct check.
Update: (11/4/2019) with 55 mA of proton the RFQ transmission is 96%.
Update: (12/4/2019) The RFQ has been conditioned up to 131 kV (10 us pulse).
As far as the RFQ design is concerned..

## Slide 36
BACKUP SLIDES

## Slide 37: Beam Dynamics done with Comparison of Parmteqm and Toutatis
Difference 0.2 %
Plot of RFQ Transmission as function of RFQ length, The toutatis runs are made with 1’000’000 macroparticles.
In this case the 3D Finite Difference poisson solver grid in Toutatis was “65x65x65 and 17x17x17”.
The PARMTEQM runs are made with 1’000’000 macroparticles. The 2D (r-z) Scheff grid was “20x40” for the Space charge solver (Image charge on, multipoles on).

## Slide 38: Gaps Effects
Gap distance [mm] | Transmission [%] Gaussian Dist. | Power Loss [W] | Max Es [Kp]* | Es Field Enhancement
0.05 | 94.4 | 1129 | 1.83 | 1.02
0.1 | 94.3 | 1136 | 1.86 | 1.03
0.2 | 94.2 | 1152 | 1.9 | 1.07
0.5 | 94.1 | 1247 | 2.1 | 1.17
1 | 93.2 | 1822 | 2.4 | 1.33
Runs with curvature r=0.5 mm
*Maximum Es=[1+d/(6*r)]*Es0
From P. Balleyguier [Linac 2000]
We use a gap of 40 μm with an
impact on Beam Dynamics (<0.1%) and
Surface field (<1%).

## Slide 39: Surface Field Enhancement on the GAP
Case with gap=1 mm
and r=0.2 mm
Ansys=1.6 eh
Formula=1.8 eh
We check the Electrical Surface Fields
Enhancement by using Ansys.
The results are similar
(with an error of +/- 10%).

## Slide 40: Beam dynamics Software
Software name | Used for | Developers | Time of life | Institution | License Type | Reference (Web Site)
TraceWin & Toutatis | LEBT+RFQ + MEBT | D. Uriot / R. Duperrier | 2000 - Now | CEA | Registered: No Source | http://irfu.cea.fr/dacm/logiciels/index3.php
Parmteqm | RFQ | K.R. Crandall et al. | 1980 - 2005 | LANL | Registered: No Source | https://laacg.lanl.gov/
Warp | Source + LEBT (neutralization) | D. P. Grote | 1980 - Now | LLNL/LBNL | Open Source | http://warp.lbl.gov/
IBSimu | Source | T. Kalvas | 2010 - Now | Un. of Jyväskylä | Open Source | http://ibsimu.sourceforge.net/index.html
AXCEL-INP | Source | P. Spädke | 1990 - Now | AET | Registered: No Source | https://www.aetassociates.com/index.php
Warp
Parmteqm
TraceWin
Axcel
IBSimu

## Slide 41
The FEM program Ansys 10.0 was used.
The Vanes shape by the LANL program Vanes.
The total number of runs was 489 (1 week run).
The Max surface fields is 1.83 Kp by Ansys.
1.8 Kp
2%

## Slide 42
Two strategies were explored in order to take into account of the space-charge compensation in the BD model:
  Design model
  Commissioning model:
Given the pressure, the cross sections of the various phenomena the software calculates the s.c.c. degree from the self-field compensation, which come from the dynamic equilibrium between the primary plasma (the beam) and the secondary plasma (residual gas ions and electrons). In this case
Software used:
WARP (t-code)
A costant factor is applied to the current of the beam, which depends with respect to the position along the LEBT.
Software used: TraceWin (s-code)
SOL1
SOL2
Injection cone

## Slide 43: Measurement of the profiles (Wire scanner)
Measure
Simulation
Sol1 = 135, Sol2 = 160. RFQ voltages 74-70-66- kV, 22 mA from the RFQ
RMS SIZE
RFQ Out
LPBD