## Slide 1
Review on Layout and Construction of the 36 MHz HSI - RFQ
U. Ratzinger, IAP
Goethe-University Frankfurt
GSI-ARIES-APEC- Workshop
Intern. Wissenschaftsforum Heidelberg
15.-16.04.2019,

## Slide 2: Content
Original motivation and early attempts
How the HSI - design got started
Complete layout
The IH – RFQ cavity
The beam dynamics and electrode designs
Frequency Tuning
-

## Slide 3: Original motivation
The construction of the SIS18-ESR complex at GSI began in 1986. However, there was no design for an adequate heavy ion linac injector
Vertical SIS18
tune shift
assumed
Penning
Source and
Wideroe 1-4:
Factor 500
missing!

## Slide 4: Early attempts
from the source - 13.5 MHz, 130 AkeV RFQ –
Gas stripper to - DTL to 216 AkeV – W2-injection
J. Klabunde et al., LINAC86 Conf., Stanford, p. 299
Design:
GSI & IAP
Into W2
of Unilac
sou
Gas Stripper

## Slide 5: Early attempts
RFQ – layouts for , front ends beam tested
13.5 MHz Split-coaxial-RFQ, R.W. Müller, GSI, and
with IAP support
R.W. Müller, Proc. LINAC79,
Montauk, NY, p. 148

## Slide 6: Early attempts
27 MHz Spiral – RFQ, IAP, with GSI support
Proc. LINAC92, p. 416.

## Slide 7: How the HSI - design got started
Results from MEVVA source beam tests
The MEVVA source can be tuned for
a maximum fraction of
After some more improvements in 1993 it turned out:

## Slide 8: How the HSI - design got started
Talk, Peter Spädtke,
Okt. 2010, IAP, Ffm
MEVVA Source with tuned charge distribution

## Slide 9: How the HSI - design got started
Design proposal bei UR
Complete
Wideroe W1-W4
Replacement.
No extra stripper
U. Ratzinger, Proc. EPAC94, London p. 288

## Slide 10: How the HSI - design got started
The requested HSI particle currents were similar to what is requested now for FAIR in case of , & -stripper
For
due to RFQ
Field Emission
& - stripper

## Slide 11: Complete HSI - layout
The project started in 1995 with GSI money
The design was based on a factor 2.5 voltage increase against
the former Wideroe structure within the same tunnel length
Most active TAC – Members for HSI – project:
Günther Plaas, CERN acc. director, Dieter Trines, DESY acc. director
Klaus Bongardt, beam dynamics expert, FZ Jülich

## Slide 12: Demounting the 27 MHz GSI Wideroe section in Nov 1998

## Slide 13: View into a 27 MHz GSI Wideroe tank

## Slide 14: The IH – RFQ cavity
- mode to realize 36 MHz at a reasonable cavity size

## Slide 15: The IH – RFQ cavity
U.Ratzinger,
K. Kaspar,
E. Malwitz,
R. Tiede,
S. Minaev,
EPAC96,
Sitges,
MOO07A,
p. 304

## Slide 16: HSI-RFQ Parameters
Norm. trans. em. x, y (mm mrad) 0.31

## Slide 17: The IH – RFQ cavity
Connecting the electrodes to the cavity stems by “crankshaft storage concept“
http://www.ws-technik.info/der-motorblock.html

## Slide 18: IH-RFQ MAFIA Simulations
No RF-Model was built, simulation only !!
K. Kaspar, U. Ratzinger, Proc. EPAC96, Sitges, WEP029L (p. 1973)

## Slide 19: IH-RFQ MAFIA Simulations
K. Kaspar, U. Ratzinger, Proc. EPAC96, Sitges, MOO07A (p. 304)
Pre-tuning by carrier rings

## Slide 20: IH-RFQ technology
Technical detail: Carrier ring and electrode
Konstruktion:
E. Malwitz,
H. Gaiser
W. Bleuel
D. Svrcina
K. Dermati
Kaiser
Galvanik:
H. Gaiser

## Slide 21: IH-RFQ technology
Measurement of field distribution
Achieved accuracy:
Measurement
and Tuning:
S. Minaev
R. Tiede

## Slide 22: HSI-RFQ
View on the installed IH-RFQ in the Unilac tunnel
Foto: A. Zschau, GSI
RF equipm.
G. Hutter
W. Gutowski
W. Vinzenz
….

## Slide 23: HSI-RFQ Entrance Chopper and Cone
Design: Ludwig Dahl

## Slide 24: HSI-RFQ
View into the 36.136 MHz IH - RFQ
Foto: A. Zschau, GSI

## Slide 25: Modular design allows electrodes exchange
HSI-RFQ
Foto: A. Zschau, GSI
Montage:
Schwedhelm
Thurau
Mühle
…..

## Slide 26: HSI-RFQ Beam Dynamics
A. Schempp, IAP, 1996

## Slide 27: HSI-RFQ Beam Dynamics
1998___ , 2008 ___, and new___, sugg. by
C. Zhang
Source: Chuan Zhang
Riezlern seminar 2016

## Slide 28: HSI-RFQ Beam Dynamics
Comparison of 3 designs
 | Design 1998 | Design 2008 | Chuan Zhang Design 2016
Input / Output Energy [keV/u] | 2.2 / 120 | 2.2 / 120 | 2.2 / 120
Inter-Vane Voltage [kV] | 125 | 155 | 125
Average Mid-Cell Aperture [cm] | 0.61 | 0.60 | 0.58
Maximum Surface E-Field [MV/m] | 31.9 | 31.2 | 30.2
Minimum Electrode Distance [cm] | 0.49 | 0.60 | 0.53
Number of Cells | 357 | 409 | 384
Length [cm] | 921.749 | 921.74 | 918.28
Input Beam Current [emA] | 16.5 | 20 | 20
Input Transv. Em. [π mm mrad] | 138 | 210 | 210
Input Transverse Twiss Alpha | 0.43 | 0.6 | 0.6
Input Transverse Twiss Beta [cm/rad] | 4.6 | 13.6 | 13.6
Transmission [%] | 89.5 | 88.5 | 94.1
Brilliance [mA / mm mrad] (80%) | NA | NA | 61.5
Source:
Chuan Zhang
Riezlern seminar 2016

## Slide 29: HSI-RFQ Beam Dynamics
Transverse beam size, design C. Zhang, 2016
mid-cell aperture
rms beam size
maximum beam size
Source: Chuan Zhang
Riezlern seminar 2016

## Slide 30: HSI-RFQ RF Conditioning
:
Too pessimistic
below 300 MHz
)

## Slide 31: HSI-RFQ Frequency Tuning
K. Kaspar, U. Ratzinger, Proc. EPAC96, Sitges, WEP029L (p. 1973)

## Slide 32: Running In with beam
Emittance
Measurements from several runs in 1999 along HSI.
Nominal current of 10 mA for was
achieved
behind RFQ!
Input: 20 mA !
Coordination:
W. Barth

## Slide 33: Running In with beam
Longitudinal measurement (P. Forck 1999)

## Slide 34: Conclusions
HSI was the final step in the SIS18 - ESR project
The realization became possible after the MEVVA source demonstrated intense - beams
IH-structures allowed a realization within the existing Unilac tunnel, former W1 – W4 location
The IH – RFQ underwent several successful electrode exchanges
The future exclusive short pulse operation
should significantly relax voltage limitations of
the IH-RFQ
HSI setup can fullfill FAIR specifications

## Slide 35: Thank you to our driving forces!
HSI Project-leader
Dieter Böhne
GSI Scientific Director
Hans Specht
GSI Accelerator Head
Norbert Angert
Time schedules
Dieter Bohn, FZ Jülich