## Slide 1: HPGe irradiation test and hyperatom experiment
Marcell Steinen
Panda Meeting 19-2, GSI, 6-25-19
Helmholtz-Institut Mainz

## Slide 2: Outline
HPGe Irradiation test at COSY
Feasibility studies of the hyperatom experiment

## Slide 3: HPGe Irradiation test at COSY
HPGe Irradiation test at COSY

## Slide 4: PANGEA in PANDA
HPGe crystals susceptible to neutron irradiation
PANDA (180 days): n fluence ≈1010 n/cm2

## Slide 5: HPGe irradiation test
Irradiation test at COSY with single crystal prototype
5.5 days COSY → 96 days PANDA

## Slide 6: Influence on spectrum of 60Co
Additional lines; enhanced compare to PANDA
Line shape changes: Low energy tails, worse resolution
Pulse shape analysis (PSA) allows partial recovery

## Slide 7: PSA: Moving window analysis
Digital pulse processing via moving window deconvolution
  Deconvolution
  Numerical differentiation
  Moving average (low pass)
Increased rate capabilities → Pile-up handling
M. Lauer, http://doi.org/10.11588/heidok.00004991

## Slide 8: Radiation damage correction
Low energy tails cause by trapped holes
Trapping prob. depends on path length of holes
Analysis of rising edge of detector signal → Radial interaction point

## Slide 9: Effect of Corrections
No correction After correction

## Slide 10: Gaussian shape recovery

## Slide 11: Results
DAQ and therm. issues decrease performance
PSA allows partial resolution recovery
Annealing recovers initial crystal performance → Detector withstands irradiation
New systematic test: TRIGA reactor (2019/20)

## Slide 12: Feas. studies: hyperatom exp.
Feasibility studies of the hyperatom experiment

## Slide 13: Hyperatoms
Hyperon puzzle in neutron stars
High initial (n,l) states
X-ray energy to keV-MeV
→ Germanium detectors
Radius of states:
→ Nuclear interaction in neutron rich periphery
→ Measurement of
Adaptation from T. Aramaki et al Astroparticle
Physics 49 (2013), pp. 52-62

## Slide 14: Observables

## Slide 15: X- - 208Pb observables
(9,8):
1.83 keV
1.33 keV
56.5 %
Calculations based on code by E. Friedman

## Slide 16: Production: Target system

## Slide 17: Secondary target
Split target system unique
  -> heavy targets possible
Optimization
  Max. X- stopping
  Min. X-ray absorption
Based on events generated in GiBUU

## Slide 18: Event selection
Signals after cuts (180 days): 1237
Signal efficiency: 0.9 %
Background suppression : 2∙106

## Slide 19: Systematics
Dominated by uncertainty of nuclear shape
High precision calibration via 152Eu
Centelles et al., Phys.Rev.Lett. 102 (2009) 122502

## Slide 20: Predictions

## Slide 21: Experimental Landscape

## Slide 22: Summary
Promising irradiation test at COSY
  PSA allows partial recovery of radiation damage
  Improvements at TRIGA in 2019/2020
208Pb hyperatoms allow to study X- optical potential in neutron rich matter
  Heavy hyperatoms unique at PANDA
  Higher rates than experiments at J-PARC
  Further improvement possible by more sophisticated cuts
Thanks for your attention

## Slide 23
Backup Slides

## Slide 25: FEP-efficiency PANGEA

## Slide 26: X- - 208Pb

## Slide 27: Absorber materials - observables