## Slide 1: PANGEA irradiation test at TRIGA
M. Bölting
HIM
PANDA Meeting 19/2, 2019-06-24

## Slide 2: Why?
Degration of HPGe under radiation
  Develop / optimize correction methods
Test at COSY not optimal
  Dynamic range
  Cooling problems
  New test desirable
2

## Slide 3: Possible Facilities
COSY
Knowledge of proton beam
Similar background
Difficult to get higher irradiation
TRIGA
High irradiation possible
No long wait time
Ease of access
Unknown rates

## Slide 4: TRIGA Mainz
Swimming pool reactor
Available power 100 mW – 100 kW
4 beam tubes
thermal column
rotary specimen rack

## Slide 5: TRIGA Mainz
Swimming pool reactor
Available power 100 mW – 100 kW
4 beam tubes
thermal column
rotary specimen rack

## Slide 6: Neutron spectrum
Quelle: http://nbn-resolving.de/urn:nbn:de:bsz:14-qucosa-231889
550 eV kinetic energy threshold for irradiation damage
6
Notes: PhD thesis Dr. Wortmann, 2007 simulations
Beam tube D user for ultra-cold neutron experiment
Beam tube a, b free
For Questions:
Graphite neutron reflector in center, D passes through it.
A, B, C don‘t
A, B, D look directly at the reactor.
C is tangential.
Thermal column ich mainly graphite

## Slide 7: TRIGA beam tube A
Electronics
Detector
7

## Slide 8: Fast neutrons @ TRIGA?
Three steps
  Measuring total rate
  Measuring fast neutron rate
  HPGe Irradiation
8

## Slide 9: Total Rate
Existing hardware – fast test (hours)
Simple DAQ
Slow neutron / γ shielding ?
9
Notes: DAQ: trigger rate of scope…
How much neutrons?
Is the next test feasible?
Bild beschriften!
Neutronen-Quelle Pfeil

## Slide 10: Fast neutron rate
Similar setup
Adjust power of TRIGA
Scintillator EJ276
  Discriminate fast n and γ
PSA similar to HPGe analysis
1-2 days
Nyibule et. Al. Digital Gamma-Neutron Discrimination with Organce Plastic Scintillator EJ 299-33
10
Notes: Feasibility study for irradiation test

## Slide 11: HPGe irradiation test
11
?
Notes: Which cluster?
Placement of cluster?
Neutron rate?
Slow neutron / gamma shielding between core and cluster?
Radiation Shielding?