## Slide 1: Unilac: QQ tests
RFQ: Vacuum pumping (2.xx E-7 mbar), RFQ input loop re-checked, okay.
QQ: Tests for operational limits done (12th Sep), magnet temperatures okay within limited operation. Wall closed.
Alvarez A3 pre-vac leakage (water), drying, IH2 pump valve to be exchanged/repaired

## Slide 2: Unilac: QQ tests
View from ion source
View from UNILAC tunnel
1st mirror plate
QQ11
2nd mirror plate
QQ12
3rd mirror plate
QQ13
4th mirror plate
QQ14
5th mirror plate
5th mirror plate
QQ14
4th mirror plate
QQ13
3rd mirror plate
QQ12
2nd mirror plate
QQ11
1st mirror plate
top:IR bottom:visual
top:IR bottom:visual

## Slide 3: Unilac: QQ tests
Testing environment:
  Magnets covered (cardboard) to emulate radiation protection wall
  Forced air cooling of beam pipe and magnet switched on
  Temperature of mirror plates 2,3,4 monitored by Type K thermocouples
  Temperature monitored by FLIR IR camera
  Safety switches (70°C) mounted on mirror plates 2,3,4
View between two magnets without air cooling
(mirror plates, safety switch holder, beam pipe housing, air nozzle)
... with air cooling

## Slide 4: Unilac: QQ tests
Testing scenarios:
  Magnet currents/strenghts, equivalent to max. needed for operation
  Timings: scenarios tested
Nomen | QQ11 | QQ12 | QQ13 | QQ14
Low-Br U(A/q=26) /V | 1,1 | 1,2 | 1,1 | 0,5
High-Br U(A/q=59,5) /V | 2,5 | 2,8 | 3,0 | 2,2
Low-Br I(A/q=26) /A | 119 | 132 | 122 | 54
High-Br I(A/q=59,5) /A | 273 | 301 | 325 | 235
Timing (reduction) | High-Br | Low-Br 1 | Low-Br 2 | Rel. therm. load
Test [1] as reference | 18 (2,7 Hz) | 0 | 0 | 1
Test 0-10 V @ 5 Hz | 10 (5 Hz) | 0 | 0 | 5,15
Scenario 1: High-Br | 10 (5 Hz) | 1 | 10 (5 Hz) | 2,2
Scenario 2: FAIR | 20 (2,5 Hz) | 1 | 4 (12,5 Hz) | 1,5xx
Scenario 3: GSI 1. Nacht | 50 (1 Hz) | 1 | 3 (16,7 Hz) | 1,5xx
Scenario 4: Nieder-Br 1 | 0 | 1 | 5 (10 Hz) | 1,2
Scenario 4a: Nieder-Br 2 | 0 | 1 | 3 (17 Hz) | 2,0