## Slide 1
Suggestion of a first Prototyp of the Central Space Frame

## Slide 2
Contents:
1. Requirements
2. Material
3. Design
4. Conclusion

## Slide 3
Requirements:
CSF has to carry the STT, the MVD and possibly the DCDC and the GBT electronics
Electronic: ~180kg in its center of gravity 1506 mm upstream from the interaction point
STT: ~80kg
MVD: ~30kg
CSF has to fix the target pipe and the target cross
The volume of material has to be preferably low
The material of the frame should have a low density and a low nuclear charge number
1. Requirements

## Slide 4
Because of coast reasons and to be more flexible, for a first prototype we choose Aluminum instead of the carbon composite
material | Titan | Aluminum | CFRP (carbon composite)
density | 4,5 g/cm³ | 2,7 g/cm³ | ~1,6 g/cm³
nuclear charge number | 22 | 13 | 6*
young‘s modulus | 105 GPa | 70 GPa | ≥ 125 GPa
2. Material comparision

## Slide 5
the mainframe is made out of four main parts and six connectors.
4. Extended design
main part 1
main part 2
main part 3
main part 4

## Slide 6
the mainframe is made out of four main parts and six connectors.
4. Extended design
main part 1
main part 2
main part 4
main part 3
connector 1
connector 1
connector 2

## Slide 7
the mainframe is made out of four main parts and six connectors.
4. Extended design
main part 1
main part 2
main part 3
main part 4
connector 1
connector 1
connector 2

## Slide 8
the support structure is also made out of several parts.
- two ribs which are connected to a tube via screws
- two flanges with a wedge shaped geometry for fixing the target pipe
- two straps to connect the tube and the flanges
4. Extended design
rib 1
rib 2
tube
strap
strap
flange
flange

## Slide 9
The two identical support structures will be attached to the mainframe via screws
4. Extended design
Support structure
Support structure
mainframe

## Slide 10
In combination, the three components close the force flow and build a stiff and stable assembly.
4. Extended design
Support structure
mainframe