## Slide 1: MVD Small Silicon Strip Disks
15.2.2018 Tobias Stockmanns

## Slide 2: Assumptions
No new sensor design:
  Wedge Sensor
    34.59/19.94 x 55.67 mm^2 // 36.87/21.69 x 57.67 mm^2
  Barrel Sensors
    S1: 58.275 x 33.315 mm^2 // 60.275 x 35.315 mm^2
    S2: 33.315 x 33.315 mm^2 // 35.315 x 35.315 mm^2
Within the boundaries of the existing disks
  Inner radius 22 mm
  Outer radius 267 mm

## Slide 3: Wedge Sensors
Does not work:
Large holes
Electronic has to be tilted
Sensor
Support

## Slide 4: Barrel Sensors
Where to put the electronics?
Sensor
Support
Sensor
Support
Sensor
Support
Sensor
Sensor
Front Side Electronics
Back Side Electronics
MCC
35 mm
20 mm
35 mm
60 mm
Sensor
Support

## Slide 5: Disk Layout

## Slide 6: Disk Layout

## Slide 7: Disk Layout

## Slide 8: Disk Layout
Sensor
Sensor
Support

## Slide 9: Requirements
2 Disks with:
  8 large modules:
    1 sensor 60 x 35 mm^2
    11 TOAST
    1-2 module controller
  8 square modules:
    1 sensor 35 x 35 mm^2
    8 TOAST
    1-2 module controller
Support structures with cooling
Holding structures
Total:
  16 large sensors
  16 small sensors
  304 TOAST
  32-64 module controller

## Slide 10: Summary
Building the forward disks based on barrel sensors seems possible
Advantage:
  Same sensor technology than barrel
  No big holes in the inner part of the disks
  No bending of electronics necessary
Disadvantage:
  Holes at larger radii
  Overlapping of electronics and sensors (problem for cooling?)