## Slide 1: CBM Iron yoke and support design
11 2019, BINP, M.Kholopov, A.Bragin, S. Pivovarov.

## Slide 2: FAIR

## Slide 3: 3D Model of CBM Magnet and cryosystem
Support (m= 4480 kg)
Coil (m=1479kg)
Feed Box (m=1160kg, D=1100mm, H=2370mm)
He transfer
Line (30kg*m)
Branch Box (m=1560kg, D=1100mm, H=2680mm)
Cryostat,
TL, magnets (m=7850kg)
Iron Yoke (m=145412kg)

## Slide 4: 3D Model of CBM Magnet (new design)
Support m= 4480 kg
Iron Yoke m=145412kg
Coils m=3100kg
Cryostat m=940kg
Cryostats TL m=710kg
The support’s load – 154 tons
1
2
5
4
3

## Slide 5: Iron Yoke and supports drawing
m= 150000 kg
L=4620mm
W=2380mm
H=4550mm
Weight and size

## Slide 6: Iron Yoke 3D Model
Mounting bracket
Geodetic platform
Geodetic holes
Top beam
13551 kg
Rack
10335 kg
Pole
3967 kg
Screen
2214 kg
Central beam
13594 kg

## Slide 7: Iron Yoke and supports drawing
-m= 145412 kg
-L=4440mm
-W=2380mm
-H=3700mm
Weight and size

## Slide 8: Iron Yoke production drawing
Drawings are processed in technologists and prepared for translation.

## Slide 9: Iron Yoke production drawing
An example of the implementation of the yoke of sheet material.
Top beam

## Slide 10: Iron Yoke production drawing
An example of the implementation of the yoke of sheet material.
Detail - Top Beam to the machining, allowance for processing 10 mm.

## Slide 11: Iron Yoke production drawing
An example of the implementation of the yoke of sheet material.
Cutting the blanks from a sheet
First step
Second step
End chamfer cutting
Cutting chamfers for welding
Third step
Sheet

## Slide 12: CBM Magnet support
m= 4480 kg
2022x3470x850mm
move in 3D ±40mm
Rotation top frame ±4⁰
Loading capacity 200000 kg
strength class of fasteners - 8.8
Top frame
Gimbal longitudinal
Screw jack Rack
Cross gimbal
Intermediate frame
Sliding support
Magnet supports alignment tools
Weight and size
Swivel bearing
Iron yoke
Fixation plate
- Position accuracy: ± 0.5 mm (meeting in December 2018)
- Orientation accuracy (roll): ± 0.5 mrad
-Also, this design allows rotation around vertical axis ± 0.5 ⁰
-The gimbals has a fixation and alignment tool

## Slide 13: Magnet supports drawing

## Slide 14: Bottom supports drawing

## Slide 15: Intermediate frame drawing

## Slide 16: Top frame drawing

## Slide 17
PTFE bearings are maintenance-free, this also applies to lubricated PTFE bearings;
Very Low Friction Constant
For the sake of simplicity, the following friction constants may be assumed under optimum installation conditions:
PTFE bearing, not lubricated about max. μ = 0.1
PTFE bearing, lubricated about max. μ = 0.04
The PTFE slidingplates are absolutely corrosion resistant, re-sistant against chemicals and aging. The steel parts of the bearings are by standard sandblasted and provided with a zinc phosphate coating. Upon request, all usual corrosion protection processes are of-fered, including hot galvanizing. Versions made of special steel alloys or stainless steel on request
PTFE plate can be replaced with radiation resistant material. For example bronze with lubrication.

## Slide 18: Fastener strength tablet
Work load,
kg
Work load,
kg
Work load,
kg
Work load,
kg
MAX load,
N
MAX load,
N
MAX load,
N
MAX load,
N
Thread
class of fasteners

## Slide 19: Screw jack Rack : design and calculation
Screw jack
Osaka Jack Co JJ10011
loading capacity 1000kN
2767 kg
Spherical bearings
(GX120FDIN ISO12240-2) loading capacity 1430kN
375 kN
Stress
200 kN (seismic load - 12%m)
G
Deformation
Margin
The bottom support is designed for a load of 200 tons and additionally added seismic hazar (20 tons)
Bottom support
1515 kg

## Slide 20: Screw jack Rack : design and calculation
750 kN
Stress
G
Margin
The bottom support is designed for a load of 200 tons and additionally added seismic hazar (20 tons)
200 kN (seismic load - 12%m)

## Slide 21: Intermediate frame : design and calculation
644 kg
Stress
200 kN (seismic load - 12%m)
G
Deformation
Margin
opening limits the movement of the Top frame
The intermediate frame is designed for seismic load which acts from the gimbal longitudinal (20 tons)

## Slide 22: Top frame : design and calculation
744 kg
Stress
200 kN (seismic load - 12%m)
G
Deformation
Margin
Box limiting the movement of the Top frame in the opening of the Intermediate frame
The top frame is designed for seismic load which acts from the gimbal longitudinal (20 tons)

## Slide 23: Gimbals : design and calculation
Stress
200 kN (seismic load - 12%m)
G
Deformation
Margin
swivel head
support plug
traction axle
locknut
workload : 50kN
design load: 200kN
Swivel bearing

## Slide 24: Calculation of studs for Pole CBM magnet
1500000N
Stress
Deformation
3000000N
Stress
Deformation
Margin
Margin

## Slide 25: Calculation of Pole & crossbar CBM magnet
3000000N
Stress
Deformation
Margin
Имя | Low carbon steel | 
General | Mass density | 7.86 г/см^3
 | Yield strength | 207 MПа
 | Ultimate tensile strength | 345 MПа
stress | young modulus | 220 ГПа
 | poisson ratio | 0.275 бр
 | Shear modulus of elasticity | 86.2745 ГПа

## Slide 26: Thank you for your attention!