## Slide 1: Oleksiy Dolinskyy 28th May, 2020
Antiproton yield in chain
of the “target +separator + CR

## Slide 2: Antiproton yield, r
Nproton - number of protons coming from SIS100 : (1-2)x1013
Npbar - required number of antiprotons, which is extracted to HESR: 108
The goal value: r ≥ 10-5
What is the predicted value r having the present design of antiproton target station, antiproton separator, injection line and CR ring.

## Slide 3: Considered chain
Particle tracking by 3 steps:
1. separator including septa
2. injection line
3. CR ring

## Slide 4
pbar distribution after horn lenz
First quadrupole
target
horn
Protons from SIS100
antiprotons
Ti window
inside: Ni rod (r = 15 mm, L = 10 cm) within graphite cylinder (r = 1 cm)
20 mrad < q < 80 mrad can be collected
I = 400 kA
Distance target center - lens: 220 mm
more simple and reliable, less expensive
The particle distribution after horn lens was calculated
by K.Knie considering the target system:

## Slide 5: After Horn
Klaus Knie simulations:
109 number of protons before the target
2.95x105 number of anti-protons after the horn-lens
acceptance of the antiproton separator
240 mm mrad 1.98x104 inside acceptance with dp/p=+-3%
93% pbars out
of acceptance
7 % pbar
captured in
acceptance
r=2 x 10-5

## Slide 6: Antiproton separator
1. Horizontal and vertical collimation
2. Momentum collimation
3. Chromatic effect of magnets
4. Non-linear field errors
5. Orbit destortion up to 4 mm.
6. Apertute of magnet.
End of septum
End of Horn.lenz

## Slide 7
1 st step of Particle tracking p-bar separator
Horizontal and vertical emittances: 240 mm mrad
The particle tracking from the horn-lens to the end of the CR septum
At the end of CR septum
horizontal plane
vertical plane
Hor. collimators
Ver. collimators
Mom. collimator
r=1.6 x 10-5
Sextupole magnets
are included

## Slide 8: particle tracking in the injection region
Injection region in the CR
r=1.6 x 10-5

## Slide 9
3D Field map of kicker magnets
Q04
end of septum magnet
- 3D field map of Kicker magnets
are included in simulations.
chromatic effect is on
- The real aperture of all quadrupoles
and other elements are included as given in TDR
(the first two quads as well)
The super-elliptical shape of
vacuum chambers are considered.
Particle tracking in injection line

## Slide 10: Magnet Field of the 3 modules
The magnet field over the length of 2.135 m, 3 modules
Lmax=2.135 m
BR=13 Tm
By from 3D field map
(Marc Petryk calculations)
The required kick angle x‘ is 5 mrad for all three modules, which means (BL)eff=65 mTm
Presently (see figure) we have (BL)eff=92 mTm, which gives x‘=7.07 mrad.

## Slide 11
Number of particles
N=1.7 x 104 (no losses)
BINP optics
GSI optics
Number of particles N=1.6 x 104 (no losses)
phase space at the middle of Q04
2nd step of particle tracking Injection line

## Slide 12
Particle tracking at ring
real apertures of all
CR systems and magnets
are included taking into
account their shape of
vacuum champers.
The RF cavities and CCC
are ‚bottleneck‘, where the
aperture is 70 mm.
1000 turns is calculated (time needed for bunch rotation)

## Slide 13
Particle tracking in the CR
Particle tracking at CR (1000 turns)
rpbar = 1.328 x 10-5
18 % of losses

## Slide 14: Antiproton yield
Antiproton production yield
(1.2 – 1.3) x 10-5
One can see that we have about 20 – 30 % margin.
- Real closed orbit distortions.
- RF de-bunching and re-bunching efficiency
- SC cooling performance in reality
- Real field quality of magnets in CR
Extraction efficiency
The acceptable theoretical particle losses should not exceed 1-3% in the
septum magnet only due to field error.
The real production yield depends on several factors, which are not possible
theoretically to predict :

## Slide 15: Next steps
My proposal is following:
The updated optics of the separator should be used to study the injection
efficiency into CR taking into account following :
The 3D field map of the septum magnet. The map exists and now under
implementation into particle tracking code.
The sextupole correction in the separator must be included. It can help
to compensate the chromatic effects of quadrupole (which means to reduce
the losses due to mismatching)
The 3D field map of inj. kicker calculated by BINP should be used to calculate
the antiproton transmission from separator to the CR.
Particle tracking in the CR taking into account
Stochastic cooling effect (acceptance). Time domain code is under development.
RF bunch rotation and re-bunching process
Measured field quality of magnets.
Closed orbit distortion (depends on alignment of magnets, quality of correctors
and BPM). This is most unpredictable effect.