## Slide 1: Landau damping in longitudinal plane for single or multi-bunch beams
E. Shaposhnikova, T. Argyropoulos, I. Karpov (CERN)
23.06.2020
Thanks to A. Burov, T. Bohl, H. Damerau, J. E. Muller, J. Repond, M. Schwarz
ARIES Workshop on Mitigations Approaches for Hadron Storage Rings and Synchrotrons

## Slide 2: Outline
Introduction
Single bunch
  Loss of Landau Damping in LHC
  Sacherer and Hofmann-Pedersen approaches
  Van-Kampen modes and Lebedev’ equation
Landau damping in a double RF system
Multi-bunch beam
  Stability diagrams in single and double RF
  Bunch-by-bunch Landau damping
Summary

## Slide 3: Introduction
Landau damping is a natural mitigation mechanism for beam instabilities
Landau damping is lost when coherent bunch frequency moves outside incoherent frequency band modified by beam-induced voltage
In longitudinal plane, Landau damping of coherent modes is achieved by synchrotron frequency spread ∆ωs, which can be increased by
  increasing filling of the RF bucket
  → minimum RF voltage for a given emittance (limited by particle losses),
  increasing longitudinal emittance
    → controlled emittance blow-up (limited by available RF voltage),
  applying a higher harmonic RF system (in active or passive mode)
Active damping by feedback is needed if these methods are not possible or sufficient

## Slide 4: Mitigation of longitudinal instabilities in CERN synchrotrons
Impedance budget control (LHC, …) and reduction programs (SPS, …)
Increasing synchrotron frequency spread by
  controlled emittance blow-up (PSB, PS, SPS, LHC):
    using a high harmonic RF system (PS) or band-limited noise
  multi-harmonic RF systems:
    SPS (and PSB)
    tested recently in the PS
    considered for HL-LHC
Active damping system in longitudinal plane exists only in PS (dipole mode, upgrade to quadrupole ongoing). In all machines: feedbacks for impedance reduction around fundamental RF frequency (beam-loading + instabilities)

## Slide 5: Longitudinal beam stability in LHC
Beam 1: controlled blow-up: τ = const
Beam 2: emittance blow-up didn’t work
→ instability during acceleration ramp
ramp
Measured average bunch length during cycle
LHC Design Report: nominal intensity N = 1.0x1011 p/b
From the criterion (F. Sacherer, 1973)
δωc < ∆ωs /4
  with ImZ/n = 0.28 Ohm, 4σ =1 ns, V=16 MV at 7 TeV: Nth = 2.4x1011 → natural Landau damping is sufficient,
  no dedicated wide-band feedback (D. Boussard et al, 1999, “Is a longitudinal feedback system required for LHC?”)
To avoid LLD during ramp → emittance ε ~ E1/2 or
Much lower LLD threshold was measured: Nth = 2.0x1011 for 4σ =1 ns, V=16 MV (scaled to 7 TeV) and ~3 times smaller ImZ/n = 0.09 Ohm
→ τ = const
since

## Slide 6: Landau damping in LHC
Similar simulation results for full impedance model (N. Mounet, 2015) and ImZ/n = 0.09 Ohm
BLonD simulations using full impedance model and bunches with μ = 2 agree with measurements
(PhD thesis J. E. Muller, 2016)
LHC impedance model
Measured & simulated
LHC threshold intensity
Nth ~ ε5/2
Measured bunch profiles and their fit with μ = 2
12 MV
450 GeV
6.5 TeV

## Slide 7: Landau damping in LHC
→ Expected scaling with energy, voltage and bunch length (small range) works in LHC with
ξth = (5.0±0.5)10-5 (ns)5V
on flat bottom, flat top and during cycle
Measurements in LHC
= ξ
ε ~ E1/2
(PhD thesis J. E. Muller, 2016)
What about absolute values for the threshold?

## Slide 8: Longitudinal beam stability in the CERN SPS
Sacherer’ criterion for ImZ/n = const
predicts a factor 10 higher impedance threshold at injection (26 GeV/c, 2 MV) than on flat top (450 GeV/c)
Measurements: similar thresholds ~1x1011
Good agreement between measurements and simulations (with rotated PS bunches and full SPS impedance model).
Cycle time [s]
Measurements: single bunch during cycle in a single RF system
Calculations
→ Voltage reduction stabilizes the beam
→ Bunch with smaller emittance becomes unstable later in the cycle

## Slide 9: Sacherer formalism (1/2)
General matrix equation (F. Sacherer, 1971) was derived from linearised Vlasov equation.
Dispersion equation was obtained for “synthetic kernel” assuming a rigid bunch motion
and Ꜫ =
Coherent frequency shifts δωc,m are calculated from general matrix equation for spread ∆ωs = 0 and effective impedance Zeff
where
Stability diagrams for binomial particle distribution functions
  → No LD with μ ≤ 1 for η ImZ/n < 0 (space charge above transition)

## Slide 10: Sacherer formalism (2/2)
Criterion for the loss of Landau damping was found for a parabolic bunch (μ = 0.5)
From stability diagram for μ = 0.5 and dipole mode (m=1) → [δωc/ ∆ωs]stab = 2/3
The popular criterion δωc < ∆ωs /4 is obtained when the stability limit for μ = 2 (“smooth” distribution) is replaced by a semi-circle with radius [δωc/ ∆ωs]stab = 0.25
Analytical solutions for ∆ωc exist for some distribution functions (Gaussian, binominal with μ = 0, 0.5, 1) → consistent approach only when used together with the exact [δωc/ ∆ωs]stab. Difficulties due to necessity to include the incoherent frequency shift.

## Slide 11: Hofmann-Pedersen formalism
Self-consistent analytical solution for ωsc and ∆ωs for μ = 0.5 and ImZ/n=const
  rigid bunch motion (also)
  coherent frequency calculation: spread ∆ωs is included
  → non-zero threshold for η ImZ/n <0
Threshold for loss of LD
with F = π4/30 for short bunches is ~ 30% higher than F = π2/4 from Sacherer criterion for m=1 and μ = 0.5 since [δωc/ ∆ωs]stab = 2/3

## Slide 12: Comparison of loss of LD thresholds for LHC
Expected from Sacherer’ criterion scaling with energy, voltage and bunch length seems to work, but
→ The thresholds predicted from Sacherer’ stability diagrams and Hofmann-Pedersen approach are 3 – 4 times higher than measured and simulated thresholds.
The discrepancy cannot be explained either by
by different particle distribution: thresholds for different distributions are similar for the same FWHM bunch length
by “missing “ impedance due to good agreement between measurements and simulations
→ More accurate methods should be used based on Van Kampen Modes (A. Burov, 2010) or Lebedev equation

## Slide 13: Landau damping: Van-Kampen modes
More accurate method (A. Burov, 2010): find Van-Kampen modes solving Vlasov equation for a perturbation of a stationary distribution expanded as (Oide & Yokoya, 1990)
Substitution into linearised Vlasov equation gives the following equation
(which is then transformed into matrix equation by replacing integration over Ꜫ by a sum)
where
Continuous spectrum - singular modes from incoherent band. Discrete modes - coherent solutions described by regular eigenfunctions → their existence outside incoherent band serve as criterion for loss of LD

## Slide 14: Lebedev equation
Matrix equation (A. N. Lebedev, 1967) in variables with
where and normalisation
Finally,
where is a solution of equation
where
Affects stability in double RF system!

## Slide 15: Sacherer dispersion equation as a low-frequency limit
In a single RF, for short bunches
For Bessel function Jm can be replaced by
or
Then, for uncoupled modes m, eigenfunction Is solution of
Lebedev’ equation for mode m → Sacherer’ stability diagram with synthetic kernel used for m > 0
This equation is valid for low frequency impedances with f < 1/(π𝜏) (𝜏 - bunch length)
The “effective” impedance doesn’t converge for ImZ/n=const
with effective impedance

## Slide 16: Van-Kampen modes vs Lebedev equation
Loss of Landau damping in LHC: comparison of calculations and measurements
Solution for ImZ/n = const does not converge → physical impedance model should be used.
The results depend on cut-off frequency for ImZ/n = const or resonant frequency of the broad-band impedance model → study ongoing
Good agreement with measurements for μ=2 and b-b impedance: fr = 5 GHz, Q = 1, ImZ/n = 0.076 Ohm, fcut = 20 GHz
→ For HL-LHC nominal bunch length was increased to 1.2 ns
→ Code MELODY (I. Karpov, 2019) solving numerically Lebedev equation gives the same thresholds as from Van-Kampen modes
A. N. Lebedev
N. G. van Kampen
In this case the effect of potential well distortion is < 10%

## Slide 17: Landau damping in a double RF system
Synchrotron frequency distribution
400
Total voltage in a double RF system:
V = V1sinφ +V2 sin(nφ + Φ2) (nV2/V1 < 1)
Maximum change in ωs(0) for Φ2 = φ2 – n φs
Above transition:
φ2 = 0 - BLM (Bunch-Lengthening Mode)
φ2 = π - BSM (Bunch-Shortening Mode)
BLM: “flat” bunches, increased bucket, larger spread for V1/V2 = n, but region with ω’s(Ꜫ) = 0 exists for any V2 /V1 (V. Balbekov, S. Ivanov, 1987) + high sensitivity to error in Φ2
→ only BSM works for LHC beam in the CERN SPS (n=4), and in PS (H. Damerau et al.)
Lower is n, point ω’s(Ꜫ) = 0 is further away from bunch center
→ For short bunches, ∆ωs is significantly increased
(by ~ 10/φb2) with optimum n ~ 5/φb (φb = hω0𝜏/2)
400 MHz RF

## Slide 18: Double RF system: single bunch stability
Thresholds from Van-Kampen modes
and simulations for ImZ/n = const
(inductive impedance above transition)
In simulations the criterion for LLD needs to be chosen (0.8)
Oscillation amplitude normalised to the kick amplitude
→ For n=2, long bunches are more stable in BSM.
Different behaviour below transition (simulations O. Boine - Frankenheim, T. Shukla, PRST AB, 2005)?

## Slide 19: Landau damping in BS-mode for n > 2
BS-mode with n=4 and V2/V1=n,
V1=0.6 MV @100 MHz , SPS @26 GeV/c
Threshold from particle simulations
(T. Argyropoulos, PhD thesis, 2015)
Synchrotron frequency distribution
in BS-mode for various n
→ Flat portion in ω’s(J) appears for n>2
Stability in BSM can be improved by phase shift, also in BLM (T. Argyropoulos, A. Burov, E.S., IPAC’12)

## Slide 20: Landau damping for multi-bunch beam
Stability diagram for
For narrow band impedance with ωr, only one resonant harmonic kr = ωr /ω0 = lM + n can be kept (M - number of equidistant bunches) in Lebedev equation:
stable
unstable
From stability diagram
(V. Balbekov, S. Ivanov, 1987):
with
→ Beam is stable if vertical line 1/Rsh is inside stability region
and

## Slide 21: Landau damping for multi-bunch beam: stability diagrams in single and double RF
μ= 2: Rth in double RF system (BLM) is higher than in single RF
Note that many modes m are excited simultaneously in the BL-mode (not in BS-mode) since
μ= 1: Rth in double RF system is decreasing with emittance
Stability diagrams (m=1) for μ = 1 and 2 in 1RF & 2RF (BLM) for various φmax
The instability threshold
→ Strong dependence on ω’s/F’
Distributions with non-zero function F’
at the edge are more unstable (μ < 1)

## Slide 22: Multi-bunch threshold
Only the FWHM bunch length is important
Lebedev matrix equation allows analysis of beam stability with both narrow and broad-band impedances.
In single RF system the threshold (no acceleration)
Threshold Rsh for coupled-bunch instabilities in FCC-hh at 50 TeV for nominal intensity Nb=1011, V = 38 MV, γt =99.3 (I. Karpov, E.S., IPAC’19)
where

## Slide 23: Stabilisation of LHC proton beam in CERN SPS
Bunch intensity should be doubled after RF upgrade, HOM damping and impedance reduction
The LHC beam in SPS is stabilised by the 4th harmonic RF system (~ factor 4 in threshold). → Extra stability margin by optimising the 800 MHz voltage program (V4 /V1 = 0.1 used before)
V800 = 0.15 V200
Optimum V800/V200
ratio during SPS cycle
Increasing V800 improves stability, …
→ higher bunch intensities were stabilized and injected into LHC
but only towards the end of the ramp
SPS @450 GeV

## Slide 24: Intensity effects and controlled emittance blow-up in a double RF
Strong beam loading in main SPS RF system (even with OTFB) shifts a relative phase between 2 RF systems (200 & 800 MHz) and bunch positions
  Synchrotron frequency spread and Landau damping is varying from bunch-to-bunch
  Optimum noise frequency band is different for each bunch…
bunch position
bunch number:
k=1
k=36
k=72
Potential well distortion also shifts incoherent frequency band ~ N/𝜏3
- initial
- after BUP
- at flat top
bunch length

## Slide 25: Damping of coupled-bunch instability with higher harmonic RF system in CERN PS
10 & 40 MHz in BL-mode
10 & 40 MHz in BS-mode
First successful tests at flat top energy in CERN PS, (H. Damerau et al., 2017)
Bunch mode spectrum

## Slide 26: Bunch-by-bunch synchrotron frequency spread
Coupled-bunch instability can also be stabilisied by bunch-by-bunch spread ∆ωs > shift ∆ωc:
spread in bunch population
{∆N/N}rms > Im{∆ωc}/Re{∆ωc}
low-frequency voltage-modulation
ωs0 ~ V1/2
from RF cavities at (h+1) or residual beam loading (from fractional ring filling) – ESRF storage ring (O. Naumann, J. Jacob, 1997)
CERN SPS simulations: LHC beam is globally more stable with fundamental impedance reduced (by feedback) than removed (J. Repond, M. Schwarz)
SPS, Q26, Nb = 3x1010 ppb, 16% RF AM
E. Vogel, T. Bohl and U. Wehrle, PRST 8 (2005)
Effect of main RF Amplitude Modulation

## Slide 27
Thresholds for different feedback models
1x72 bunches, V200/V800 = 10MV/1MV, Q20, full SPS impedance model
Model feedback of 200 MHz by
  Reduction of Rshunt by 26dB (continuous)
  Impedance reduction factor (data points)
  No 200 MHz TWC (dashed)
Reducing the shunt impedance yields similar threshold as without the 200 MHz TWCs
No threshold was found when using the impedance reduction factor , even though it has more ‘residual’ impedance around 200 MHz
M. Schwarz, 2019

## Slide 28: Summary
Sacherer stability diagrams in longitudinal plane are justified only for low-frequency impedance and in other cases should be used with caution.
More complete formalisms (Van-Kampen modes and Lebedev equation) together with particle simulations are available for accurate threshold estimations, which should be based on realistic impedance model.
Dependence of intensity thresholds on particle distribution can be reduced by using the FWHM bunch lengths.
Landau damping can be significantly increased by additional, higher harmonic RF system, but its limitations in BLM and, for n > 2, in BSM should be taken into account for the choice of the beam and RF parameters.
Main mitigation measures used at CERN against loss of Landau damping and instabilities in longitudinal plane are controlled longitudinal emittance blow-up and high harmonic (Landau) cavity (in addition to FB around main impedance)

## Slide 29: Spare slides

## Slide 30: Thresholds for different distribution functions
Distribution function
Again full-width half-maximum bunch length is a good parameter for stability evaluation
The same full-width half-maximum bunch length
I. Karpov

## Slide 31: Threshold of loss of Landau damping for different particle distributions
Threshold of LLD for different particle distributions with 0.8 ns FWHM @4.0 TeV
Threshold of LLD for different particle distributions with 1 eVs emittance @4.0 TeV
J. E. Muller

## Slide 32: Synchrotron frequency distribution and phase between 2 RF systems in BS-mode
Very good agreement between measurements and simulations (with SPS impedance model):
single bunches are unstable in BS-mode with V2/V1=4
can be stabilised by significant phase shift of 800 MHz RF system
(T. Argyropoulos et al., IPAC’12)