## Slide 1
Chandra Bhat, Kiyomi Seiya and Jean-Francois Ostiguy
Fermilab, Batavia, Illinois, USA
W. Pellico
K.Y. Ng,
R. Ainsworth
S. Wolfram
M. Syphers
H. Damerau
“The Curse of Transition Crossing”
in Synchrotrons
“Mitigation Approaches for Hadron Storage Rings and Synchrotrons”
ARIES-APEC workshop,
Virtual Workshop, GSI: https://indico.gsi.de/event/10458/page/1098-scientific-program
22 June to 1 July 2020

## Slide 2: Outline
Fermilab’s important role in the history of transition crossing
High intensity beam issues at transition.
Mitigation options
Addressing transition issues in our synchrotrons during high intensity PIP-II era

## Slide 3
Fermilab Accelerator Complex & Experiments
Short Baseline Neutrino:
MicroBooNE, ANNIE, ICARUS (SBND)
Long Baseline Neutrino:
NOvA
Muon Campus:
g-2(Mu2e)
Switchyard:
SeaQuest, test beam
(SpinQuest)
8GeV
Slip Stacking
Rebunching
2nd Oldest
RCS in the World
 | Booster(RCS) | Main Injector
E (GeV) | 0.4-8 | 8-120
R(m) | 75.4 | 528.7
Beam Cycle | 15(Hz) | 1.2s
 | 5.47 | 21.65
Beam pipe radius (cm) | No beam pipe | 5.8
Z/n() | <40* | <10
 | Booster(RCS) | Main Injector
E (GeV) | 0.4-8 | 8-120
R(m) | 75.4 | 528.7
Beam Cycle | 15(Hz) | 1.2s
 | 5.47 | 21.65
Beam pipe radius (cm) | No beam pipe | 5.8
Z/n() | <40* | <10
Ion Source
RFQ
750keV
Booster
LINAC
400MeV
LINAC
400MeV
Main Injector
Long Baseline Neutrino:
(LBNF/DUNE)

## Slide 4: Fermilab’s Role in the History of Transition Crossing
“Longitudinal Space Charge Effects at Transition in NAL Booster and Main Ring”. E.D. Courant, FERMILAB-FN-0187,May 20, 1969,
-Jump Scheme: “Compensation of Space-charge Mismatch at Transition of Booster using the Transition-Jump Method”, L.C. Teng, FN-207 0400, (1970),
“Beam Bunch Length Matching at Transition Crossing with Space-Charge Forces”, W.W. Lee and L.C. Teng, PAC1971,
“Transition Jump system for the Fermilab Booster”, W. Merz, C. Ankenbrandt and K.Koepke, PAC1987,p 1343, (but removed in 2006)
Focus Free Transition Crossing: “Proposal for Experimental Test of RF Harmonic Transition Crossing in the Main Ring”, J.Griffin and C.M. Bhat, Fermilab Internal Note, MI-0062, (1991); “Transition crossing in proton synchrotrons using a flattened rf wave” C.M.Bhat, J.Griffin,et.al., Phys. Rev. E, Vol. 55, (1997), p.1028,
Imaginary -Lattice for Synchrotrons: “A Transition-less Lattice for the Fermilab Main Injector”, K.Y. Ng, D.Trbojevic and S. Y. Lee, PAC1991, p 159.
Thought about new ways of dealing with crossing

## Slide 5: Transition Crossing in a Synchrotron
Transition Energy and What is Transition Crossing?
  Particles with different momenta travel along different paths with a revolution period T=C/v
-
Why Transition Crossing is a Curse?
  Beam losses due to large dp/p at transition crossing  Increased beam loading, Space charge effects
  Non-adiabaticity around Transition Crossing Disappearance of phase focusing
  Johnsen’s effect/non-linear effects
  Microwave instability
  Negative Mass instability
  Umstatter’s Effect
  Lattice Issues, Chomaticity-Jump
  And Many more ….
Momentum Compaction factor
Phase-slip factor
Transition 
In reality the phase jump is not symmetric

## Slide 6: Beam Losses due to Large dp/p during Transition Crossing
During
Transition
Crossing
One can expect beam loss if momentum spread of the beam exceeds momentum acceptance of the machine.
Example:
Fermilab Main Ring
Chart: Bucket height and Synchrotron frequency in the Booster
dE

## Slide 7: Non-adiabatic and Non-linear Effects in Synchrotrons
Non-adiabatic Time: During transition the synchrotron oscillations of the beam particles are FROZEN for a time intervaland the longitudinal motion of the particle becomes non-adiabatic,
Johnsen-Effect: Emittance growth due to chromatic non-linearities arising from different particles in a bunch crossing transition at different times. Then the total non-linear time is,
h is harmonic number,
are relativistic quantities at transition,
is angular velocity of the synchronous particle,
is the rate of change of at transition
is synchronous phase angle of the bunch
and
=
 | FNAL Booster (PIP/PIPII) | FNAL MI | BNL AGS | BNL RHIC | KEKPS | CERN PS
(s-1) | 391(15Hz)/489(20Hz) | 267 | 70 | 1.6 | 40 | 60
 | 0.213/0.20 | 1.8 | 2.5 | 36 | 1.8 | 1.5
 | 0.073/0.08 | 0.2 | 0.6 | 63 | 0.7 | 0.5
 | FNAL Booster (PIP/PIPII) | FNAL MI | BNL AGS | BNL RHIC | KEKPS | CERN PS
 | 391(15Hz)/489(20Hz) | 267 | 70 | 1.6 | 40 | 60
 | 0.213/0.20 | 1.8 | 2.5 | 36 | 1.8 | 1.5
 | 0.073/0.08 | 0.2 | 0.6 | 63 | 0.7 | 0.5
During this time the particles with high and low momenta follow hyperbolic divergent paths.

## Slide 8: Microwave Single Bunch Instability
Generally Microwave single bunch instability is handled using Keil-Schnell -Boussard Criteria for a bunched beam,
SYLee, JWei, LCTeng, JMWang: At a capacitive (, an inductive) longitudinal coupling impedance Z|| at a “broad-band” frequency will cause a Microwave Instability, if
Because of a small synchrotron frequency spread in this region, Landau damping for microwave single bunch instability vanishes Keil-Schnell criteria unsuitable
VRF is Accelerating RF voltage at Transition Energy

## Slide 9: Microwave Single Bunch Instability Limit for Fermilab Booster
Longitudinal Impedance
Measurements: J Crisp,Fermilab-TM-2145, (2001)
Total Longitudinal Impedance
Model: V. Lebedev, BD5146(2016)
Z||/n=40 

## Slide 10: Negative Mass instability
Particles with v c can not travel much faster on acceleration but gain momentum and move in orbits of larger radii. Above transition energy, particles that normally repel each other appear to experience an attractive force; this leads to an instability.
  According to W. Hardt (Int-Conf-on-HEAccels-Stanford-1974) and K.Ng (FNAL,1994) the net emittance growth resulting from transition crossing is characterized by a critical parameter,
If “CP” <1 No blowup due to Negative mass Instability
is classical radius of the proton, R is radius of the synchrotron.
is number of protons per bunch, A= Beam 95% beam emittance
, =4.3494, a numerical constant
KYNg,FERMILAB-Conf-94/25

## Slide 11: Microwave and Negative Mass Instability Limits in the FNAL Main Injector
L=0.11 eVs
L=0.16 eVs
L=0.24 eVs
Current emittance
1.2MW-Beam
700kW Beam
=21.66
CBhat, MI Note 0218, 1997

## Slide 12: Umstatter’s Effect
The transverse space-charge force changes the tune of each individual particle, making dependent on the azimuthal beam density. Then
is linear density at the center of the bunch and
are transverse beam half width and half height, respectively,
is electrostatic image coefficient (Laslett),
Consequently some particles at the center of the bunch will cross transition earlier than synchronous particles by for Fermilab Main Injector.
This is much smaller than - non-adiabatic time. So, Umstatter effect is negligible.

## Slide 13: Mitigation Techniques
Jump scheme
Focus free transition crossing (using harmonic cavities, broad-band RF cavities in induction accelerators)
RF Duck-Under  is done almost at every synchrotron
RF triple jump and other phase jump Techniques
Avoiding
  Operate the synchrotrons well above the
  Imaginary Lattice: Total avoidance of transition energy, (issues with imaginary lattice)
  L. Teng infinite
No major lattice change, but, needs good LLRF control

## Slide 14: -Jump scheme
-Jump scheme is a way of crossing transition fast enough to avoid all of the issues mentioned earlier.
  This is done by manipulating the focusing properties of the machine. A set of quadrupole magnets are pulsed rapidly to reduce transition crossing to a blip for a period of
Fermilab Booster
(1987-2006)
CERN PS (since 1969)
 | FNAL Booster | BNL AGS | BNL RHIC | CERN PS
& (t msec) | 1 (0.1ms) | 3.5 (2ms) | 1 (40ms) | 3 (0.4ms)
(s-1) | 391 | 70 | 1.6 | 60
 | 0.28 | 3.1 | 99 | 2
 | FNAL Booster | BNL AGS | BNL RHIC | CERN PS
 | 1 (0.1ms) | 3.5 (2ms) | 1 (40ms) | 3 (0.4ms)
 | 391 | 70 | 1.6 | 60
 | 0.28 | 3.1 | 99 | 2
t
t
t

## Slide 15: Focus Free Transition Crossing using RF cavities
2nd Harmonic
3rd Harmonic
ESME Simulations
for 2E10ppb (SC&Imp)
FFTC is an RF technique to accelerate beam across transition energy.
  The rf phase focusing vanishes around the transition energy for a period of resulting in growth of momentum spread. This can be controlled using a flattened rf wave that provides constant acceleration to all particles.
Bhat et. al.,Phys. Rev. E, Vol. 55

## Slide 16: Experiment in the Fermilab Main Ring
= 90, 5 ms, V3/V1 0.13, with V3 =270kV, fRF (h=1)  53MHz
This method is applied in the KEK Induction Accelerator to cross Transition
Simulations with and without higher-ordered terms in the slip factor 
 This mitigation technique has limitations
Things get Complicated
Phys. Rev. E, Vol. 55
159 MHz RF
cavity in
the Main Ring
NO FFTC
FFTC
Cavity from CERN
NO FFTC
FFTC
Meas. Data
Simulations

## Slide 17: Intensity Frontier Efforts at Fermilab

## Slide 18: Increasing beam power on 120 GeV neutrino target
PIP*
PIP-PIP II
PIP-II
Target | 700kW** | 900 kW | 1.2MW
Beam line | 1.3E17 pph (NuMI beam line) | 1.7E17 pph (NuMI beam line) | LBNF
Main Injector (MI)/ Recycler(RR) | 4.9E13 ppp 1.333 sec | 5.6E13 ppp 1.2 sec | 7.5E13 ppp 1.2sec
Booster | 4.3E12 ppp 15 Hz | 5.0E12 ppp 15Hz | 6.5E12 ppp 20Hz
LINAC | 25mA | 30mA | PIP-II SC LINAC
*Proton Improvement Plan: PIP
**Record power: 758kW in April, 2019
50% more beam from the Booster
70% increase in beam power from MI

## Slide 19: Transition Crossing in Booster (RCS) (history, current and future)
Addressing Transition Crossing in a RCS is not trivial.
Past
  Had -jump from 1987 -2006
    Had =1, change in 0.1 ms, cross transition ~25 times faster
    It didn't help as much as it hurt. Removed in 2006 (Newly developed longitudinal dampers and -Jump scheme could not co-exist.)
Current: Issues and Mitigation Techniques
  Beam Intensity: 4.3E12-5E12 ppp @Exit
  Standard Phase Jump (15Hz)
  Issue: Timing jitter (>40 sec)
  Mitigation
    Frequency based phase jump
    Longitudinal quad damper
With -Jump asymmetric
3 ms
1
t
Merz et.al., PAC1987,p1343

## Slide 20: High Intensity Booster Beam through Transition after implementing fRF based Transition Crossing
Without mode Damper
Inj. to Ext. Efficiency
91%
94%
95%
Mountain Range Plot
of 81 Bunches
at Extraction
Operational Intensity
With mode Damper

## Slide 21: High Intensity Booster Beam through Transition after fRF based Transition crossing (cont.)
ESME Simulations showed that the observed bunch length oscillations and emittance dilution are primarily due to bunch- to-bucket mismatch after Transition crossing.
Mitigation: LLRF will be improved to make an additional phase jump in addition to normal phase jump of - at transition energy.
(C. Drennan and B. Schupbach)
Current Mitigation Technique: Use of a quad damper
Data without Quad Damper

## Slide 22: Damping Coupled Bunch Mode-oscillations After Transition Crossing in Booster (Ongoing and Future Mitigation Plans)
PIP-II Requirements
  Beam Intensity: 6.5E12 ppp@Exit with L(95%)/bunch  0.1 eVs and (T (95%)16-mm-mr)
Standard Phase Jump (20Hz) – no other schemes are in baseline design
Ongoing and Future Upgrade Plans
  Quad Digital Damper- in progress
  Higher Ordered Mode Dampers: As a side effect of going through transition, bunches become very narrow. The enhanced higher harmonic contents of the beam drives higher order cavity modes- thereby coupled bunch beam modes are excited.
    Digital dampers – in progress
  Paraphase, RF phase calibration, Digital LLRF Upgrades -ongoing
  –in progress
  -jump using correctors
  triple phase jump,
  Combination of the above
  Lattice modification
Under Consideration

## Slide 23: Transition Crossing in the Main Injector (history, current and future)
Past
  -jump scheme (S. Holmes, S. Peggs, W. Chou,V. Visnjic)
  Focus free transition crossing (J. Griffin, C. Bhat, J. MacLachlan, K. Meisner and many)
  Transition Free lattice (K.Y. Ng, D.Trbojevic and S. Y. Lee,)
  Main Injector Intensity Limitations at Transition, (C. Bhat, MI Note 0218)
Current
  Standard Phase Jump; Beam Intensity 4.9E13-5.6e13ppp
    Our analysis and experience showed that for intensity ~5-6E13 p/486 bunches (L/bunch  0.2 eVs), transition crossing is not an issue.
  fRF based transition crossing since (2001), highly improved LLRF system
  Run with high chromaticity
  Digital wide-band longitudinal dampers (since 2006)
PIP-II Requirements
  Beam Intensity ~8E13 p/486 bunches with (L/bunch~0.8 eVs)
    Non-linear effects will become an issue
Future Plans
  -jump using dedicated pulsed magnets
Transition Crossing is an issue

## Slide 24: 6D Transition Crossing Simulations (including Space Charge effect using PIC code Synergia)
with -jump
no -jump
- jump will be installed for PIP-II operation.
Particle
Loss
Momentum spread
Horizontal beam size
Based on PAC1991, p1660
R. Ainsworth
(IPAC2017,p 3347)
Losses seen for the 0.75unit jump
as transverse not longitudinal
without - jump

## Slide 25: Summary and Conclusions
“Transition Energy has been both a nuisance in machine operation and a possible blessing… bunches with ultra-small beam width.” – S. Y. Lee
  In HEP hadron synchrotrons transition is more a NUISANCE than a Curse.
In this talk we addressed a number of issues one needs to worry about if beam has to go through transition energy.
Fermilab Current and Future Plans for Transition Crossing are discussed
  Booster
    It is unknown if Transition Crossing will be a problem since there is no “Reliable Modeling”. However, measurements in the Booster indicate that there may not be a problem for the designed that PIP-II intensity.
    Continue with standard RF phase jump with improved LLRF system
    Efforts are underway to identify issues
    Upgrade longitudinal quad dampers and coupled-mode dampers are in place
    Work in progress on -jump scheme using existing quad-correctors
  Main Injector
    Transition Crossing is going to be an issue for PIP-II Intensity
    Formal 1st order - jump will be installed for PIP-II operation