## Slide 1: Performance and Limits at CSNS
Sheng Wang
CSNS, IHEP Jun. 29, 2020
Mitigation approaches for Hadron storage rings and synchrotron

## Slide 2: Contents
1
2
Introduction to CSNS
Performance of CSNS
3
Beam commissioning and limits
4
Summary
5
Upgrade plan

## Slide 3: Site of CSNS
★
Dongguan branch Established on Feb. 19th 2013, to construct and manage the CSNS
Located in Dongguan, Guangdong Province

CSNS

## Slide 4: Key milestone of CSNS
4
Feb. 2001
Jan. 2006
Sep. 2008
Sep. 2011
Proposal for the CSNS Project
Prototyping R&D started
May 2012
Oct. 2014
Proposal approved
Jan. 2016
Apr. 2017
May. 2017
Aug. 2017
DTL-1 Beam commissioning
Linac beam commissioning
Mar. 2018
Mar. 2020
RCS commissioning start
Construction started
Civil construction started
100kW
Construction complete
(6.5 years from start)
First beam on target, first neutron beam

## Slide 5: CSNS Civil Engineering
    Linac service building
    RCS service building
    Target and experiment hall
    North experiment hall
    South experiment hall

## Slide 6
Linac tunnel
RCS tunnel

## Slide 7: CSNS Overview
1.6GeV, 25Hz
100kW
80MeV H- linac

## Slide 8: Front End and H- Linac
 | Ion Source | RFQ | DTL
Input Energy（MeV) |  | 0.05 | 3.0
Output Energy(MeV) | 0.05 | 3.0 | 80
Pulse Current (mA) | 20/40 | 15/30 | 15/30
RF frequency (MHz) |  | 324 | 324
Chop rate (%) |  | 50 | 50
Duty factor (%) | 1.3 | 1.05 | 1.05
Repetition rate (Hz) | 25 | 25 | 25
EMQ option in FFDD lattice for DTL
Electrostatic chopper in LEBT

## Slide 9: Rapid Cycling Synchrotron
Lattice of 4-fold symmetry, triplet.
227.92m circumference.
Four long straight sections for injection, acceleration, collimation and extraction.
24 main dipoles with one power supply.
48 main quadrupoles with 5 power supplies.
Ceramic vacuum chambers for the AC&pulsed magnets.
8 RF ferrite loaded cavities to provide 165 kV.

## Slide 10: First CSNS Neutron Beam
Aug. 28, 2017

## Slide 11
Commissioning plan
IS+LEBT | 2015.4.14 - 2015.4.14
RFQ+MEBT | 2015.4.15 - 2015.7.15
DTL1 | 2015.12.28 - 2016.2.26
DTL2-4+LRBT | 2016.11.20 - 2016.12.20
RCS+RTBT | 2016.12.25 - 2017.6.16
RTBT （on target) | 2017.6.17 - 2017.9.30
First neutron beam | 2017.9.30
10kW | 2017.9.30 - 2017.12.31
To acceptance goal | 2017.12.31
Official acceptance | 2018.3
100kW | 2018.3.1-2021.3.1
2016.1.9
2017.4.14–2017.4.24
2017.5.27–2017.8.27
2017.8.28
2017.8.28
2017.10.25- 2017.11.9
2017.11.9
2018.3
2020.6 100kW
Plan
Achieved

## Slide 12: Historical Curve of Beam Power
Nov., 2017, First 10kW beam strike on target for a short while;
Mar. 2018, beam power over 20 kW in the test operation;
Jan. 2019, after 4 weeks beam commissioning , beam power was gradually increased to 50kW+ with well controlled beam loss.
Sep. 2019, based on the 6 weeks beam commissioning, the beam power in user operation was increased to 80 kW step by step.
The beam power was increased to 100kW in the end of Feb. 2020.

## Slide 13: 24 hours beam operation (Mar.1,2020)

## Slide 14: Machine hours Statistics (2019)
14
~4500 hours was provided to users in operation of 2020
The availability is over 92% during the user operation

## Slide 15
Beam Commissioning and Limits

## Slide 16: Linac Commissioning
LRWS00
LRWS01
LRWS02
LRWS03
MEBT matching minimizing RMS beam sizes at the exit of the DTL
The stability of Ion source

## Slide 17
Tune Optimization
The tune variation during the beam acceleration process was well controlled
The design tunes (4.86 4.78) were adopted at low-intensity beam commissioning
Harmonic compensation on magnets was used for the tune optimization
Before harmonic compensation
Harmonic compensation

## Slide 18
The tunes at injection were set at (4.81, 4.87) to reduce space charge induced beam loss
The tunes were moved downward to suppress the beam instability
Tune Optimization
Tune optimization at high-intensity beam commissioning

## Slide 19
Anti-correlated painting scheme
The anti-correlated painting is design scheme
By using the anti-correlated painting, the beam power reached 50kW.

## Slide 20
Correlated painting scheme
Emittance growth,
beam loss during injection
Uncontrolled beam loss in acceleration
Distortion of extracted beam distribution
A new methods was proposed to perform the correlated painting under the anti-correlated

## Slide 21
Comparison between the correlated and anti-correlated paintings
By correlated painting:
Beam loss is well controlled
Beam distribution is much better

## Slide 22
Coherent oscillation study - measurement
A coherent oscillation appears at 2 ms for design mode of 86/78 when the beam power is bigger than 50 kW (7.8E12 ppp)
It depends on circulated beam power, horizontal tune and chromaticity.
The coherent oscillation mainly occurs in horizontal plane, but it also appears in vertical plane with special vertical tune and chromaticity.
The head-tail mode is also detected through BPM waveform
The beam spectrum is consistent of resistive wall impedance

## Slide 23
Coherent oscillation study - calculation
The high order headtail instability in RCS is calculated according to the Sacherer formula
The growth time is the function of tune and chromaticity

## Slide 24
Coherent oscillation study - simulation
The head-tail instability simulation code is developed
The coherent oscillation and head-tail mode are consistent with the measurement.
Simulation
Measurement

## Slide 25
Coherent oscillation study - taming
Depress the oscillation by optimizing the tunes and chromaticity
  The changing tune pattern is adopt
  The operation chromaticity is about -8/ -6.5 (with DC sextupoles)
The oscillation in RCS operation is depressed, but may appears again with much higher beam intensity
TBT orbit

## Slide 26: COD Correction (AC)
x-before
x-after
y-before
y-after
±15mm
±2mm
±10mm
±5mm

## Slide 27
Localizing beam loss
The beam transmission was about 99.5% without collimators.
The beam transmission was about 98.5% with collimators.
BLM signals along the RCS
Most of remaining beam loss is well localized at the collimator section;
The collimation efficiency was evaluated to be 95%~98%;

## Slide 28: Beam loss and control

## Slide 29
Pushing the limits
Install the Trim-Qs to shape the tune curves
Install the AC sextupoles to control the coherent oscillations
Re-install the injection components to realize the real correlated painting scheme
Re-sorting the dipoles according to the magnetic field measurement at AC mode

## Slide 30: CSNS Overview
1.6GeV,25Hz
80MeV H- linac
Reserved space for linac upgrade
SC Linac 300-350MeV
500kW
Dual harmonic RF cavity

## Slide 31: Summary
CSNS has been constructed on schedule.
The beam commissioning have been successfully done, reached design goal of 100kW beam power after two and half years beam commissioning.
Quickly open to users, and the availability is over 92%. Many excellent research results have been achieved.
Steps will be taken to push the limits.
Upgrading for high beam power will start in near future.

## Slide 32
Thank you !