## Slide 1: Mitigation strategies for RHIC and EIC hadron beams Wolfram Fischer
s
Notes: 09:20, 25+10 min, 25 slides

## Slide 2: Mitigation of beam degradation in RHIC and EIC
Many topics presented last week in excellent talks
Many of these topics are also relevant in the RHIC/EIC hadron rings, and the injectors, where all of the standard mitigations are used
Will only highlight some examples that go beyond standard solutions
Will then focus use on beam cooling, which
changed the way we operate RHIC with ions
allowed for experiments not previously possible (Zr-96 / Ru-96, Au+Au below nominal injection energy with 4x L)
will also play an important role in the EIC

## Slide 3
s
Start of operation : 2000
Circumference : 3.8 km
Max dipole field : 3.5 T Species : ph to U (incl. asymmetric) Energy : Au 100 GeV/nucleon : ph 255 GeV
Max ph–ph L : 2.67x1032 cm-2s-1
Experiments : STAR, sPHENIX
high intensity H– polarized H –
He to U
p to Au (backup)

## Slide 4: RHIC – study of QGP requires flexibility
nominal injection energy

## Slide 5: EIC – Electron Ion Collider (now a project, CD-0 Dec 2019)
Addition of electron
Linac (400 MeV)
Rapid Cycling Synchrotron (18 GeV)
Storage Ring (18 GeV)
Start of operation : ~2030
Circumference : 3.8 km
Max dipole field : 3.5 T Species : eh–ph to eh–U Energy : eh 18 GeV
: Au 110 GeV/nucleon : ph 275 GeV
Max eh–ph L : 1x1034 cm-2s-1
Experiments : 1 or 2

## Slide 6
Booster, AGS, RHIC, EIC
RHIC electron lenses
Booster, AGS, RHIC, EIC
AGS, RHIC, EC
Booster
Booster, RHIC, EIC
Booster, RHIC, EIC
RHIC, EIC
Booster, AGS, RHIC, EIC
Linac, AtR, RHIC, EIC
RHIC, EC

## Slide 7: High intensity high brightness ion sources + pre-injectors
Au1+ ions into EBIS
Au32+ ions out of EBIS
Most flexible laser ion source + EBIS for Booster
NASAL Galactic Cosmic Ray Simulator: 33 beams (species, E) in 80 min
reliably 0.5-1.0 mA
polarized H- ion current.
Polarization at 200 MeV:
P = 80-85%.
Beam intensity (ion/pulse)
routine operation:
Source - 1012 H-/pulse
Linac - 5x1011
AGS - 1.5-2.0x1011
RHIC - 1.5x1011/bunch
Unique polarized H- source for 200 MeV Linac
Tandem Van de Graaff
Low emittance beams from electrostatic accelerators
2 electrostatic accelerators
32 MV (=2x16 MV) voltage
>40 ion species p to Au
Highest current H- source for 200 MeV Linac
M. Stockli, ICFA BD Newsletter No. 73, 2018

## Slide 8: Orbit/tune/coupling/chromaticity feedcbak
Blue beam
Yellow beam
Main dipole current
Beam intensity
100 GeV
100 GeV
Ramp start
Polarimeter analyzing power is energy dependent
Useful calibration is to accelerate-decelerate to an energy plateau and compare polarization
Model uncertainty on down ramp
Chromaticity feedback
  RF freq modulated at 0.5 Hz
  Tune feedback effort deviations over each modulation cycle used to calculate a chrom
  Update sent to the sextupoles
Chrom feedback effort during the down ramp was up to 40 units!
Successful measurement completed in one shift with feedback
Would have taken days without it => Would never have been done
Use orbit (1 Hz, 10 Hz), tune, coupling feedback on every ramp (not shown).
Example is for chromaticity feedback for deceleration (2011), not used since.
V. Schoefer, ARIES 2018
250 GeV
Notes: Figure of merit for this experiment is not precision of chrom feedback, but cost of experiment

## Slide 9: Transition crossing in RHIC
RHIC is only supercond. accelerator crossing transition (all ions except p)
Instabilities at transition occurred in past due to impedance and e-clouds, leading to emittance growth and beam loss (tail of bunch trains) => was intensity limit in previous runs
With stochastic cooling can tolerate emittance growth (not beam loss) => allows for more intensity to be accelerated
C. Montag

## Slide 10: Head-on beam-beam compensation Principle
Correction in same turn, need to fulfill 2 conditions:
(1) kp phase advance minimizes beam-beam resonance driving terms – implemented with ATS type lattice (Simon White, now ESRF) new lattice with better DA and larger bb param. x
(2) Same amplitude correction kick as bb kick reduces beam-beam tune spread – implemented with electron lenses (not possible with magnets)
beam-beam parameter

## Slide 11: RHIC e-lens Parameters
Technology sources: Tevatron e-lenses (V. Shiltsev et al.), RHIC Electron Beam Ion Source (EBIS) (J. Alessi et al.)

## Slide 12: Head-on bb compensation Footprint compression
tune distribution can be measured with BTF and p+Al collisions proton beam: (Qx,Qy) = (.685,.695); Al beam: (Qx,Qy) = (.685,.695); DQx, DQy >> x => no coherent modes
no bb
2x bb
DQ reduction from e-lens
Can only reduced BB tune spread (black curve is limit)

## Slide 13: Beam cooling in RHIC and EIC
Heavy ions – strong IBS, cooling envisioned early, bunch intensity ~100x reduced from protons
RHIC stochastic cooling
  heavy and medium ions at high energy
Electron cooling
  Au at low energy (below nominal injection energy)
EIC design options:
  Strong cooling in store (=> strong enough for protons)
  Frequent (every hour) hadron injection with pre-cooling at 25 GeV
tmin ~ 820 s
1984 Nobel prize with C. Rubbia

## Slide 14: 3D stochastic cooling for heavy ions
M. Brennan, M. Blaskiewicz, F. Severino, PRL 100 174803 (2008); K. Mernick PRSTAB, PAC, EPAC
longitudinal kicker cavity (half side with waveguides)
horizontal kicker (open)
horizontal and vertical pickups
longitudinal pickup
5-9 GHz, cooling times ~1 h
vertical kicker (closed)
Notes: Frequency range: 5-8 GHz transverse, 6-9 GHz longitudinal

## Slide 15: U+U operation at burn-off limit – allows measurement of stot
97% of intensity burned off at Lmax
Burn-off dominated operation allows for determination of total U+U cross section stot – and comparison with calculation (mostly QED) published in Phys. Rev. C =>

## Slide 16: RHIC Au+Au operation with stochastic cooling
2007, Beginning of RHIC-II upgrade
2014, End of RHIC-II upgrade
Increase in initial luminosity result of larger bunch intensity
Increase in luminosity lifetime result of 3D stochastic cooling, high peak luminosity not useful without cooling (IBS), losses burn-off dominated
~90% burn-off

## Slide 17: 96Zr+96Zr / 96Ru+96Ru at 100 GeV/nucleon
Zr+Zr
Ru+Ru
Zr+Zr
Ru+Ru
Ru+Ru
Zr+Zr
Ru+Ru
Zr+Zr
beam experiments dedicated
scheduled maintenance
VERY expensive source material (Ru-96) - special enrichment run at ORNL
Need for flat L and same store conditions
Would not have been possible without cooling
Notes: WEEK: 30-Apr-18 to 07-May-18

## Slide 18: RHIC – study of QGP requires flexibility
nominal injection energy

## Slide 19
COOLING
in Blue RHIC ring
COOLING
in Yellow RHIC ring
64 m to IP2
Beam Dump
20° Bending Magnets
DC e- Gun
704 SRF
Booster Cavity
2.1 GHz Cu Cavity
9 MHz Cu Cavity
704 MHz Cu Cavity
Commissioning
Diagnostic Line 1
Commissioning
Diagnostic Line 2
RHIC TRIPLET
RHIC DX
180° Bending Magnet
e-
e-
LEReC Solenoids
Compensating (LF)
Matching (HF)
Merger/Transport
e-
Low Energy RHIC electron Cooling (LEReC)
(not to scale)
Energies E : 1.6, 2.0 MeV Avg. current Iavg : 27 mA Momentum dp/p : 5×10-4
Luminosity gain : 4×
A. Fedotov
1st electron cooler with RF acceleration
+ extends energy reach beyond DC
- dp/p after acceleration 50x too large

## Slide 20: Low Energy RHIC electron Cooler, cooling sections

## Slide 21
[1] A.V. Fedotov et al., PRL, 23, 021003 (2020)
[2] D. Kayran et al., PRAB 23, 021003 (2020)
[3] X. Gu et al., PRAB 23, 013401 (2020)

## Slide 22: EIC – cooling overview
Ion cooling like in RHIC with upgraded stochastic cooling system
For highest luminosity eh–ph (1x1034 cm-2s-1) investigate 2 design options
  Strong cooling = proton cooling at full proton energy
  Frequent (~hourly) full energy proton injection
    Use 1 RHIC ring for acceleration, 1 RHIC for storage
    Proton pre-cooling injection (25 GeV) => extend LEReC technology / ERL
Also investigate proton cooling at 41 GeV for lowest COM
Recent workshop at Fermilab, organized by Sergei Nagaitsev explored cooling options

## Slide 23: EIC strong hadron cooling in pre-CDR
A number of variants with different amplifiers

## Slide 24: Coherent electron Cooling (CeC), V. Litvinenko et al.
experimentally studied in RHIC
unacceptable electron beam noise suppressed in 2019
2 types of amplifiers (undulators, Plasma Cascade)

## Slide 25: Present EIC proton beam cooling concepts
Electron pre-cooling (~10 GeV/u) before injection to EIC
Electron cooling (50 – 150 MeV electron beam energy):
  The key idea here is to compensate for the unfavorable γ2 dependence with a higher electron beam current density
  ERL- based (JLab/ODU): bunched beam ERL and a multi-turn cooling ring
  Induction Linac – based (Fermilab): DC beam (100 A) and a storage ring
  Ring-based cooler concept (BNL); two-energy ring (JLab/ODU)
Stochastic cooling
  All concepts are based on a transit time method
  The key idea here is to increase the bandwidth from ~GHz to ~many THz’s
  Coherent Electron Cooling (BNL/SBU, SLAC)
  Optical Stochastic Cooling (Fermilab, Cornell)
Summary 2019 EIC Cooling Workshop
S. Nagaitsev

## Slide 26: One alternative: Induction Linac Concept (S. Nagaitsev, Fermilab)
We are considering a range of electron beam and linac parameters: 100-200 A beam current, 100 – 200 Hz rep. rate
Pulse length: 380 ns (to fill the ring)
Beam power to dump: 0.8 MW (worst case), 200 kW (best case)
Protons, 100 GeV
Cooling Section, 40-m, 2 kG
Beam dump
Electron Induction Linac
100 m, 55 MeV
Electron ring (115 m circumference)

## Slide 27: EIC – 25 GeV proton beam pre-cooler schematic layout
DC Gun
197 MHz
RF structure.
~2-2.5 MeV
~400 keV
2-2.5 MeV x 123 mA
300 kW Beam Dump
From the cooling section 13.5 MeV
~11 MeV LINAC
197 MHz +591 MHz structure.
~ 6m (with real estate gradient 2 MeV/m)
3-5m Ballistic compression
197 MHz
Some Solenoids
To the cooling section 13.5 MeV
Cooling section: length 130 m, beta* 150-200 m
D. Kayran, A. Fedotov et al.
cooling of proton beams after injection (25 GeV) before acceleration to full energy (275 GeV)
uses LEReC approach (RF acceleration of e-beam, non-magnetized) + ERL

## Slide 28: Summary – Mitigation strategies for RHIC and EIC hadron beams
Essentially all standard and some unique techniques used in AGS Booster, AGS, RHIC and EIC:
bright sources (high-intensity H-, polarized H-, laser+EBIS)
orbit/tune/coupling/(chromaticity) feedbacks on ramps/in stores
transitions jumps (AGS, RHIC – slow ramping sc machine)
beam-beam compensation with electron lenses
Beam cooling fundamentally changed how RHIC is operated
2 cooling systems operational (stochastic for high-E ions electron for low-E Au)
much more luminosity and cleaner operating conditions
operating modes not otherwise possible
Beam cooling also an important technique to fully realize the EIC potential
Au+Au w/ and w/o electron cooling