## Slide 1
E. Métral (many thanks to all the HSC team and for ongoing discussions with Y. Alexahin, M. Blaskiewicz, X. Buffat, A. Burov, C. Hogh, G. Iadarola and A. Oeftiger)
Mitigation of TMCI through Space Charge?
(SC)

## Slide 2
E. Métral (many thanks to all the HSC team and for ongoing discussions with Y. Alexahin, M. Blaskiewicz, X. Buffat, A. Burov, C. Hogh, G. Iadarola and A. Oeftiger)
Many thanks to my dear friend AlexeyB indeed (for all the very interesting discussions on this subject and others for many years)! ;-)
(SC)
Mitigation of TMCI through Space Charge?

## Slide 3
Contents
Introduction (and why this question)
Coherent SC modes from GALACTIC Vlasov solver
  vs. ABS (Air-Bag Square-well) model
  vs. BimBim code (using the Circulant Matrix Model)
What can we deduce from the observation of the intra-bunch motion in the CERN SPS (without math)?
Can this be consistent with some previous instability studies?
Conclusion and outlook

## Slide 4
Contents
Introduction (and why this question)
Coherent SC modes from GALACTIC Vlasov solver
  vs. ABS (Air-Bag Square-well) model
  vs. BimBim code (using the Circulant Matrix Model)
What can we deduce from the observation of the intra-bunch motion in the CERN SPS (without math)?
Can this be consistent with some previous instability studies?
Conclusion and outlook

## Slide 5
Introduction (and why this question)
1st observations in 2003 at SPS injection with Q26 optics
turns

## Slide 6
1st comparison between the measured and simulated (w/o SC and using the BB resonator model of that time) intra-bunch motions
Head
Tail
Head
Tail
G. Rumolo (HEADTAIL)
TMCI
Introduction (and why this question)

## Slide 7
Possible “indirect” observation of mode-decoupling (but no direct observation of mode-coupling)
B. Salvant
Introduction (and why this question)

## Slide 8
Some other observation of intra-bunch motion
Introduction (and why this question)

## Slide 9
PROBLEM: Since 1998 and using the ABS model, it has been found that the TMCI is suppressed by SC => So what could be this instability?
Introduction (and why this question)

## Slide 10
PROBLEM: Since 1998 and using the ABS model, it has been found that the TMCI is suppressed by SC => So what could be this instability?
  1st explanation: it is NOT a TMCI
+
A. Burov, Fermilab APT talk, May 12, 2020
Introduction (and why this question)

## Slide 11
  2nd (possible) explanation: it is a TMCI but we need a more involved/realistic model to treat it
Introduction (and why this question)

## Slide 12
  2nd (possible) explanation: it is a TMCI but we need a more involved/realistic model to treat it
Let’s use the GALACTIC Vlasov solver with the WBL (Water-Bag, Linear RF) model, which will provide also the radial modes => 2-step approach:
Introduction (and why this question)

## Slide 13
  2nd (possible) explanation: it is a TMCI but we need a more involved/realistic model to treat it
Let’s use the GALACTIC Vlasov solver with the WBL (Water-Bag, Linear RF) model, which will provide also the radial modes => 2-step approach:
  1) Solve the Eigenvalue system for the SC impedance, which is a “negative inductance”
Introduction (and why this question)

## Slide 14
  2nd (possible) explanation: it is a TMCI but we need a more involved/realistic model to treat it
Let’s use the GALACTIC Vlasov solver with the WBL (Water-Bag, Linear RF) model, which will provide also the radial modes => 2-step approach:
  1) Solve the Eigenvalue system for the SC impedance, which is a “negative inductance”
  2) Add the linear force as the SC force is
Introduction (and why this question)

## Slide 15
  2nd (possible) explanation: it is a TMCI but we need a more involved/realistic model to treat it
Let’s use the GALACTIC Vlasov solver with the WBL (Water-Bag, Linear RF) model, which will provide also the radial modes => 2-step approach:
  1) Solve the Eigenvalue system for the SC impedance, which is a “negative inductance”
  2) Add the linear force as the SC force is
Introduction (and why this question)
Could be of course easily extended to Gaussian distribution

## Slide 16
  2nd (possible) explanation: it is a TMCI but we need a more involved/realistic model to treat it
Let’s use the GALACTIC Vlasov solver with the WBL (Water-Bag, Linear RF) model, which will provide also the radial modes => 2-step approach:
  1) Solve the Eigenvalue system for the SC impedance, which is a “negative inductance”
  2) Add the linear force as the SC force is
  Pending question: is it fine/sufficient or do we need to solve this fully self-consistently? => Future work to see what the difference between the 2 approaches is
Introduction (and why this question)

## Slide 17
Contents
Introduction (and why this question)
Coherent SC modes from GALACTIC Vlasov solver
  vs. ABS (Air-Bag Square-well) model
  vs. BimBim code (using the Circulant Matrix Model)
What can we deduce from the observation of the intra-bunch motion in the CERN SPS (without math)?
Can this be consistent with some previous instability studies?
Conclusion and outlook

## Slide 18
Coherent SC modes from GALACTIC: first w/o radial modes

## Slide 19
SC parameter
Coherent SC modes from GALACTIC: first w/o radial modes

## Slide 20
ABS model
SC parameter
Coherent SC modes from GALACTIC: first w/o radial modes

## Slide 21
ABS model
?
SC parameter
Coherent SC modes from GALACTIC: first w/o radial modes

## Slide 22
Is there something else to compare with?
Coherent SC modes from GALACTIC: first w/o radial modes

## Slide 23
=> BimBim code (Gaussian)
E. Gottlob (with X. Buffat and T. Pieloni, EPFL, 2018)
ABS model
Is there something else to compare with?
Coherent SC modes from GALACTIC: first w/o radial modes

## Slide 24
=> BimBim code (Gaussian)
WBL model
ABS model
E. Gottlob (with X. Buffat and T. Pieloni, EPFL, 2018)
Is there something else to compare with?
Coherent SC modes from GALACTIC: first w/o radial modes

## Slide 25
=> BimBim code (Gaussian)
WBL model
ABS model
E. Gottlob (with X. Buffat and T. Pieloni, EPFL, 2018)
Is there something else to compare with?
Coherent SC modes from GALACTIC: first w/o radial modes

## Slide 26
ABS model
Results from E. Gottlob (BimBim code, 2018)

## Slide 27
With factor 1.8 between the SC parameters (horizontal axis)
Results from GALACTIC

## Slide 28
With factor 1.8 between the SC parameters (horizontal axis)
Results from GALACTIC

## Slide 29
C. Høgh (with X. Buffat and T. Pieloni, EPFL, 2020)

## Slide 30
Results from C. Høgh (BimBim code): Gaussian, 20 slices, 1 ring (blue)
C. Høgh (with X. Buffat and T. Pieloni, EPFL, 2020)

## Slide 31
Results from C. Høgh (BimBim code): Gaussian, 20 slices, 1 ring (blue)
Results from C. Høgh (BimBim code): Gaussian, 20 slices, 10 rings (pink)
C. Høgh (with X. Buffat and T. Pieloni, EPFL, 2020)

## Slide 32
Results from GALACTIC (WBL model, w/o radial modes)

## Slide 33
Can we be sure that the positive modes are really crossing 0 as predicted by GALACTIC and observed in BimBim code?
Coherent SC modes from GALACTIC: first w/o radial modes

## Slide 34
Can we be sure that the positive modes are really crossing 0 as predicted by GALACTIC and observed in BimBim code? => Let’s check what the BimBim code gives for the ABS model
Coherent SC modes from GALACTIC: first w/o radial modes

## Slide 35
With Linear RF (BimBim)
Can we be sure that the positive modes are really crossing 0 as predicted by GALACTIC and observed in BimBim code? => Let’s check what the BimBim code gives for the ABS model
C. Høgh (with X. Buffat and T. Pieloni, EPFL, 2020)
Coherent SC modes from GALACTIC: first w/o radial modes

## Slide 36
=> Indeed, in this case the positive modes DO NOT cross 0!
With Linear RF (BimBim)
Can we be sure that the positive modes are really crossing 0 as predicted by GALACTIC and observed in BimBim code? => Let’s check what the BimBim code gives for the ABS model
C. Høgh (with X. Buffat and T. Pieloni, EPFL, 2020)
Coherent SC modes from GALACTIC: first w/o radial modes

## Slide 37
CONCLUSION: it seems that the coherent SC modes from GALACTIC (Water-Bag) and BimBim (Gaussian) are very different from the ones of the ABS model (Air-Bag): to be checked/confirmed!!!
  => Positive modes become (heavily) negative with SC parameter + Radial modes
Coherent SC modes from GALACTIC: first w/o radial modes

## Slide 38
CONCLUSION: it seems that the coherent SC modes from GALACTIC (Water-Bag) and BimBim (Gaussian) are very different from the ones of the ABS model (Air-Bag): to be checked/confirmed!!!
  => Positive modes become (heavily) negative with SC parameter + Radial modes
Next question to answer for GALACTIC: why is the mode 00 going down (it remains at 0 for BimBim code)? => See first discussion in Appendix where for instance for the mode 00 in the H-plane of a flat chamber, it was recently found that it is does not remain at 0 (is it also the case here or not?)
Coherent SC modes from GALACTIC: first w/o radial modes

## Slide 39
Coherent SC modes from GALACTIC: w radial modes

## Slide 40
=> Even much more modes becoming negative (as in BimBim or Boxcar model: See Appendix)
Coherent SC modes from GALACTIC: w radial modes

## Slide 41
=> Next: to be checked first!!! Then, detailed (quantitative) analysis of the impact of SC on the TMCI intensity threshold from the SPS impedance
Coherent SC modes from GALACTIC: w radial modes
=> Even much more modes becoming negative (as in BimBim or Boxcar model: See Appendix)

## Slide 42
Contents
Introduction (and why this question)
Coherent SC modes from GALACTIC Vlasov solver
  vs. ABS (Air-Bag Square-well) model
  vs. BimBim code (using the Circulant Matrix Model)
What can we deduce from the observation of the intra-bunch motion in the CERN SPS (without math)?
Can this be consistent with some previous instability studies?
Conclusion and outlook

## Slide 43
Can we understand this intra-bunch signal?

## Slide 44
Can we understand this intra-bunch signal?
Head
Tail
PyHT simulation with 1 bunch: impedance only (i.e. no SC)
K. Li et al.

## Slide 45
YES! => It is a Head-Tail instability

## Slide 46
YES! => It is a Head-Tail instability

## Slide 47
YES! => It is a Head-Tail instability
=> See e.g. below results using Laclare’s formalism (assuming independent head-tail modes): standing-wave pattern along the bunch

## Slide 48
Can we understand this intra-bunch signal?

## Slide 49
Can we understand this intra-bunch signal?
PyHT simulation with 1 bunch: impedance only (i.e. no SC)
M. Beck et al.

## Slide 50
YES! => It is a TMCI (“just above” the threshold)

## Slide 51
YES! => It is a TMCI (“just above” the threshold)

## Slide 52
=> Here the head-tail modes need to be considered together: travelling-wave pattern along the bunch.
=> See more info here: https://cds.cern.ch/record/2714322/files/CERN-ACC-NOTE-2020-0018.pdf
YES! => It is a TMCI (“just above” the threshold)

## Slide 53
Head
Tail
YES! => It is a TMCI (“just above” the threshold)

## Slide 54
Head
Tail
YES! => It is a TMCI (“just above” the threshold)

## Slide 55
Head
Tail
YES! => It is a TMCI (“just above” the threshold)

## Slide 56
Head
Tail
=> TMCI is head-dominated “just above” the threshold
YES! => It is a TMCI (“just above” the threshold)

## Slide 57
Head
Tail
=> TMCI is head-dominated “just above” the threshold
YES! => It is a TMCI (“just above” the threshold)

## Slide 58
TMCI: what happens at higher intensities?

## Slide 59
TMCI: what happens at higher intensities?
=> The signal moves to the tail: amplification from Head to Tail (the higher the bunch intensity, the larger the amplification)

## Slide 60
TMCI: what happens at higher intensities?
Head
Tail
=> The signal moves to the tail: amplification from Head to Tail (the higher the bunch intensity, the larger the amplification)

## Slide 61
TMCI: what about mode-decoupling?

## Slide 62
TMCI: what about mode-decoupling?
=> In case of mode-decoupling, convective instabilities are observed: amplification from Head to Tail with 0 growth rate

## Slide 63
TMCI: what about mode-decoupling?
Head
Tail
=> In case of mode-decoupling, convective instabilities are observed: amplification from Head to Tail with 0 growth rate

## Slide 64
TMCI: what about mode-decoupling?
Head
Tail
Head
Tail
=> In case of mode-decoupling, convective instabilities are observed: amplification from Head to Tail with 0 growth rate

## Slide 65
Head
Tail
TMCI: what about mode-decoupling?
=> In case of mode-decoupling, convective instabilities are observed: amplification from Head to Tail with 0 growth rate

## Slide 66
TMCI: what about mode-decoupling?
=> In case of mode-decoupling, convective instabilities are observed: amplification from Head to Tail with 0 growth rate

## Slide 67
Can we understand this intra-bunch signal?

## Slide 68
PyHT simulation with 1 bunch: impedance only (i.e. no SC)
Can we understand this intra-bunch signal?
D. Amorim et al.

## Slide 69
YES! => It is a TMCI (“well above” the threshold)

## Slide 70
YES! => It is a TMCI (“well above” the threshold)

## Slide 71
YES! => It is a TMCI (“well above” the threshold)
TMCI intensity threshold at ~ 5e11 ppb
Head
Tail
D. Amorim

## Slide 72
YES! => It is a TMCI (“well above” the threshold)

## Slide 73
YES! => It is a TMCI (“well above” the threshold)

## Slide 74
Finally, can we understand this intra-bunch signal at SPS injection with Q26 optics?

## Slide 75
Factor ~ 1.6 above TMCI w/o SC
Finally, can we understand this intra-bunch signal at SPS injection with Q26 optics?

## Slide 76
Assuming it is a TMCI… between (2) transverse modes (which still need to be fully characterised)

## Slide 77
Assuming it is a TMCI… between (2) transverse modes (which still need to be fully characterised)
… it can be estimated that
1) The measurement intensity is “well above” the intensity threshold
2) SC decreases the intensity threshold such that the latter is a factor of ~ 10-20 below the measurement intensity

## Slide 79
H. Bartosik

## Slide 80
H. Bartosik

## Slide 81
Contents
Introduction (and why this question)
Coherent SC modes from GALACTIC Vlasov solver
  vs. ABS (Air-Bag Square-well) model
  vs. BimBim code (using the Circulant Matrix Model)
What can we deduce from the observation of the intra-bunch motion in the CERN SPS (without math)?
Can this be consistent with some previous instability studies?
Conclusion and outlook

## Slide 82
Can SC decrease so much the intensity threshold?

## Slide 83
w/o SC
0
Bunch
intensity
Measurement intensity
Factor ~ 1.6 above TMCI threshold
TMCI intensity threshold
Can SC decrease so much the intensity threshold?

## Slide 84
w/o SC
w SC
0
0
Bunch
intensity
Measurement intensity
Bunch
intensity
Measurement intensity
“Well above” TMCI threshold
Factor ~ 1.6 above TMCI threshold
TMCI intensity threshold
TMCI intensity threshold
Can SC decrease so much the intensity threshold?

## Slide 85
=> Could be consistent with 5 studies

## Slide 86
=> Could be consistent with 5 studies
2-particle model

## Slide 87
=> Could be consistent with 5 studies
2-particle model
PyHT simulations

## Slide 88
=> Could be consistent with 5 studies
2-particle model
2-mode model
PyHT simulations

## Slide 89
=> Could be consistent with 5 studies
2-particle model
2-mode model
PyHT simulations
Soft-slice (instead of rigid-slice) model

## Slide 90
=> Could be consistent with 5 studies
2-particle model
2-mode model
PyHT simulations
Soft-slice (instead of rigid-slice) model
BimBim simulations

## Slide 91
=> Could be consistent with 5 studies
2-particle model

## Slide 92
=> Could be consistent with 5 studies
Chin-Chao-Blaskiewicz_PRAB2016

## Slide 93
=> Could be consistent with 5 studies
Chin-Chao-Blaskiewicz_PRAB2016
Succession of mode-coupling mode-decoupling with reduction of instability growth rate

## Slide 94
=> Could be consistent with 5 studies
Chin-Chao-Blaskiewicz_PRAB2016
PyHT simulations
Succession of mode-coupling mode-decoupling with reduction of instability growth rate

## Slide 95
=> Could be consistent with 5 studies
A. Oeftiger (2018)
Chin-Chao-Blaskiewicz_PRAB2016
Succession of mode-coupling mode-decoupling with reduction of instability growth rate

## Slide 96
=> Could be consistent with 5 studies
A. Oeftiger (2018)
Chin-Chao-Blaskiewicz_PRAB2016
Growth rates to be updated (“envelope fitting” instead of fitting only the first rise)
Succession of mode-coupling mode-decoupling with reduction of instability growth rate

## Slide 97
=> Could be consistent with 5 studies
A. Oeftiger (2018)
Chin-Chao-Blaskiewicz_PRAB2016
2-mode model
Growth rates to be updated (“envelope fitting” instead of fitting only the first rise)
Succession of mode-coupling mode-decoupling with reduction of instability growth rate

## Slide 98
=> Could be consistent with 5 studies
A. Oeftiger (2018)
Chin-Chao-Blaskiewicz_PRAB2016
IPAC19
Growth rates to be updated (“envelope fitting” instead of fitting only the first rise)
Succession of mode-coupling mode-decoupling with reduction of instability growth rate

## Slide 99
=> Could be consistent with 5 studies
A. Oeftiger (2018)
Chin-Chao-Blaskiewicz_PRAB2016
IPAC19
See also https://indico.cern.ch/event/924630/contributions/3903233/attachments/2056784/3449240/SPS_TMCI_with_SC_InstabGrowthRate_EM_15-06-20.pdf for discussion about the instability growth-rate
Growth rates to be updated (“envelope fitting” instead of fitting only the first rise)
Succession of mode-coupling mode-decoupling with reduction of instability growth rate

## Slide 100
=> Could be consistent with 5 studies
A. Oeftiger (2018)
Chin-Chao-Blaskiewicz_PRAB2016
IPAC19
Soft-slice (instead of rigid-slice) model
See also https://indico.cern.ch/event/924630/contributions/3903233/attachments/2056784/3449240/SPS_TMCI_with_SC_InstabGrowthRate_EM_15-06-20.pdf for discussion about the instability growth-rate
Growth rates to be updated (“envelope fitting” instead of fitting only the first rise)
Succession of mode-coupling mode-decoupling with reduction of instability growth rate

## Slide 101
=> Could be consistent with 5 studies
A. Oeftiger (2018)
Y. Alexahin (MCBI 2019)
Chin-Chao-Blaskiewicz_PRAB2016
IPAC19
See also https://indico.cern.ch/event/924630/contributions/3903233/attachments/2056784/3449240/SPS_TMCI_with_SC_InstabGrowthRate_EM_15-06-20.pdf for discussion about the instability growth-rate
Growth rates to be updated (“envelope fitting” instead of fitting only the first rise)
Succession of mode-coupling mode-decoupling with reduction of instability growth rate

## Slide 102
=> Could be consistent with 5 studies
A. Oeftiger (2018)
Y. Alexahin (MCBI 2019)
Chin-Chao-Blaskiewicz_PRAB2016
IPAC19
See also https://indico.cern.ch/event/924630/contributions/3903233/attachments/2056784/3449240/SPS_TMCI_with_SC_InstabGrowthRate_EM_15-06-20.pdf for discussion about the instability growth-rate
“Vanishing TMCI threshold instead of a vanishing TMCI”
Growth rates to be updated (“envelope fitting” instead of fitting only the first rise)
Succession of mode-coupling mode-decoupling with reduction of instability growth rate

## Slide 103
=> Could be consistent with 5 studies
A. Oeftiger (2018)
Y. Alexahin (MCBI 2019)
Chin-Chao-Blaskiewicz_PRAB2016
IPAC19
See also https://indico.cern.ch/event/924630/contributions/3903233/attachments/2056784/3449240/SPS_TMCI_with_SC_InstabGrowthRate_EM_15-06-20.pdf for discussion about the instability growth-rate
“Vanishing TMCI threshold instead of a vanishing TMCI”
Growth rates to be updated (“envelope fitting” instead of fitting only the first rise)
Mentioned to be also consistent with Core-Halo TMCI
Succession of mode-coupling mode-decoupling with reduction of instability growth rate

## Slide 104
=> Could be consistent with 5 studies
BimBim simulations

## Slide 105
=> Could be consistent with 5 studies
C. Høgh (with X. Buffat and T. Pieloni, EPFL, 2020)
  Ongoing analyses => Intensity threshold reduced for intermediate SC parameter (due to TMCI) with Gaussian distribution, which is not observed with Air-Bag. To be continued with larger SC parameters

## Slide 106
3e10 ppb
10e10 ppb
Head
Tail
PyHT simulations (with SC) from A. Oeftiger

## Slide 107
3e10 ppb
10e10 ppb
Head
Tail
PyHT simulations (with SC) from A. Oeftiger
Would be consistent with factor ~ 4 above TMCI (2e12 ppb with previous example)

## Slide 108
3e10 ppb
10e10 ppb
Head
Tail
PyHT simulations (with SC) from A. Oeftiger
Would be consistent with factor ~ 12 above TMCI (6e12 ppb with previous example)
Would be consistent with factor ~ 4 above TMCI (2e12 ppb with previous example)

## Slide 109
Contents
Introduction (and why this question)
Coherent space charge modes from GALACTIC Vlasov solver
  vs. ABS (Air-Bag Square-well) model
  vs. BimBim code (using the Circulant Matrix Model)
What can we deduce from the observation of the intra-bunch motion in the CERN SPS (without math)?
Can this be consistent with some previous instability studies?
Conclusion and outlook

## Slide 110
Conclusion

## Slide 111
Conclusion
Factor ~ 1.6 above TMCI w/o SC
This picture
H. Bartosik

## Slide 112
Conclusion
Factor ~ 1.6 above TMCI w/o SC
tells me 2 things
1) It is a TMCI (well above the TMCI intensity threshold)
2) SC decreases the TMCI intensity threshold by more than an order of magnitude!
This picture
H. Bartosik

## Slide 113
Conclusion
Factor ~ 1.6 above TMCI w/o SC
tells me 2 things
1) It is a TMCI (well above the TMCI intensity threshold)
2) SC decreases the TMCI intensity threshold by more than an order of magnitude!
This picture
H. Bartosik
i.e. a coupling between (2) transverse modes

## Slide 114
Conclusion
Factor ~ 1.6 above TMCI w/o SC
tells me 2 things
1) It is a TMCI (well above the TMCI intensity threshold)
2) SC decreases the TMCI intensity threshold such that the latter is a factor of ~ 10-20 below the measurement intensity
This picture
H. Bartosik
i.e. a coupling between (2) transverse modes

## Slide 115
=> Answer to the question: I would say NO

## Slide 116
=> Answer to the question: I would say NO

## Slide 117
NO from measurements => Compatible with TMCI
  Possible “indirect” observation of mode-coupling / mode-decoupling
  Intra-bunch motion from TMCI (“well above” threshold) – travelling-wave
NO from simplified theories: 2-particle (and 2-mode) models => Compatible with TMCI
    Intensity threshold strongly reduced for high SC parameter (due to TMCI)
NO from PyHT simulations => Compatible with TMCI
    Intensity threshold strongly reduced for high SC parameter
NO from theory (soft-slice) => Compatible with TMCI
    Intensity threshold strongly reduced for high SC parameter (due to TMCI)
NO from BimBim simulations => Compatible with TMCI
  Ongoing analyses => Intensity threshold reduced for intermediate SC parameter (due to TMCI)
=> Answer to the question: I would say NO

## Slide 118
NO from measurements => Compatible with TMCI
  Possible “indirect” observation of mode-coupling / mode-decoupling
  Intra-bunch motion from TMCI (“well above” threshold) – travelling-wave
NO from simplified theories: 2-particle (and 2-mode) models => TMCI
    Intensity threshold strongly reduced for high SC parameter
NO from PyHT simulations => Compatible with TMCI
    Intensity threshold strongly reduced for high SC parameter
NO from theory (soft-slice) => Compatible with TMCI
    Intensity threshold strongly reduced for high SC parameter (due to TMCI)
NO from BimBim simulations => Compatible with TMCI
  Ongoing analyses => Intensity threshold reduced for intermediate SC parameter (due to TMCI)
=> Answer to the question: I would say NO

## Slide 119
NO from measurements => Compatible with TMCI
  Possible “indirect” observation of mode-coupling / mode-decoupling
  Intra-bunch motion from TMCI (“well above” threshold) – travelling-wave
NO from simplified theories: 2-particle (and 2-mode) models => TMCI
    Intensity threshold strongly reduced for high SC parameter
NO from PyHT simulations => Compatible with TMCI
    Intensity threshold strongly reduced for high SC parameter
NO from theory (soft-slice) => Compatible with TMCI
    Intensity threshold strongly reduced for high SC parameter (due to TMCI)
NO from BimBim simulations => Compatible with TMCI
  Ongoing analyses => Intensity threshold reduced for intermediate SC parameter (due to TMCI)
=> Answer to the question: I would say NO

## Slide 120
NO from measurements => Compatible with TMCI
  Possible “indirect” observation of mode-coupling / mode-decoupling
  Intra-bunch motion from TMCI (“well above” threshold) – travelling-wave
NO from simplified theories: 2-particle (and 2-mode) models => TMCI
    Intensity threshold strongly reduced for high SC parameter
NO from PyHT simulations => Compatible with TMCI
    Intensity threshold strongly reduced for high SC parameter
NO from theory with soft-slice model => TMCI
    Intensity threshold strongly reduced for high SC parameter
NO from BimBim simulations => Compatible with TMCI
  Ongoing analyses => Intensity threshold reduced for intermediate SC parameter (due to TMCI)
=> Answer to the question: I would say NO

## Slide 121
NO from measurements => Compatible with TMCI
  Possible “indirect” observation of mode-coupling / mode-decoupling
  Intra-bunch motion from TMCI (“well above” threshold) – travelling-wave
NO from simplified theories: 2-particle (and 2-mode) models => TMCI
    Intensity threshold strongly reduced for high SC parameter
NO from PyHT simulations => Compatible with TMCI
    Intensity threshold strongly reduced for high SC parameter
NO from theory with soft-slice model => TMCI
    Intensity threshold strongly reduced for high SC parameter
NO from BimBim simulations => Compatible with TMCI
  Ongoing analyses => Intensity threshold reduced for intermediate SC parameter (due to TMCI)
=> Answer to the question: I would say NO

## Slide 122
NO from measurements => Compatible with TMCI
  Possible “indirect” observation of mode-coupling / mode-decoupling
  Intra-bunch motion from TMCI (“well above” threshold) – travelling-wave
NO from simplified theories: 2-particle (and 2-mode) models => TMCI
    Intensity threshold strongly reduced for high SC parameter
NO from PyHT simulations => Compatible with TMCI
    Intensity threshold strongly reduced for high SC parameter
NO from theory with soft-slice model => TMCI
    Intensity threshold strongly reduced for high SC parameter
NO from BimBim simulations => TMCI
  Ongoing analyses => Intensity threshold reduced for intermediate SC parameter with Gaussian distribution, which is not observed with Air-Bag See https://indico.cern.ch/event/931949/contributions/3916708/attachments/2064517/3464419/Presentation2.pdf
C. Høgh (with X. Buffat and T. Pieloni, EPFL, 2020)
=> Answer to the question: I would say NO

## Slide 123
Conclusion
Interesting to observe that the usual “damping mechanisms” (such as active damping and tune spread) can be detrimental when several modes are involved!

## Slide 124
Conclusion
Interesting to observe that the usual “damping mechanisms” (such as active damping and tune spread) can be detrimental when several modes are involved!
This is for sure not a TMCI anymore!

## Slide 125
Conclusion
Interesting to observe that the usual “damping mechanisms” (such as active damping and tune spread) can be detrimental when several modes are involved!
This is for sure not a TMCI anymore!

## Slide 126
Conclusion
Interesting to observe that the usual “damping mechanisms” (such as active damping and tune spread) can be detrimental when several modes are involved!
This is for sure not a TMCI anymore!

## Slide 127
Conclusion
Interesting to observe that the usual “damping mechanisms” (such as active damping and tune spread) can be detrimental when several modes are involved!
This is for sure not a TMCI anymore!

## Slide 128
Conclusion
Indeed, the detuning impedance of flat chambers is (also) detrimental (for the same driving impedance) for the SPS TMCI (“long-bunch” regime) and does not suppress/increase it!
=> See https://cds.cern.ch/record/2714848/files/CERN-ACC-NOTE-2020-0019.pdf

## Slide 129
Outlook
The coherent SC modes from GALACTIC and BimBim are very different from the ones of the ABS model (different distribution) => Positive modes become negative with SC parameter + Radial modes
  Was it also observed with other models / simulations? => To be checked/confirmed
  What is the impact on the predicted “convective instabilities” (Burov_PRAB2019)?
Finalise study with GALACTIC
  Fully understand if mode 00 is shifting or not with intensity (do we need to integrate the incoherent force in the Eigenvalue problem)?
  Study the impact of the new SC modes on TMCI

## Slide 130
Outlook
The coherent SC modes from GALACTIC and BimBim are very different from the ones of the ABS model (different distribution) => Positive modes become negative with SC parameter + Radial modes
  Was it also observed with other models / simulations? => To be checked/confirmed. What could be the mistake in the 2 codes?
  What is the impact on the predicted “convective instabilities” (Burov_PRAB2019)?
Finalise study with GALACTIC
  Fully understand if mode 00 is shifting or not with intensity (do we need to integrate the incoherent force in the Eigenvalue problem)?
  Study the impact of the new SC modes on TMCI

## Slide 131
Outlook
The coherent SC modes from GALACTIC and BimBim are very different from the ones of the ABS model (different distribution) => Positive modes become negative with SC parameter + Radial modes
  Was it also observed with other models / simulations? => To be checked/confirmed. What could be the mistake in the 2 codes?
  If confirmed, what would be the impact on the predicted “convective instabilities” (Burov_PRAB2019)?
Finalise study with GALACTIC
  Fully understand if mode 00 is shifting or not with intensity (do we need to integrate the incoherent force in the Eigenvalue problem)?
  Study the impact of the new SC modes on TMCI

## Slide 132
Outlook
The coherent SC modes from GALACTIC and BimBim are very different from the ones of the ABS model (different distribution) => Positive modes become negative with SC parameter + Radial modes
  Was it also observed with other models / simulations? => To be checked/confirmed. What could be the mistake in the 2 codes?
  If confirmed, what would be the impact on the predicted “convective instabilities” (Burov_PRAB2019)?
Finalise study with GALACTIC (and compare to BimBim)
  Fully understand if mode 00 is shifting or not with intensity (do we need to integrate the incoherent force in the Eigenvalue problem)?
  Study the impact of the new SC modes on TMCI

## Slide 133
Outlook
The coherent SC modes from GALACTIC and BimBim are very different from the ones of the ABS model (different distribution) => Positive modes become negative with SC parameter + Radial modes
  Was it also observed with other models / simulations? => To be checked/confirmed. What could be the mistake in the 2 codes?
  If confirmed, what would be the impact on the predicted “convective instabilities” (Burov_PRAB2019)?
Finalise study with GALACTIC (and compare to BimBim)
  Fully understand if mode 00 is shifting or not with intensity (do we need to integrate the incoherent force in the Eigenvalue problem)?
  Study the impact of the new SC modes on TMCI

## Slide 134
Outlook
The coherent SC modes from GALACTIC and BimBim are very different from the ones of the ABS model (different distribution) => Positive modes become negative with SC parameter + Radial modes
  Was it also observed with other models / simulations? => To be checked/confirmed. What could be the mistake in the 2 codes?
  If confirmed, what would be the impact on the predicted “convective instabilities” (Burov_PRAB2019)?
Finalise study with GALACTIC (and compare to BimBim)
  Fully understand if mode 00 is shifting or not with intensity (do we need to integrate the incoherent force in the Eigenvalue problem)?
  Study the impact of the (new, if confirmed) SC modes on the TMCI intensity threshold from the SPS impedance

## Slide 135
APPENDIX

## Slide 136
H modes in a flat chamber
w/o detuning impedance
GianniI
Coherent SC modes vs. driving+detuning modes in a flat chamber

## Slide 137
SC modes (w radial)
w/o incoherent force
H modes in a flat chamber
w/o detuning impedance
GianniI
Coherent SC modes vs. driving+detuning modes in a flat chamber

## Slide 138
SC modes (w radial)
w/o incoherent force
H modes in a flat chamber
w/o detuning impedance
GianniI
Coherent SC modes vs. driving+detuning modes in a flat chamber

## Slide 139
H modes in a flat chamber
w detuning impedance
GianniI
Coherent SC modes vs. driving+detuning modes in a flat chamber

## Slide 140
H modes in a flat chamber
w detuning impedance
GianniI

## Slide 141
H modes in a flat chamber
w detuning impedance
The bend of mode 00 comes from a phase shift (increasing with intensity) which is in the “driving” matrix M
GianniI

## Slide 142
H modes in a flat chamber
w detuning impedance
The bend of mode 00 comes from a phase shift (increasing with intensity) which is in the “driving” matrix M
The “detuning” matrix is linear with intensity
GianniI

## Slide 143
H modes in a flat chamber
w detuning impedance
The bend of mode 00 comes from a phase shift (increasing with intensity) which is in the “driving” matrix M
The “detuning” matrix is linear with intensity
The small difference observed comes from the coupling between the modes
GianniI

## Slide 144
H modes in a flat chamber
w detuning impedance
SC modes (w radial)
w incoherent force
The bend of mode 00 comes from a phase shift (increasing with intensity) which is in the “driving” matrix M
The “detuning” matrix is linear with intensity
The small difference observed comes from the coupling between the modes
GianniI

## Slide 145
H modes in a flat chamber
w detuning impedance
SC modes (w radial)
w incoherent force
The bend of mode 00 comes from a phase shift (increasing with intensity) which is in the “driving” matrix M
The “detuning” matrix is linear with intensity
The small difference observed comes from the coupling between the modes
GianniI
The mode 00 is also bent here (GALACTIC, water-bag)

## Slide 146
w/o detuning impedance
Reminder: driving+detuning from GALACTIC using a “constant detuning tune shift”
w detuning impedance
Shift of mode 00 due to coupling between the modes

## Slide 147
Conclusion
The case of the driving+detuning modes in the H-plane of a flat chamber seems now well understood with the new DELPHI of GianniI et al. => In particular the mode 00 is shifting up with intensity due to 2 effects
  A phase shift (increasing with intensity) which is in the driving matrix (but coming from the detuning term)
  Coupling between the modes

## Slide 148
Conclusion
A similar effect (shift of the mode 00 with intensity) is also observed with SC using GALACTIC (with a water-bag distribution and applying the incoherent force separately)
  Note: a detuning impedance introduces a kick on the slice centroid, while the SC force cannot do that. For this reason, the effect on the mode-00 tune shift might indeed be different
  This is not observed in the BimBim code (using a Gaussian distribution) where the modo 00 remains at 0
  Is the effect observed in GALACTIC real or due to the fact that the incoherent force is applied separately?
  => To be clarified, checked also with new and new new DELPHI. Others?

## Slide 149
Comparison with boxcar distribution of Balbekov_2017 (https://journals.aps.org/prab/pdf/10.1103/PhysRevAccelBeams.20.034401)
WBL w 3 radial modes
Boxcar model

## Slide 150
Comparison with boxcar distribution of Balbekov_2017 (https://journals.aps.org/prab/pdf/10.1103/PhysRevAccelBeams.20.034401)

## Slide 151
Comparison with boxcar distribution of Balbekov_2017 (https://journals.aps.org/prab/pdf/10.1103/PhysRevAccelBeams.20.034401)

## Slide 152
Why the results from the SYNERGIA code seemed to work so nicely with past predictions?
Typo: negative sign missing (comment from A. Burov)
PRAB Burov_2015 (https://journals.aps.org/prab/pdf/10.1103/PhysRevSTAB.18.074401)