## Slide 1: Advances in Collimation at GSI
ARIES-APEC workshop "Mitigation Approaches for Hadron Storage Rings and Synchrotrons"
Lars Bozyk

## Slide 2: Content
Introduction and Motivation
  How to generate high intensity heavy ion beams?
  Ionization loss and dynamic vacuum as an intensity limitation
Dynamic Vacuum
  Measurement of dynamic vacuum effects
  Simulation of dynamic vacuum
Activities around charge exchange collimation
  Systematic measurements of collimator materials
  Collimation in SIS100
  Measurement of cryogenic pumping speed

## Slide 3: Introduction and Motivation
Reaching higher intensities requires a lower charge state:
  Reduction of space charge
  Reduction of stripping losses
New challenges appear:
  Losses due to charge exchange with residual gas
  Dynamic vacuum by ion induced gas desorption
  Self amplification of losses limiting the intensity
Counter measures:
  UHV to XHV conditions, very low static residual pressure
  Careful lattice design remove losses controlled
  Low desorbing surfaces at defined loss positions
  High pumping speed to quickly remove released gases
 U28+ is used

## Slide 4: Dynamic Vacuum
collimator / ion catcher
dipole
beam loss
desorption
desorption
electron loss
electron capture
further
charge exchange
adsorbed
residual gas

## Slide 5: Ionization Cross Sections
Calculated cross sections for single atoms
Cross sections for residual gas molecules are calculated by Bragg‘s additivity rule, e.g.
Assumption on residual gas composition required to calculate total effective cross section

## Slide 6: Simulation of Dynamic Vacuum
StrahlSim has been developed in the past decade at GSI:
Simulation of a self-consistent pressure profile along the ring for each residual gas component individually
Number of charge exchanged ions is calculated for each time step individually, according to energy dependent cross sections for different ionization channels
U28+  U29+
U28+  U30+
Loss distribution for each ionization channel is calculated via linear ion optics, ionized ions are distributed according to this mapping
Simulation of ion induced desorption: Outgassing at the impact cells is increased, depending on the presence of ion catcher
Number of ions and number of pumped gas particles is counted (saturation calculations)
Pressure profile is re-calculated for the next time step  pressure profile evolution

## Slide 7: Simulation of Dynamic Vacuum
Pressure in mbar
Longitudinal Position
Injection-Losses
Extraction-Losses
rf-Capture-Losses (distributed)
no Ion-Catcher

## Slide 8: Measurement of Dynamic Vacuum
Residual gas pressure in mbar, 2010-07-31, U39+

## Slide 9: More Measurements of Dynamic Vacuum Effects
Beam Loss Monitors, 2010-07-31, U39+

## Slide 10: Collimator Material
Different materials and combinations have been investigated in the past
Material of choice for collimators is copper
Coated with gold to prevent the surface from oxidation
Gold and Copper diffuse into each other
Hence, a diffusion barrier our of Chromium, Nickel or Silver is applied
Three coating methods available: thermal evaporation, sputter coating and electro deposition. Systematic desorption measurements ongoing in material science department
M.Bender, Dissertation, 2008
Most important: perpendicular incidence! for grazing incidence η ≈ 25.000

## Slide 11: Ion Catcher in SIS18
G.Otto, 2009
U28+  U29+
65% Catching efficiency

## Slide 12: Ion Catcher Currents
U28+
U63+

## Slide 13: Normalized Ion Catcher Currents
Inner side
Electron Loss
Outer side
Electron Capture
U28+
U63+

## Slide 14: Normalized Ion Catcher Currents U28+
Measurement
Simulation

## Slide 15: Static Lifetime in SIS18

## Slide 16: SIS18 - Intensities
world record
NEG-Panels
in injection septum
ion-catcher and
NEG coating
of magnet chambers

## Slide 17: SIS100 Lattice
SIS100 lattice has been optimized to reach a maximum catching efficiency
U28+  U29+
Loss distribution is strongly localized between the quadrupoles where the ion catcher will be installed

## Slide 18: Cryocatcher in SIS100
Keep cryocatcher at higher temperature (e.g. 77 K)
Direct deposited energy from lost ions into thermal shield cooling (cheaper) instead of magnet cooling
Keep load onto LHe low
Fit into cryostat
Heat from
lost ions

## Slide 19: SIS100 Cryocatcher
 Controlled catching of ionized ions on surfaces with low desorption yield (gold)  most ionized ions are caught by the ion catcher
 Surrounding cold chamber acts as cryopump quickly removing desorbed gases
 Cryocatcher block will be kept at a higher temperature to prevent gases from cryosorbing on the surface of incidence
 Significant reduction of gas desorption  dynamic vacuum effects are suppressed effectively
 Activation and radiation damage of magnets by beam losses are reduced

## Slide 20: SIS100 Cryocatchers: Series production ongoing
60 Cryocatchers will be installed in SIS100

## Slide 21: SIS100 Cryocatcher in Quadrupole Module

## Slide 22: Pumping Properties of Cryogenic Surfaces
Cryocondensatioin:
  According vapour pressure curves
  No capacity limit
  „useable“ H2 partial pressure only for T < 3 K
Cryoadsorption:
  Weak binding of gas particles on the surface
  Limited capacity, max. one monolayer
  H2 get already bout for T 25 K
  Can be described by sticking probability and sojourn time
  Dependence on temperature of sticking probability, sojourn time, and capacity are investigated

## Slide 23: Test Setup Cryopumping
F.Chill

## Slide 24: Implementation in StrahlSim
Adsorption isotherms are included in StrahlSim
Residual gas density is calculated, dependent on temperature and surface coverage
Temperature increase can lead to gas release and subsequent increased loss rate

## Slide 25: Summary
GSI/FAIR is aiming for highest heavy ion intensities
Dynamic vacuum limits the maximum achievable intensity
Ion catcher can shift this limit to higher intensities
SIS18 is equipped with an ion-catcher system, the maximum beam intensity could be improved
SIS100 was designed around an ion-catcher system
60 cryocatcher will stabilize the dynamic vacuum during operation
Thank you.