## Slide 1: Manipulation Measures Including Cooling for Storage and Decelerating Highly Charged Isotopes
M. Steck, Accelerator Operations, Storage Rings,
GSI Helmholtzzentrum, Darmstadt

## Slide 2: Decelerated Beams for Atomic Physics
relativistic Doppler transformation
relativistic transformation of solid angle:
Elab: photon energy in lab system
Eproj: photon energy in emitter system
deceleration reduces:
dependence on velocity and observation angle lab
influence of energy and intensity
deceleration:
provides increased reaction cross sections
opens new reaction channels (transitions, polarization)
radiative recombination U92+
X-rays of REC U92+ -> N2

## Slide 3: Decelerated Beams for Nuclear Astrophysics
  high energy production & separation of radioactive beams in FRS
    most efficient and versatile technique available
  deceleration to energies below 10 MeV/u
    access to the famous Gamow window relevant for nuclear physics of stars
  cooled beam in combination with a thin gas jet target
    inverse kinematics studies at unmatched energy resolution
  storage and recycling of the rare ion beam
    extremely efficient technique for studies on beams of limited intensity
To investigate the origin of elements
in stars, nuclear astrophysics aims for
challenging reaction studies on
rare ion beams.
Heavy ion storage rings at GSI provide unique possibilities and unrivalled conditions for such experiments.
supernova
remnant
x-ray
binary
Experimental setup of the reaction study 124Xe(p,g)125Cs in the ESR at beam energies as low as 5.5 MeV/u
Notes: ESR – early 90s

## Slide 4: Decelerated Beams for HITRAP and CRYRING@ESR
SIS
stripper/ production target
400 MeV/u
UNILAC
FRS
ESR
4 MeV/u
HITRAP
4 K
4-10 MeV/u
CRYRING@ESR
4 MeV/u … 100 keV/u
400–X MeV/u
Slow, heavy, highly charged Ions and Rare Isotopes
Energy range 10 MeV/u to sub eV/ion
105-107 highly charged ions, Pb82+,U92+
linear decelerator
ring decelerator
UNILAC
SIS
FRS
ESR
CRYRING @ESR
HITRAP
11.4 MeV/u

## Slide 5
Connecting ESR to CRYRING@ESR
max. rigidity 1.44 Tm 15 MeV/u U92+
min. rigidity ~ 0.054 Tm 21 keV/u U92+
electron cooling with magnetic expansion factor 100
ESR decelerates cooled highly charged ions or rare isotope beams from 400 MeV/u to 4-15 MeV/u
goal: stored, cooled highly charged ions at lowest energies

## Slide 6
highly charged ions and rare isotopes are produce in thick stripper/target followed by cooling to reduce the beam emittance after the target
good beam quality of stored beam  high precision experiments
high luminosity with internal target for internal experiment
long lifetime of stored beam  vacuum pressure 10-11 mbar or below
fast extraction at 4 MeV/u for HITRAP, defined by the decelerator linac
fast extraction below 10 MeV/u for CRYRING, defined by bending power
slow extraction employing charge changing processes (cooler, target)
goal: maximum intensity (particles per time interval) to HITRAP/CRYRING,
i.e. large particle number, short cycle time
Goals for Deceleration in the ESR

## Slide 7
Fast injection (stable ions / RIBs)
Stochastic cooling (  400 MeV/u)
Electron cooling ( 3 - 430 MeV/u)
Laser cooling (C3+ 120 MeV/u)
Internal gas jet target
Deceleration (down to 3 MeV/u)
Fast extraction (HITRAP/CRYRING@ESR)
Slow (resonant) extraction
Ultraslow extraction (charge change)
Beam accumulation
Multi charge state operation
Schottky mass spectrometry of RIBs
Isochronous mode (TOF detector)
The Heavy Ion Storage Ring ESR

## Slide 8
energy 400 (-550) MeV/u bandwidth 0.8 GHz (range 0.9-1.7 GHz)
p/p = 0.35 %  p/p = 0.01 % e = 10 m  e = 2 m
electrodes
combiner station
power amplifiers
stochastic pre-cooling on the injection orbit
Beam Cooling at the ESR
electron energy 1.6 – 250 keV
electron current 0.001 – 1 A
beam diameter 50.8 mm
magnetic field 0.01 - 0.2 T
collection efficiency 0.9998
transverse temperature 0.1 eV
longitudinal temperature ~0.1 meV
vacuum 1  10-11 mbar
electron cooling
Subsequent electron cooling
fast stochastic pre-cooling

## Slide 9
Cooling after Injection
The injection energy of the ESR is flexible (30- 500 MeV/u)
the production rate of highly charged heavy ions increases with energy, but the larger energy reduction conflicts  the production rate needs to be traded off
electron cooling can be applied for any energy  430 MeV/u
stochastic cooling is presently available at 400 MeV/u but could be extended to higher energies (up to 550 MeV/u)
at 400 MeV/u stochastic cooling is faster than electron cooling
Kr32+ 400 MeV stochastic cooling electron cooling (Iel= 300 mA)
T30 s
T  350 s
cooled beam after  5 s

## Slide 10
rf amplitude
ion current
magnetic
field
Ni28+ 400  30  4 MeV/u
1100 A  180 A  25 A
45% 37%
cycle time 45 s
h=2  4
Typical ESR Deceleration Cycle
1) injection (at 400 MeV/u)
2) stochastic/electron cooling
3) deceleration to 30 MeV/u
4) electron cooling
5) changing rf harmonic 2  4
6) deceleration to final energy
7) electron cooling, bunching, extraction
maximum change of p (B): 13
1)
2)
3)
4)
5)
6)
7)
1.2×108 2.2×107

## Slide 11
Efficiency of Deceleration
Chart: particle number
| 1850000 | 2050000 | 3100000 | 4400000 | 5900000 | 7100000 | 9100000 | 10200000 | 10500000 | 11000000 | 14800000 | 18500000 | 21000000 | 22500000 | 26000000 | 35500000 | 36000000 | 43000000 | 48500000 | 49000000
efficiency | 95 | 96 | 95 | 85 | 87 | 82 | 81 | 76 | 81 | 79.5 | 65 | 43.8 | 43.6 | 35 | 34.3 | 24 | 24.6 | 22 | 18.7 | 17.7
Chart: initial particle number
| 1850000 | 2050000 | 3100000 | 4400000 | 5900000 | 7100000 | 9100000 | 10200000 | 10500000 | 11000000 | 14800000 | 18500000 | 21000000 | 22500000 | 26000000 | 35500000 | 36000000 | 43000000 | 48500000 | 49000000
 | 1757500 | 1968000 | 2945000 | 3740000 | 5133000 | 5822000 | 7371000 | 7752000 | 8505000 | 8745000 | 9620000 | 8103000 | 9156000 | 7875000 | 8918000 | 8520000 | 8856000 | 9460000 | 9069500 | 8673000
deceleration cycle Bi83+ from 400 to 30 MeV/u
loss-free deceleration of some 106 ions
increasing loss above 107 injected ions
stoch. cooling
electron cooling
deceleration
particle number during deceleration

## Slide 12
Efficiency of Deceleration
Losses increase with increase of initial stored particle number most likely due to IBS
in a bunched beam during deceleration transverse emittance is growing
due to intrabeam scattering
no cooling,
larger emittance of bunched beam and due to adiabatic emittance growth ( 1/)
during deceleration the beam is also
approaching the space charge
dominated regime
energies below 15 MeV/u require a change to a higher rf harmonic debunching (h=2), rebunching (h=4)

## Slide 13
Space Charge Limit
Space charge limit due to incoherent tune shift
at 4 MeV/u, for Qx=0.1 and x = 1 mm mrad:
Coasting (B=1): Ne10+: 1.8  108
Kr36+: 5.8  107
U92+: 2.5  107
For bunched beam the intensity limit is reduced by the bunching factor.
Experimental observation: with rf amplitude 100 V (h=1) the bunching factor is B  1/20.
Therefore good control of low rf amplitudes is mandatory.
Bunched ( 1s, B=1/5): Ne10+: 4  107
Kr36+: 1  107
U92+: 5  106

## Slide 14
Modernized Beam Diagnostics
deceleration
orbit shift
bunched beam diagnostics with new BPM digitization
Chart: ESR-BPMs
horizontal beam position during a deceleration cycle from 75 to 15 MeV/u
tune measurements with moderate excitation
orbit shift
deceleration
time
time
horizontal tune
vertical tune
future optimization of the deceleration cycle is indispensable for highest intensities of the decelerated beam
position x [m]
Pb78+

## Slide 15
Beam Parameters of Decelerated Ions
Intrabeam Scattering rate
in case of equipartitioning:
emittance increases  proportional 
ne=5106 cm-3
C6+
equilibrium electron cooling - IBS

## Slide 16
Emittance of Extracted Decelerated Beam
horizontal profile
vertical profile
fast extracted beam Ca20+ 4 MeV/u
the increase of the beam emittance with intensity due to IBS
reflects in the beam size of the extracted cooled beam

## Slide 17
Heating by Intrabeam Scattering
Growth of Beam Emittance due to Intrabeam Scattering
52Cr23+ 4 MeV/u
P. Görgen, Master Thesis, 2011
stronger (faster) cooling results in faster IBS heating
for highly charged ions IBS is expected to scale with Q4/A2
highly charged uranium heats up 10 times faster than Cr23+
It is an open issue whether an
efficient beam transport from ESR to CRYRING can be achieved with the present extraction mode.

## Slide 18
Loss during Bunching a Low Energy Beam
P. Görgen Master Thesis, 2011
Growth after Bunching the Cooled Coasting Beam
 Precise control of rf amplitude down to small values

## Slide 19
Chart: 
| 30 | 20 | 15 | 12 | 10 | 8
 | 374 | 136 | 86 | 42 | 31 | 20
Ne10+
Low Energy Beams – Vacuum
4
Xe54+
measurement of beam half life with an average pressure of p  1  10-10 mbar
REC  ZP
V. Shevelko
simulation for CRYRING
lifetime in the residual gas and cooling time can be of similar value
excellent vacuum and fast cooling
are crucial for low highly charged ions and rare isotopes at lowest energy
Pb82+

## Slide 20
beam half life (vacuum dominated):
30 MeV/u: T1/2  480 s
4 MeV/u: T1/2  2 s
Deceleration to 4 MeV/u
rf amplitude
ion current
bending
field
Ni28+ 400  30  4 MeV/u
1100 A  180 A  25 A
45% 37 %
I
Main losses:
End of ramp
Storage and cooling at low energy
extraction
cycle time
45 s
2107
4106
h=2  4

## Slide 21
Fast Beam Extraction from ESR to CRYRING
fast beam extraction from ESR to CRYRING is employing a sophisticated scheme
with a distorted closed orbit for the circulating beam before extraction to CRYRING consequence: cooling during extraction is questionable, risk of significant heating and emittance growth, particularly for highly charged ions
(expensive remedy: additional kicker in the northern arc)
S. Litvinov
beam orbit in the ESR:
injection/extraction orbit corresponds to p/p=1%

## Slide 22
Slow Extraction by Charge Change
septum magnet installed in UHV
extracted cooled beam
after deceleration (to  10 MeV/u)
small emittance
good control of extraction rate
extraction time minutes to hours
diagnostics in the beamline
two charge states (Au79, Au78+) can simultaneously circulate
extracted dc beam Au78+ at 20 MeV/u

## Slide 23
Additional Options
cooling allows accumulation of higher beam intensity
important for low intensity primary beams and secondary (rare isotope) beams
various methods are available, all based on cooling
bunch compression and decompression
also suitable for flexible creation of bunches at very low energy
new barrier bucket cavity
rf stacking (stochastic/electron cooling on injection orbit, electron cooling on stack orbit)
barrier bucket stacking
injection
orbit
stack
orbit
gap for injection
100 injections over 40 minutes

## Slide 24
Outlook
All manipulations of the ESR operation have to be re-commissioned with the new FAIR control system which is based on LSA (LHC software architecture).
It offers much larger flexibility in tuning machine parameters.
Optimization of the deceleration cycle of the ESR mainly means optimization of the parameters of the cooling systems (reduction of cooling time),
in addition: faster ramping is supported by the hardware.
Various advanced diagnostics hardware and tools have to be integrated into operation and machine optimization, incl. automated procedures.
Vacuum is an issue which requires further investigations.