## Slide 1
Overview on CBM-STS Mechanics
GSI Darmstadt
30.06.2020
O. Vasylyev
DL Engineering

## Slide 2
Agenda
STS design
Detailed system and components overview
  Mainframe and components
  C – frame and components
  Ladder bearings

## Slide 3
STS inside the thermal enclosure
Self carrying STS Mainframe
STS Units
STS Carbon ladders
1. STS Model overview
General facts:
8 Stations
9 Units
106 Carbon ladders
896 Sensor modules
STS inside the magnet

## Slide 4
2. Mainframe overview
Outer Enclosure
Power cable feedthroughs
Insulation:
Between Al Frame and thermal enclosure sandwich
No hard requirements
Easy assembly
Different shapes, and materials available
C-Frame rail supports
Conceptual Insulation
Industrial feedthroughs „Roxtec“
Flexible configuration possible
individual feedthrough access
Amagnetic, high precision rails
C-Frame fixtures
Industrially available
Mainframe structure:
Combination of standard and custom Al profiles
Easy assembly
Large knowledge base
Different precision levels
Extensive industrial support
30.06.2020

## Slide 5
Cooling manifolds
Idea: K. Agarwal
Out manifold
In manifold
Front flange
Rear holder
Connection to the cooling blocks
Concept Facts:
Two manifolds per quarter STS
Flange and manifold is one assembly unit
Space-saving on the front wall
Flexible connection to the C-Frame -> vibration damping
Individual C – Frame access (mostly)
Feasibility test required
Damping:
Swagelok flexible tube
Custom shaped C-Frame piping required!
Disassembly:
Unscrew the flange, holder and cooling lines -> pull towards the rear wall
30.06.2020
2. Mainframe overview

## Slide 6
Side view
Rear view
Power cable
bundles
Robotrax
cable trays
Custom
holders
Custom holders
Robotrax cable tray
3D cable movement possible
Mostly used on robotic arms
Highly customizable system
Idea requires testing
Cable bundles
Bundle area approximation
Only power bundles now
Required space estimation
Integration issues:
Only side routing possible
Space on the front panel
Robotrax dimensioning
Fibers integration
Individual C – Frame access
=>
To be tested in the STS mechanical demonstrator
30.06.2020
2. Mainframe overview

## Slide 7
Overview Unit 07R:
Represents a „worst case Unit“
Extremely limited space for:
  Rail system
  Cable routing
  Sensor cooling
~27mm
~30mm
~24mm
Power cable bundle
C-Frame wagon mount
Fixed ladder bearing
Power cable cover
Perforated tube
Cooling system adapter
Reserved for read-out cables
Most critical components realistically designed
30.06.2020
2. C-Frame overview

## Slide 8
Sensor cooling concept:
C - Frames
Ladders with hidden FEB Boxes
Top view
Visible sensor surface
Visible sensor surface
cooling
element
cooling
element
cooling
element
cooling
element
cooling
element
cooling
element
cooling
element
cooling
element
cooling
element
FESTO Fittings
3D Printed holders
Perforated tubes
Concept Facts:
Nozzles are an example
Space is available
Easy to use tubes e.g. FESTO
Routing is flexible
Concept test
Vibrations?
3. Conceptual integration: sensor cooling
30.06.2020

## Slide 9
3. Ladder bearings
Design and slides by F. Nickels (DTL)
easy assembly
moderate manufacturing
few parts
ideally no adjustment
increased stiffness
high precision due to simple shapes and common mechanical fits!
30.06.2020

## Slide 10
Thank you
DL Engineering