## Slide 1: Firmware Status
17.08.2020
Jochen Frühauf

## Slide 2: Status
Implemented
  32 GET4 Readout / GBTx + debug information
  reconfig only single GET4 instead of all GET4 connected on one GBTx
    reconfig is disabled at startup
    enable reconfig in debug tool ( run debug tool and press e )
  better controlled data path over FIFO stages
    FIFO FULL flag to ignore Hits and save only EPOCH messages
  latency check using deserializer error
  GBTx status bits checker via IP BUS
    tells you if GBTx is looked or a PWR cycle is needed before configuration
    works most of the time
missing
  FIFO Full Flag information inside data-stream
  handling of back pressure from FLIB
    leads to uncontrolled Data loss
    seems to be the next bottle neck
  Firmware startup after reboot / reload
    before reload “configWR” needed
    cannot be loaded out of FLASH device

## Slide 3: Tests
running stable with 10kHz on all channel for 5 days
Rate capability seems to be improved by a factor of 2
before 50kHz => now 100kHz (~98% efficiency)

## Slide 4: Firmware to test in HD
PADI X
https://git.cbm.gsi.de/j.fruehauf/DPB_design/-/jobs/9375/artifacts/download
PADI XI
https://git.cbm.gsi.de/j.fruehauf/DPB_design/-/jobs/9377/artifacts/download