## Slide 1: Requirements to controls for CR commissioning
Oleksii Gorda
17 September 2020
Workshop on Controls developments for FAIR commissioning

## Slide 2: Recap: overview and tasks of CR
 | Operation mode | Kin. Energy | Nmax | Cycle Time
1 | pre-cooling | 3 GeV | 108 | 10 s *
2 | RIB pre-cooling | 740 MeV/u | 108 | 1.5 s
3 | RIB isochronous mass-measurements | 400-790 MeV/u | 1-108 | few turns
4 | Delivery of primary stable beams from SIS-18 to HESR ** | On demand, (with pre-cooling if necessary) |  | 
 | Operation mode | Kin. Energy | Nmax | Cycle Time
1 |  | 3 GeV | 108 | 10 s *
2 | RIB pre-cooling | 740 MeV/u | 108 | 1.5 s
3 | RIB isochronous mass-measurements | 400-790 MeV/u | 1-108 | few turns
4 | Delivery of primary stable beams from SIS-18 to HESR ** | On demand, (with pre-cooling if necessary) |  | 
extraction to HESR *
extraction to HESR *
in-ring
* within the Modularized Start Version (MSV) of the FAIR project
** option under consideration
extraction to HESR **
Antiprotons
εx,y = 240 mm mrad
δp/p = ± 3%
from -separator
from Super-FRS
RIBs
εx,y = 200 mm mrad
δp/p = ± 1.5%
to HESR
No beam acceleration or deceleration. Operation at the fixed magnetic rigidity.
Flexibility in switching between the different operation modes.
Polarity change of equipment required when switching between antiproton and RIB modes.
Beam
Circumference 221.45 m
Max. magnetic rigidity 13 Tm
TCR1

## Slide 3: CR cooling cycle
Injection
single-turn
Bunch rotation & de-bunching
Max. RF voltage of 100 kV for p-bar bunch rotation.
Stochastic cooling
Re-bunching
Extraction
Re-excite RF voltage for re-bunching
Simultaneous 3D cooling
to HESR
injected bunch length σb ~ 50 ns.
Schematic RF pattern for antiprotons *
* not true to scale
Injection

## Slide 4: Planned operation cycle
Appropriate timing signals/sequences for the septum magnets, kicker magnets, RF cavities and stochastic cooling system.
Real-time timing triggers for the machine modes, RF clock, stochastic cooling and other events: manual adjustment/optimization of the timing sequence depending on the operation mode.
Individual equipment timing triggers during the commissioning with/without beam.
Synchronization of hardware operation including Super-FRS, pbar-separator, RF turn on, equipment state changes, data acquisition for power supplies and beam diagnostics.
Polarity change of the main magnets, kickers and septa for commissioning and operation with different beams.
* not true to scale
** values in () correspond to RIB mode

## Slide 5: Commissioning without beam
Testing/dry running of individual TCR1 and CR equipment – testing of components and data acquisition systems according to specifications (magnets/power converters, RF system, injection/extraction, beam diagnostics, stochastic cooling components, experimental devices).
Manual and/or automated testing with using of programmable sequencer tasks (connection/communication, powering, interlocks, etc.).
Tools for data analysis and visualization – manual or automated (for standard testing procedures)?
Possibility of parallel equipment testing: lock test circuits during testing to prevent simultaneous access.
Dry running of the complete CR system within programmed sequencer tasks taking into account the required timing dependencies.

## Slide 6: Example: power converters
DC magnets/ correctors
Injection/ Extraction
magnets
48
QPC+TCR1 DPC
26
ACU
26
SPC
12
OPC
48
ACU+DCCT
Thermostab
Control rack
6
SCU+IO
INJECTION
SEPTUM
EXTRACTION
SEPTUM
3
SCU+IO+Sync
2
SCU+IO+Sync
1
DPC
53
CPC
27
SCU+IO
CR Magnet System

## Slide 7: Example: quadrupole PC control
Specific features:
  testing of the polarity change within the specified time of 60 sec.
  quadrupole ramping test within the planned antiproton cooling cycle according to the requirements (0.024 T/s ramping rate).
List of QPC type PC control and status
channels:
Control: PC soft start
Control: PC on/off
Control: Output current setpoint
Status: Load current
Status: Load voltage
Status: Primary current
Status: Dclink voltage
Status: Earth current
Status: up to 20 DIN
Interlock source | Interlock | ICM target connector
ICM board |  | 
Main contactor | DIN1 - Main contactor | X4
Fast shutdown + Door switch | DIN2 – Fast OFF | X5
Control Part Mains Monitor | DIN3 – Control Part Mains Voltage | X6
Power Part Mains Monitor | DIN4 – Power Part Mains Voltage | X7
Control part power CBs status | DIN5 – Protective Power Switch | X8
Heatsink TSW | DIN6 – Heatsink overheat | X9
PAS Interlock / reserve | DIN7 – PAS interlock | X10
WCable connection TSW | DIN8 – Load cable TSW | X11
Termoswitch @130 Transformer | DIN9 – Step-down transformer warning | X12
TermoSwitch @120 Transformer | DIN10 – Step-down transformer Overheat | X13
Output overvoltage | AIN1 – Load voltage | X2
Primary overcurrent | AIN2 – Primary current | X31
DC Link voltage level | AIN3 – DCLink voltage | X3
Earth current monitor | AIN4 – Earth current | X32
Out Oscillations | AIN5 | X15
Waterflow monitor 1 | WF1 – PC waterflow monitor | X30
Waterflow monitor 2 | WF2 – WCable waterflow monitor | X30
40 DIN Extention board |  | 
Thermo SW Magnet 1 – EXT1 | DIN11 – Load protection TSW | EBoard
CWater SW Magnet 1 – EXT1 | DIN12 – Load protection Water | EBoard
Thermo SW Magnet 2 – EXT2 | DIN13 – Load protection TSW | EBoard
CWater SW Magnet 2 – EXT2 | DIN14 – Load protection Water | EBoard
Thermo SW Magnet 3 – EXT3 | DIN15 – Load protection TSW | EBoard
CWater SW Magnet 3 – EXT3 | DIN16 – Load protection Water | EBoard
Thermo SW Magnet 4 – EXT4 | DIN17 – Load protection TSW | EBoard
CWater SW Magnet 4 – EXT4 | DIN18 – Load protection Water | EBoard

## Slide 8: RF de-bunchers
* not true to scale
Schematic RF pattern for antiprotons *
Testing of interfaces for pulse, amplitude and phase control in operational environment.
Flexibility in manual setting and testing of the RF pattern implementation and timing sequences for the RF processes during commissioning and operation with beam.
Different operation modes (antiprotons, RIBs, stable ions) require specific settings and timing: system optimization and dry running of pre-defined RF cycles according to the planned operation modes (create sequencer tasks?).
Saving settings and archiving measured parameters.

## Slide 9: Stochastic cooling system
Palmer Pick-Up
Slot-line double Pick-Up
Kickers
Local controls developed by technical expert group. Development of operational planned in collaboration with FZJ colleagues to be integrated into FAIR control system.
Implementation of different cooling methods depending on operation modes (antiprotons, RIBs, stable ions) require different sequences/cooling time/hardware need flexibility in setting up of the operation cycles/timing signals.
Interfaces for testing and tuning of movable linear motors of the cryo pick-ups within planned working cycles following shrinking beam during cooling.
Testing of controls for the cryocompressors, interlocks etc.

## Slide 10: Commissioning with beam
First stage - commissioning and tuning of the machine with proton beam (later with stable ions) from SIS18: commissioning with antiprotons and RIBs – later stage.
Multiple settings have to be prepared, pre-programmed and saved according to the commissioning stages/available beams.
Provide possibility for manual and/or automated control of individual equipment.
Dedicated timing sequences/dependencies and hardware synchronization between SIS18, pbar-separator, Super-FRS and beamlines according to the commissioning stages/operation modes.

## Slide 11: Commissioning with beam – injection
Control and optimization of key equipment section-by-section.
Collect and save equipment settings and measured data from the beam diagnostics devices.
Diagnostics in TCR1 channel: 6 BPMs and 3 scintillation screens to measure the transverse beam position and shape.
Diagnostics in CR injection region: 2 BPMs and 2 scintillation screens.
Beam stopper will be used for relative measurement of the beam current and for protection of the ring equipment.
Beam loss monitors might be used for beam loss detection at specific locations.
Proton beam
TCR1
CR
Injection kicker
Injection septum magnet
Beam stopper
Scintillation screen
Scintillation screen
BPM
BPM

## Slide 12: First turn stored beam
Proton beam
First turn – data from scintillation screens, BPMs and scrapers to monitor the beam position/profile.
Beam stoppers for terminating the beam and measurements of relative beam current.
Application of beam loss monitors for control of beam losses and estimation of beam position in combination with scrapers.
For commissioning with antiprotons additional collimation in the pbar-separator might be necessary, e.g. need to adjust and control the device settings and timing sequence.
Beam current measurements and evaluation of injection efficiency.
Stored beam – standard measurements of the main parameters:
  orbit measurements, tuning and corrections,
  tune and chromaticity measurements and corrections etc.
Longitudinal bunch profile measurements during the RF processes.
Measurements of transverse beam profile and momentum distribution during the stochastic cooling.
Data collection and saving for further analysis and visualization.

## Slide 13: Outlook
Establish a more intense and regular communication with Controls department regarding interfaces to the control system and specific requirements for CR involving technical experts.
Preparation of detailed test procedures for equipment testing by technical expert groups.
Major part of the CR components including magnets, power converters, injection/extraction, beam diagnostics and vacuum will be produced and delivered by BINP (Novosibirsk). BINP colleagues would like to be involved into development of the control system interfaces for CR in order to prepare for testing and commissioning of equipment (writing FESA classes etc.) taking into account requirements of the FAIR control system.

## Slide 14
Thank you!