## Slide 1: Specific Controls Requirements for pLinac Workshop on Controls Developments for FAIR Commissioning and the Operation of the existing Accelerator Complex 17 Sep 2020 C. Kleffner PLI

## Slide 2: Overview
Beam Energy (MeV) | 70 → 68
Design Current (mA) | 70
Beam Pulse (µs) | 36
Repetition Rate (Hz) | 4 → 2,7
Frequency (MHz) | 325.224
Beam Loading (peak) (MW) | 4.9
RF Power (peak) (MW) | 2.2
Klystron (3 MW Peak Power) | 7
Solid State Amplifier | 3
Total Length (RFQ + CH) | ≈ 27 m

## Slide 3: overall design
2.45 GHz ECR source generating 100 mA of 95 keV protons
LEBT & diagnostics chamber: faraday cup / allison scanner / wien filter
ladder 4-Rod RFQ with chopper and a beam dump in front
Six normal conducting crossbar cavities of CCH and CH type aranged in two sections with intermediate diagnostic section
CEA
IAP

## Slide 4: pLinac: main devices
Control System Standard Devices
RF: 7 klystrons & modulators / 3 transitor amlipifiers
vacuum devices / pulsed power supplies / movable dev.
GSI (FAIR) beam instrumation devices
Non-Standard Standard Devices
CEA Ion Source, LEBT, BI, Chopper: Labview → LSA
mobile testbench with special BI devices during construction / set-up phase in the accelerator tunnel
CEA
IAP

## Slide 5: FAIR primary beam chain: Protons
pLinac

## Slide 6: FAIR booster operation: Protons
anitiproton production chain in a periodic pattern

## Slide 7: FAIR parallel operation
parallel operation
example pattern with periodic antiproton chain
parallel operation of Unilac and pLinac the TK !

## Slide 8: pLinac booster mode
SIS18
pLinac / Unilac parallel operation mode

## Slide 9: pLinac machine-test beam-dump
periodic operation mode (i.e. 0,5 Hz)
independent to Unilac operation mode

## Slide 10: pLinac machine-test with TK
periodic operation mode (i.e. 0,5 Hz)
exclusive pLinac
TK9 Cup

## Slide 11: pLinac step-by-step installation
periodic operation mode (i.e. 0,5 Hz)
independent to Unilac operation mode
support of mobil testbench (spektrometer, beamshape monitor, emittance measurement …..
Start 2023 after ion source installation
step-by-step cavity installation
and commissioning with beam

## Slide 12: pLinac demands
support of all devices including mobile testbench
parallel / indepent operation: timing / sequencer
stability pulses for RF systems (2,7 Hz ?)
parameter scans (orchestrated operation) of parameters should be possible
(spektrometer, amplitude/phase scans,…)
support for machine dependant applications?

## Slide 13
thank you for your attention