## Slide 1: Effects of overlapped quadrupole fringe fields for HSI-RFQ transverse matching
C. Xiao
UNILAC post stripper upgrade department, GSI

## Slide 2: Outline
general introduction
transfer matrix method
introduction of new QQ focusing system
measured one-dimensional field-map including fringe field
Mathcad program
comparing of results of hard edge and fringe field models
conclusion

## Slide 3: HSI-LEBT and quadrupole quartet (QQ)

## Slide 4: General introduction
4: matching the envelope to the HSI-RFQ, set proposed setting, and measure HSI-RFQ transmission efficiency
1: replacement of the QQ by a new one
2: commissioned with low and high current Argon beam
3: measuring Twiss parameters in front of the new QQ
5: vary the proposed setting in order to maximize transmission efficiency
6: re-simulate all measurements and compare simulations and experiment
7: using the transfer matrix (hard-edge mode) method showed disagreement: best setting (experiment) not as proposed, but 1.075 times the proposed values

## Slide 5: Idea of quadrupole fringe field overlap
will the overlapped fringe field of quadrupoles reduce the effective values: ?
to be investigated
No
No

## Slide 6: Standard transfer matrix method

## Slide 7: Algorithm of precise fitted function
a cubic spline non-linear function can be
written
a fitting function can be described as
position
magnetic gradient
+
small step (more measures) means precise fitting

## Slide 8: Measured field maps of the QQ quadrupoles
effective length of quadrupole is calculated as
numerical integration of cubic spline fitted function
courtesy F. Kloos et al.
maximum gradient

## Slide 9: Mathcad routine
quad
quad
quad
quad
initial
final
target
solution
emittance measurements
drift
drift
drift
drift
drift
Mathcad
RFQ entrance
transfer matrix of drift
transfer matrix of quadrupole
target !!!

## Slide 10: Overlapped fringe field map ()
parameter | [mm mrad] |  | [m/rad]
horizontal | 107.96 | -5.52 | 11.18
vertical | 122.43 | -2.94 | 4.33
parameter |  |  | 
horizontal | 107.96 | -5.52 | 11.18
vertical | 122.43 | -2.94 | 4.33
parameter | [mm mrad] |  | [m/rad]
horizontal | 107.96 | 1.03 | 0.065
vertical | 122.43 | 1.00 | 0.065
parameter |  |  | 
horizontal | 107.96 | 1.03 | 0.065
vertical | 122.43 | 1.00 | 0.065
measurements at slit/grid position (in front of QQ)
transported parameters at the HSI-RFQ entrance
basing on the standard transfer-matrix method
setting #0
one dimensional field map

## Slide 11: Multiplying all slice matrices from field map
decomposition of an actual quadrupole field profile into many segments of hard edge quadrupoles
multiplying all slice matrices
divided in to many slices

## Slide 12: Simulated beam envelopes
.0
m/rad
target Twiss @ RFQ
setting #0 has been used (assumes hard edge fields!)
the corresponding hard edge field mode and overlapped fringe field mode have been simulated for comparison

## Slide 13: Tuning the quadrupole strengths
setting #0
hard edge field mode: all the gradients of quadrupoles are not changed
overlapped fringe field mode: all gradients of quadrupoles are multiplied by factor of 1.069
factor
unchanged
two modes has the similar results
.0
m/rad
target Twiss @ RFQ

## Slide 14: Experiment using high current beam
setting #1: designed gradients from hard edge field
setting #2: scaled gradients from overlapped fringe field
both settings simulated with overlapped fringe fields
Setting #1
Setting #2

## Slide 15: Experiment using low current beam
setting #3: designed gradients from hard edge field
setting #4: scaled gradients from overlapped fringe field
both settings simulated with overlapped fringe fields
Setting #3
Setting #4

## Slide 16: Exp. and simulated results of LEBT QQ & RFQ
beam currents have been measured before and after the HSI-RFQ
simulations have been done with BEAMPATH code
KV distributions have been assumed at the entrance of the HSI-RFQ
 | setting #1 | setting #2
simulation | 24.28% | 59.53%
experiment | 28% | 55%
 | setting #3 | setting #4
simulation | 36.99% | 99.53%
experiment | 34% | 100%
high current beam
low current beam
HSI-RFQ transmission efficiency
settings #1 and setting #3: neglecting fringe overlap
settings #2 and setting #4: considering fringe overlap

## Slide 17: Conclusion
The new QQ at GSI LEBT section is applied to match the Twiss parameters at the RFQ entrance to the required value
The new QQ at GSI LEBT has been investigated using two modes: hard edge mode and field-map mode
A dedicated program basing on MATHCAD has been developed to simulate the above modes through the new QQ section
Fringe field effects of the quadrupole in beam line were often neglected in previous studies
Sharp cut-off approximation of fields (hard edge mode) can be assumed in DTL simulations as quadrupoles are well separated w.r.t. fringe extension
Field imperfections from overlapped fringe fields can significantly affect final Twiss parameters
A specific factor of 1.069 has been determined using field-map mode by simulations. The experimental result of 1.075(25) agrees very well
Thanks for the support and help from our colleagues at GSI