## Slide 1
I.FAST-REX Kick-off Meeting 8th to 9th of February 2021
Discussion Session
First of all: Thank you for your extremely valuable contributions
and the fact that you share your developments with the community
In green: Commitments during discussion

## Slide 2
Observations concerning micro-spill Investigations
Observations and proposals for common problem analysis: (personal view)
Different beam parameters e.g. 24 or 400 GeV/c at CERN, 0.1-0.4 GeV/u at MedF. 0.2-20 GeV/u at GSI
But: Relevance of scaled values e.g. transit time Ttr [turns] & Ttr / Tsyn , long.-trans.: …..
might not be so different.
 Proposal: Prepare a list of scaled quantities  volunteers from MedA
Different extraction methods: tune-variation incl. COSE (CERN, GSI,MedA), KO (GSI, MedF), Betatron (MedF), long. rf driven (MedA, CNAO), several methods available at MedA
What are the differences and what are common challenges?
 Expectation: This topic will be discussed during the start phase of I.FAST-REX.
What is the sensitivity of the beam to PS ripple for the different methods?
Dependence of micro-spill structure on extraction time?
 Certainly important for GSI, others not clear.
Power supplies: Which field (dipole, quad) fluctuation is dominant? What is the ripple amplitude I/I? What is the relevant frequency range?
 Expectation: This specification cannot be given right now, but will be part of I.FAST-REX project.
What is the sensitivity of the beam (e.g. ‘magnet bandwidth’, eddy currents in vacuum chamber…)?
Can the same technology used for super-conducting magnets?
 This topic was not discussed in detail in this meeting, to be continued
Continuation at
next slide

## Slide 3
Observations concerning micro-spill Investigations
Observations and proposals for common problem analysis: (personal view)
For mitigation of ripple effects different methods are used:
1. Active PS stabilization, feedforward, proposal of precise measurements, ACQ 50 Hz-harm. compensation…
2. Robustness by beam parameters: bunch beam extraction, empty bucket channeling, tune wobbling
3. Feedback using PS measurement versus feedback using beam measurement
(e.g. detector bandwidth, transfer function, delay, regulation bandwidth incl. extraction time dep.)
Definition of spill characterization: Duty factor is commonly used, but sampling time not mentioned
Experimental investigations: Experimental methods incl. detectors are different
List of scaled values, ‘scaled’ challenges and mitigations for comparison would be helpful
Proposal: Can be included in an overview list task will be started by Florian Kühteubl (MedA).
continuation of the first list prepared in the 1st slow extraction workshop
Pervious comparison for various facilities, status November 2017:
Comparison of micro-spill quality complied at Slow Extraction Workshop GSI 1-3 June 2016:
https://indico.gsi.de/event/4496/images/494-comparison_of_spill_structure.pdf
List of slow extraction types and characterizations from Slow Extraction Workshop CERN 9-11 Nov. 2017:
https://indico.cern.ch/event/639766/sessions/253774/attachments/1562975/2461614/catalogue_SE_types.pdf

## Slide 4
Road Map for micro-spill Improvements
Observations and proposal for common problem mitigation: (personal view)
Perspective related other parameters, e.g. low loss, pointing stability, emittances, reproducibility
Investigations at CERN: COSE, emittance manipulations (octupoles), feedforward tune adaption…
Investigations at GSI: sextupole dependence, tune wobbling, bunching (if acceptable for user)
Mitigations at MedF: bunched beams, empty bucket channeling + HFRI + p/p increase, macro-spill feedback, ACQ with 50 Hz-harmonics compensation. Is KO excitation a common outlook for all MedF?
Feedback possibilities to be investigated
List of achievements and their comparison incl. new devices e.g. ACQ would be helpful
 Proposal: Can be included in the overview list

## Slide 5
Road Map for micro-spill Improvements
Technical specifications: (personal view)
Comparison & specification for PS concerning I(f)/I (depends on Imax, required ramp-rate or BW
interface to PS control ….)
For KO-extraction: Requirement of signal generation, power level
Signal generation: Software Defined Radio seems appropriate, see talk by Eike Feldmeier.
Power amplifier: Specification must be defined.
Comparison of beam instrumentation (type, bandwidth, noise contribution…)
R&D aspects of the industry contributions
Battery-driven or precise current source PS stabilization?
 List of specifications and ‘wish list’ would be helpful
Beam dynamics simulations: (personal view)
MADX used CERN and GSI, non-linear methods at CERN (maptrack, Henon maps…)
Methods used at CERN adapted to MedAustron
Other simulations at MedF ?
List of experiences and exchange of input files would be helpful
Topic was not discussed in detail during meeting  waiting for working group formation

## Slide 6
Practical Considerations for I.FAST-REX
Workshare , communication, common efforts (personal view)
Collaboration efforts based on the proposed lists on previous slides?  must be defined during project
What are common interests & challenges, what is better investigated for each facility?
 answer related to the outcome of the working groups
Common specification efforts and technical realizations?  formation of working groups
Common experimental campaigns and simulation efforts? (e.g. one model synchrotron?)  not discussed
Workshare and responsibilities of the technical developments?  formation of working groups
Communication: Common web-site to post documents  google drive better to be established by GSI
Communication: Periodicity of meetings, expert meetings?
 Formation of working groups with experts, meeting every  3 month
 All involved persons, meeting every  6 month
List of involved persons?  All participants of this workshop as members of a mailing list
Update table from Stefan Sorge?  Task will be started by Florian Kühteubl (MedA)
Administrative efforts of the project (Grant Agreement not signed…)?  Only bilateral meetings
Your wish list and ideas for I.FAST-REX
Further commitments:
 Formation of working groups related to several subjects  proposal by P. Forck & R. Singh (GSI)
 Synergies with HITRI+ will be evaluated (EU-Project start May 2021, focus on bio-physics related topics)