## Slide 1: SIS18-EP-109.01 Brho calibration of FRS dipoles
Motivation: After major repair and re-assebly of all four dipoles in the symmetric branch of the FRS, these magnets need a new absolute brho-calibration. Deviations from known systematics were seen during the beamtime in 2020.
Activity: center a primary beam at different but known brho through the FRS record current of the dipole magnets
Needs: low Z primary beam which is mainly fully ionized at 1.5 Tm e.g. 12C,16O (unpleasent alternative: measure with removed vacuum window between SIS-FRS) 10 SIS energies in the range from 1.5 – 18 Tm, Energy in SIS must be measured with 10-4 accuracy
Beam request: 3 x 2 shifts with SIS-18 experts (for accurate SIS energy), magnet group (for accurate current recording), FRS, Super-FRS groups

## Slide 2: ESR-EP-115.01 Improvement of radioactive-beam injection into ESR
Motivation: there are several FRS-ESR experiments with radioactive beams; more are expected to come in next years; the intensity requests are increasing; while FRS and ESR can accept beams with large momentum spread (exceeding ±1% and ±1,5%, respectively), the bottleneck is the transfer channel between both instruments and the ESR injection area; an ion-optical description, which can model the injection conditions in a realistic manner, is still missing; mapping studies with a primary beam via TE-line are suggested.
Activity: primary beam shall be injected via TE-line and via FRS; the two quadrupole dubletts between FRS and ESR shall be varied systematically based on ion-optical calculations; all calculated settings will be compared with measurements; the best matching conditions shall be determined via beam-position measurements (profile grids inside ESR) and via transmission/injection-efficiency measurements.
Needs: primary beam with 400 MeV/u
Beam request: 2 times 2 shifts in close cooperation with ESR experts

## Slide 3: SIS18-EP-110.01 SIS-18 extraction efficiency and transmission measurement to FRS target
Motivation: the extraction efficiency depends on magnetic resp. electric rigidity of the heavy-ion beams; the transmission between SIS-18 and FRS target station is not known; both figures shall be quantified by systematic measurements.
Activity: beam intensity shall be measured inside SIS, with SEETRAM behind SIS extraction and with SEETRAM at FRS entrance for primary beam covering rigidities 8...18Tm.
Needs: primary beam with several different SIS energies
Beam request: 2 times 2 shifts in close cooperation with SIS18 experts

## Slide 4: proposals related to the FRS
SIS18-EP-109.01 Brho calibration of FRS dipoles -> important -> A
SIS18-EP-110.01 SIS-18 extraction efficiency and transmission measurement to FRS target –> better to postpone until SIS18-AP-097.01 completed -> C
ESR-EP-115.01 ESR injection improvement -> important -> A
SIS18-EP-109.01 should have priority over ESR-EP-115.01
further proposals with FRS involvement:
SIS18-112.01 Beam-based Macro-Spill Feedback Control -> important for NUSTAR program -> A
  FRS part is planned to be adressed in S511
HEST-AP-095.01 Emittance measurements and Optics verification for the following HEST lines: ESR-CRYRING, ESR-HTA and FRS-HTM
  cooperative efforts for FRS-HTM is very welcome and useful, in particular with respect to planned BARB program in june 2021 -> important -> A