## Slide 1: Unilac – 16.2.2021
Beam time: protons and carbon from CH3. Since Monday 8th Feb 2021, after beam commissioning GSI with Ar8+ from HLI (US3MK2 PS defect+repaired), and operator training 5th to 7th February.
Beam tuning CH3:
  The A4 / 10 Hz problem (new software version, checked 14th Jan, okay) occurred again, Ion source 2 Hz, Alvarez RF-conditioning Vacc 2 Hz “absorbed” beam pulses. Solved by P. Kainberger. Comment: Problem only sometimes “happen to appear”, can be solved by stopping and restarting virtual accelerator.
  Proton beam setup (Alvarez at 1.5 – 1.8 Volts, modified phases) with 1200 mbar gas stripper pressure. Also Carbon6+ beam, 2000 mbar. Tue 16th Feb Re-Optimisation
Dirt and dust in TK1 to TK4, working site in “Z1”
Date for pulsed gas stripper assembly (preliminary) defined: 7th April 2021.
HLI Beam (Argon) for Cw Demonstrator requested:
  17th to 21st May 2021 (BSM commissioning)
  31st May to 4th June 2021 (BSM commissioning)
  2 weeks within 18th June to 16th July (preferably late)
Clarify/confirm C3+ for ESR: (11.-16.5.) from EZR with O4+, problems known by experimentalist (D. Winters)
HLI beam for CW cryostat commissioning (cryo module no.2 for 4 cavities) desired for end of June (parallel with Oxygen, from 21st June on)
Obligo shift 2020---2021…. Step motor parts (BEA): surety (Bürgschaft) found, but payment on 2020 budget in 2021 impossible.
Leakage in Z-branch: finished (also turbo pump valve repaired).
Leakage: UXC, MU3 dipole baffle plate. Plates pumped extra, beam operation uncooled.
RF Topics:
  Beam Time Operation now
  Alvarez A1 problems, A4 venting valve

## Slide 2: Reserve
HSI-RFQ “re-calibration” by software done (norm. Amp: 0,1244 Ph:323°). Corresponding 7.4 Volt at RFQ (instead of 8.3 Volt) for Uranium, 7.5 V for Ta.
Successful Tantalum beam tests on Thursday 28th January. (181Ta3+, A/q 60.5 > 59.5 U4+). RFQ Transmission 95% at 4 mA Ta3+, HIS transmission 75%. Max. RFQ voltage 7.35 Volt. Working point from “85%” on (appr. 7.1 V).