## Slide 1: Unilac – 23.2.2021
Beam time:
  protons and carbon parallel, from CH3, finished on Monday morning 22nd Feb.
  Now Setting up Gold and Lead beam (197Au8+ PIG, 208Pb4+ North), Alvarez A1 Repair..
Dirt and dust in TK1 to TK4, floor cleaned Monday 22nd Feb. Building site in “Z1”, should be made better next time.
Date for pulsed gas stripper assembly (preliminary) defined: 7th April 2021. Meeting with B. Lorentz on Wed 24th Feb, 10:30.
HLI Beam (Argon) for CW Demonstrator requested:
  17th to 21st May 2021 (BSM commissioning)
  31st May to 4th June 2021 (BSM commissioning)
  2 weeks within 18th June to 16th July (preferably late)
Leakage in Z-branch: finished, incl. switch-off (Freischaltung).
RF Topics:
  Beam Time Operation
  Alvarez A1 problems (Air venting flow rate low?), A4 venting valve

## Slide 2: Reserve
Leakage: UXC, MU3 dipole baffle plate. Plates pumped extra, beam operation uncooled.
Clarify/confirm C3+ for ESR: (11.-16.5.) from EZR with O4+, problems known by experimentalist (D. Winters)
HLI beam for CW cryostat commissioning (cryo module no.2 for 4 cavities) desired for end of June (parallel with Oxygen, from 21st June on)
Obligo shift 2020---2021…. Step motor parts (BEA): surety (Bürgschaft) found, but payment on 2020 budget in 2021 impossible.
HSI-RFQ “re-calibration” by software done (norm. Amp: 0,1244 Ph:323°). Corresponding 7.4 Volt at RFQ (instead of 8.3 Volt) for Uranium, 7.5 V for Ta.
Successful Tantalum beam tests on Thursday 28th January. (181Ta3+, A/q 60.5 > 59.5 U4+). RFQ Transmission 95% at 4 mA Ta3+, HIS transmission 75%. Max. RFQ voltage 7.35 Volt. Working point from “85%” on (appr. 7.1 V).