T. Dritschler, M. Caselle, L. Ardila, S. Chilingaryan, A. Kopmann
Flexible DAQ systems for Tera-Scale experiments

---
Challenges for modern DAQ Systems
- Modern DAQ systems are becoming increasingly more heterogeneous
- Development effort, maintainability and scalability are key challenges
- Interconnections between components need to be performant, reliable, flexible and future-proof

---
Conventional Data transfer
Application Space
Kernel Space
System Bus
Buffer

---
Conventional Data transfer
Application Space
Kernel Space
1) Data arrives and
    is placed in buffer
2) CPU fetches data
Fetch
Fetch
Place
Place
Place
Place
System Bus
3) CPU places data
    in Kernel Memory
    (Driver)
Fetch
Fetch
Buffer
Data
Data
4) CPU fetches data
    again
5) CPU places data
    into user space
    memory

---
Direct Memory Access Data transfer
Application Space
Kernel Space
1) CPU ‘Pins’
    memory segment
2) CPU Configures
    DMA engine of IO
    device, effectively
    ‘Mapping’ the
    memory to the
    device
System Bus
Mapping
Pin
DMA
Engine
Data
Configure
3) Data can now be
    placed directly into
    destination memory
    by DMA engine
    without the CPU

---
InfiniBand, the ‘de facto’ standard for RDMA
Supports both: InfiniBand AND Ethernet!
[...]

---
KIRO: An InfiniBand programming library
KIRO Server / Client
- Unidirectional data transfer from Server to Client (Clients “Pull” from Server)
- Fixed-Size memory segment
- Supports multiple connected clients per server
  KIRO Messenger (Beta)
- Layers bi-directional point-to-point messaging on top of KIRO
- Messengers can connect to multiple peers
- Fully RDMA enabled arbitrary sized memory exchange (“Push” and “Pull”)
© Mellanox
Clone it on Github!
https://github.com/ufo-kit/kiro

---
Next Generation RDMA capable computing accellerators
- Commercially available components
- Software Programmable
- Low development effort
- Easy to upgrade to newer generations, once they become available
- (R)DMA Capable
- Optimized for Machine Learning and AI applications!
Nvidia EGX A100:
Ampere GPGPU,
200Gbps Network,
Ethernet + InfiniBand
© Nvidia
Xilinx ALVEO SmartNIC:
Up to 1.1M LUTs
Up to 100Gbps Ethernet
© Xilinx

---
Ethernet is ubiquitous
Ethernet is one of the most common commercially available interconnects
Network Infrastructure
GPU
FPGA
PC / CPU
Ethernet ✓
Ethernet ✓
Ethernet ✓
Ethernet ✓
Is there a way to benefit from RDMA using Ethernet?

---
RoCE: RDMA over Converged Ethernet
RoCE uses UDP packets
and encapsulates InfiniBand
“instructions” into the
UDP payload.

---
KIRO: An InfiniBand programming library
and
KIRO Server / Client
- Unidirectional data transfer from Server to Client (Clients “Pull” from Server)
- Fixed-Size memory segment
- Supports multiple connected clients per server
  KIRO Messenger (Beta)
- Layers bi-directional point-to-point messaging on top of KIRO
- Messengers can connect to multiple peers
- Fully RDMA enabled arbitrary sized memory exchange (“Push” and “Pull”)
© Mellanox
Clone it on Github!
https://github.com/ufo-kit/kiro

---
Novel DAQ architecture using commercial HPC Components
- Versatile DAQ optimized for detector and AI applications
- High-performance ML inference on modern programmable hardware platforms
- Novel heterogeneous FPGA/GPU architecture based on emerging Ethernet protocols
On-line data path (by commercial devices)
Modular readout
Detectors
HPC
Ethernet fabrics
(hundreds Gb/s)
GPUs
Ethernet
AI
…
AI
HighFlex
Fast Feedback
…
FPGA
AI
ETH
…
FPGA
AI
ETH
…
FPGA
AI
ETH
Alveo
AI

---
Concepts for future ‘software defined DAQ’
RoCE Fabric
?
Network „Supervisor“
Packet Inspection
SB 1
...
SB 2
SB 3
„Smart“ Fabrics (Programmable)
allows „On-the-Fly“ readdressing of packets
Rerouting based on Super Burst ID / Sequence Number (?)
HYPOTHETICAL!

---
Concepts for future ‘software defined DAQ’
RoCE Fabric
GPUs
Network „Supervisor“
Computing on
FPGAs
Machine-Learning
on GPUs
Testing / Validation on CPU
...
„Smart“ Fabrics (Programmable)
allows „On-the-Fly“ readdressing of packets
Rerouting based on Operation Mode (?)
HYPOTHETICAL!
Alveo FPGAs

---
Concepts for future ‘software defined DAQ’
RoCE Fabric
Feedback
Network „Supervisor“
FAULT X
...
„Smart“ Fabrics (Programmable)
allows „On-the-Fly“ readdressing of packets
Rerouting based on Fault / Occupancy (?)
HYPOTHETICAL!

---
RDMA networking: Benefits and Drawbacks
Drawbacks:
- Integration into existing infrastructure requires (complex) retooling
- Difficult to deploy and operate from within virtualized software environments
- Full performance can only be reached when using dedicated networking hardware
Benefits:
- Computing Accelerator integration → Full support for HPC and on-line processing
- Readily available Hard- and Software → Drastically reduces development efforts
- Single, commercial components → Easy maintenance and easy upgrades to newer versions
- Highly versatile → Unify communication between all components: CPU, GPU, FPGA