## Slide 1: Unilac – 2.3.2021
Beam time:
  Gold and Lead beam (197Au8+ PIG, 208Pb4+ North).
  500-700 µA Pb67+@TK7
  Sudden closing of pump valves in TK, forced by beam pulse. Under investigation.
Date for pulsed gas stripper assembly defined: 7th April 2021. (Meeting with B. Lorentz on Wed 24th Feb).
Schedule for machine studies UNILAC under discussion.
First beam in X-branch after repair of tunnel septum.
HLI Beam (12C3+) :
  Preparation for ESR beam in May to define pollution degree (oxygen)
  check of emittance measurement setup @UN6
RF Topics:
  RF conditioning finished successfully
  A1 still a problem with “switch off” in local control..

## Slide 2: Reserve
Leakage: UXC, MU3 dipole baffle plate. Plates pumped extra, beam operation uncooled.
Clarify/confirm C3+ for ESR: (11.-16.5.) from EZR with O4+, problems known by experimentalist (D. Winters)
HLI beam for CW cryostat commissioning (cryo module no.2 for 4 cavities) desired for end of June (parallel with Oxygen, from 21st June on)
Obligo shift 2020---2021…. Step motor parts (BEA): surety (Bürgschaft) found, but payment on 2020 budget in 2021 impossible.
HSI-RFQ “re-calibration” by software done (norm. Amp: 0,1244 Ph:323°). Corresponding 7.4 Volt at RFQ (instead of 8.3 Volt) for Uranium, 7.5 V for Ta.
Successful Tantalum beam tests on Thursday 28th January. (181Ta3+, A/q 60.5 > 59.5 U4+). RFQ Transmission 95% at 4 mA Ta3+, HIS transmission 75%. Max. RFQ voltage 7.35 Volt. Working point from “85%” on (appr. 7.1 V).
Dirt and dust in TK1 to TK4, floor cleaned Monday 22nd Feb. Building site in “Z1”, should be made better next time.
Leakage in Z-branch: finished, incl. switch-off (Freischaltung).
Alvarez A1 problems (Air venting flow rate low?), A4 venting valve