## Slide 1: CBM Magnet design. Current status 04.2021.
2021 04, BINP, M.Kholopov, A.Bragin.

## Slide 2: FAIR

## Slide 3: 3D Model of CBM Magnet and cryosyctem
Iron Yoke and Support m= 105T
Cryostat, Coils and Cryostats TL m=4750kg
Branch box m=3476kg
Transfer Line m=982kg
1
2
4
3
State of affairs:
1. Magnet yoke and Support-The 3D model is finished, the calculations are done, the drawings are ready.
2. Cryostat and coils-3D model is finished, calculations are at the final stage, drawings are being prepared.
3. Branch box-the 3D model is ready, the calculation of pipelines is performed.
4. Transfer line-the conceptual design is ready, there is a clarification of the lengths of the transfer line parts and the location of the supports.

## Slide 4: 3D Model of CBM Magnet & support
Iron Yoke (m~146tons)
Coils (m~1.5tons)
Support (m~4.5tons Loading capacity 200tons)
total weight ~155 tons
1
2
3
Adjustment
positioning precision: ± 0.5 мм
The accuracy of the orientation (angular):± 0.5 mrad
Adjustment range: ±40 mm in x, y, z direction, ±4° around the Z axis.

## Slide 5: Iron Yoke drawing

## Slide 6: Iron Yoke specification
The material of the main parts is steel 1.0322.
The material of the fasteners is steel of the 8 strength class.

## Slide 7: CBM Magnet support
m= 4500 kg
2022x3470x850mm
move in 3D ±40mm
Rotation top frame ±4⁰
Loading capacity 200000 kg
strength class of fasteners - 8.8
Top frame
Gimbal longitudinal
Screw jack Rack
Cross gimbal
Intermediate frame
Sliding support
The accuracy of the alignment
Weight and size
Swivel bearing
Iron yoke
Fixation plate
- Position accuracy: ± 0.5 mm (meeting in December 2018)
- Orientation accuracy (roll): ± 0.5 mrad
-The gimbals has a fixation and alignment tool

## Slide 8: Magnet supports drawing

## Slide 9: Magnet supports drawing

## Slide 10: Top frame drawing

## Slide 11: Bottom part of the support: design and calculation
The bottom part of the support is designed for a load of 240 tons and additionally added seismic hazar (20 tons)

## Slide 12: Bottom part of the support: design and calculation

## Slide 13: The CBM magnet support: calculation
The Magnet support was calculated under a double load from the magnet (the weight of the magnet+ 150 Tons) + 2 variants of the seismic load: frontal and longitudinal (20 Tons)

## Slide 14: The CBM magnet support: calculation longitudinal variant
Parameter | Min | Max
Von Mises stress | 0 MPa | 479 Mpa*
Deformation | 0 mm | ~0.255 mm
Safety factor | 0.48 | >10

## Slide 15
The CBM magnet support: calculation frontal variant
Parameter | Min | Max
Von Mises stress | 0 MPa | 256 Mpa*
Deformation | 0 mm | ~0.242 mm
Safety factor | 0.898 | >10

## Slide 16: Cross gimbals : design and calculation
swivel head Fmax=16T
workload : 60kN
design load: 240kN
Swivel bearing Fmax=4T
The working load is the movement of the magnet.
The design load takes into account the seismic impact.
Swivel bearing Fmax=20T
Crosspiese Fmax=24T
The old design
The new design
The function of adjusting the position of the magnet in the horizontal plane and fixing its position in the working position is performed by Cross gimbals.
The Longitudinal gimbal is used to create a point of rotation on the axis of the magnet.

## Slide 17: Gimbals : design and calculation
The new design

## Slide 18: Gimbals : calculation
Parameter | Min | Max
Von Mises stress | 0 MPa | 433 MPa
Deformation | 0 mm | 0.408 mm
Safety factor | 2.21 | >10
Material: 1.6511 steel | Value
Density | 7850.000 kg/м^3
Modulus of elasticity | 215000.000 МPа
Poisson's ratio | 0.300
Yield strength | 1600.000 МPа
Ultimate strength | 1750.000 МPа
Elongation % | 12.000

## Slide 19: 3D Model of CBM Magnet and cryosyctem. Location in the CBM hall.
With the active participation of Peter Kuhl, work is being done on tracing the Transfer Line and ways to fix it in the space of the hall.

## Slide 20: 3D Model of CBM Branch box
Vacuum shell
Input interface
Cu Thermal shield
DB2 detectors iterface
He Pipelines
Valves
HADES iterface
pressure sensors pipe
pressure sensors flange
Gate valve DN160
Size: Tank shells diameter=1.5m, L=2.6m
Weight: 3476 kg

## Slide 21: Designe of the CBM Transfer line
Vacuum shell DN200
Line part
Cu Thermal shield
He Pipes
Ball joint
G10 spacer
Angle part 2
Angle part 3
Angle part 1
Total length of the transfer line: L=29m
Weight: 982 kg
Straight section parts of TL:
croosection

## Slide 22: 3D Model of CBM Transfer line
Vacuum shell DN200
Angle part of TL
Cu Thermal shield
Ball joint
G10 spacer
Angle vacuum shell DN250
He Pipes
Metal hose

## Slide 23: 3D Model of CBM Transfer lines supports
Sliding support
Spring-sliding support
We suggest using 2 types of supports to the Transfer Line.
-Sliding support for the upper part (axial movement only).
-Sliding support with compensating springs for the lower part (axial movement and vertical compensation+ - 20mm).
The Transfer Line fixing points are assumed to be on the Cryostat and Branch Box.
Sliding support m=42kg
Spring-sliding support m=58kg
Clamp DN200
Sliding part
PTFE plate
Support plate
Spring block
Bracket

## Slide 24: Thank you for your attention!