Update Central Space Frame(CSF)

---
The mainframe will be made out of four carbon composite parts, two of which are identical.

---
The frames will be a tube or hollow profile.
By only providing local reinforcements, precisely where they are needed, we can reduce the weight even further.
sectional view
local reinforcements

---
Various brackets and fixings made of aluminum are connected to the mainframe.

---
We made an optimization of the vertical aluminum connectors.
The point was a potential collision between the STT straw tubes and the connector.

---
The moving works via ceramic roller which rolls over hard anodized aluminum shaft which will be attached to a clip profile, for example available by the company item.
The clip profile is jammed into a 8 mm groove, which will be integrated in the Barrel DIRC beams in the final design.
Roller
Clip profile
Aluminum shaft

---
The moving works via ceramic roller which rolls over hard anodized aluminum shaft which will be attached to a clip profile, for example available by the company item.
The clip profile is jammed into a 8 mm groove, which will be integrated in the Barrel DIRC beams in the final design.
Roller
Clip profile
Aluminum shaft

---
Conclusions:
-	We are in contact with several companies which are specialized for such carbon composite parts
-	Together with our colleagues from Jülich, we are planning a prototype for testing the connections between he	CSF and the target pipe
Thank you for your attention!