The latest DISC DIRC test beam results
using a glass radiator
Peter Koch on behalf of AG Düren
Panda Coll. Meeting XXXIX
Dec 12 - Dec 16, 2011

---
Testbeam Setup Design
- Use a quarter disc radiator
- At least 5 light guides on the outer rim
- Spatial
  resolution
  of sensors
  ~1mm

---
The Radiator
- Produced
  by ZygoLOT
- from Borofloat
- honed sides
- 840mm
  x 840mm
  x 21mm

---
The Light Guides
- 15mm Plexiglas
- 74mm x 78mm
- Polished by our workshop
- VM 2000 reflective foil
- BC 630 optical grease

---
The Sensors
- Hamamatsu
  H10151B sensor
- 16 strip PMT
- 1mm channel pitch
- Elastosil Silicon Pads

---
The Detector Elements
Focussing LG
PCB for
HV and data
PMT

---
Setup with readout board

---
First lab-tests with
Quartz
Light Guides

---
Focussing Light Guides - Specs
- imaging 25 degrees onto 32mm focal plane length
- foreseen for Philips dSiPM sensors, cooled (~253K)
- 1mm insulating gap between FLG block and sensor

---
Focussing Light Guides
- HERAEUS synthetic fused silica
- ICOS in Beckenham, UK (South London) shaping and polishing
- evaporated
  Al reflective coating
  on curved surface

---
Exploratory test setup

---
Measurement Images
z0=5mm
z0=10mm
z0=15mm

---
Quartz FLGs – first conclusions
- two sample pieces have been manufactured
- the challenge of the curved surface is mastered
- very first quality measurement
    - improvised setup
    - analysis chain run through
- for the one angle measured just within specs
- measure full set of angles
- measure light intensities

---
Some
Online-Results

---
Scattered light from outside the box
Darkcount,
without molleton
Darkcount,
with molleton

---
Calorimeter Crosstalk
- Calorimeter in channel 119
- Channel 120 was broken
- Got 315165 signal in empty channel 118

---
Calorimeter Crosstalk
All 315165 events in channel 118
are in coincidence with calorimeter signal

---
Some Measurements

---
Scan in y-direction

---
Y-scan
50cm in 5cm steps

---
Scan in x-direction

---
x-scan PMT5
65cm in 5cm steps

---
Scan in different angles

---
Angle scan PMT3
6° – 9° in 0.2° steps

---
Conclusions
- Setup successfully tested
- Light guides can be produced
Outlook
- Analysis
- Next test with
  - more sensors
  - Borofloat light guides
  - Mirrored rims on radiator