## Slide 1
Status of Finnish in-kind components for accelerators (Super-FRS)
Tuomas Grahn
Helsinki Institute of Physics &
University of Jyväskylä
Super-FRS Experiment Collaboration meeting
Walldorf, 27 April 2023

## Slide 2
Beam indentification at Super-FRS
Measurements in the B𝜌-TOF-𝛥E method:
D is despersion, M is magnification and B𝜌0 is reference magnetic rigidity
A and Z
Measured quantities

## Slide 3
Finland will provide detectors…
…that measure
Enegy loss 𝛥E ⇒ Z (MUSIC detectors)
Particle position in the xy plane ⇒ B𝜌 (GEM-TPC detectors)
In addition, beam profile (SEM-grid) detectors are needed

## Slide 4: Beam insertion device seven different variants
xy
xy
TOF
MUSIC
slit
SEM-grid
GEM-TPC
Media board
Calibration tool holder
Conceptual design report conditionally accepted.
Mechanical design at University of Jyväskylä (J. Tuunanen)

## Slide 5: MUSIC 𝛥E detector
The MUSIC detector is in final desing phase
Mitigations to problems observed in summer 2022 beam time ongoing
Design by GSI DL (B. Voss et al.)
Field cage
Pneumatic drive

## Slide 6: GEM-TPC position detector
The project is in conceptual design phase
In collaboration between HIP (F. Garcia) and GSI DL (B. Voss et al.)
So far the readout electronics have been a problem, new test results just published (by M. Luoma et al.)

## Slide 7: SEM-grid beam profile
Based on the Fermilab design, produced by Hbar Technologies, LLC
Holding structure designed by University of Jyväskylä (J. Tuunanen)
50-75 𝜇m Au-plated W wires in x and y
Signal readout through POLAND digitisers
SEM-grid on a pneumatic drive
Target SEM-grid

## Slide 8: Super-FRS flask
The Super-FRS flask (Finland) and PANDA (Sweden) pbar flask were tendered together by FAIR. The contract was awarded to Billfinger Noell GmbH.
We are now entering the production phase
PSI flask
Status at the moment

## Slide 9: Helium Recovery Unit
Recovers >98% of (precious!) buffer gas He 6.0
Purifies buffer gas at each cycle
Final design report accepted
Purchasing underway. Test and Assembly of first components starts in the coming weeks.
Applied for beamtime in the GSI engineering run 2023
Developed in collaboration with GSI and ELI-NP
Notes: Essential unit for the CSC operation.
For reference a standard gas bundle – 12 gas cylinders 50l each will last only 2.5 days without HRU. With HRU it is ~1 year of continuous operation.
And much more