## Slide 1: Status of LH2 target G. Authelet, A. Corsi, A. Lagni, Ch. Mailleret CEA/IRFU R3B WS, June 8th 2022
GET_INvolved Programme

## Slide 2
LH2 target in 2022
April 4th-8th: 4th : 5-cm Target installation;
5th : 10-6 mbar vacuum reached in 20h;
6th : PLC and software update;
7th : Cooling.
April 12th-15th: 12th: 5-cm target filling, parameters adjusments;
13th-14th : target stability values fine adjustments;
15th: Target emptying and warming.
May 16th-June 8th: target filled for S522 & S509;
Since today: warm up and vent for the end of the week.
Notes: Programmable Logic Controller

## Slide 3
LH2 target in 2022
To be monitored by shifters

## Slide 4
LH2 target in 2022
Target filling April, 16th
8h20: Gas insertion
14h25: Target filled

## Slide 5
LH2 target in 2022
Target filling took 6 hours – should always count at least 10 hours since this time, strongly depends on environment.
Target running stable for 23 days!
On Sunday 29th afternoon (tuning of 12C beam): The temperature sensor on the return circuit become unstable, and indicated 1 degree more, target pressure and vacuum increased for half an hour.
A possible explanation is that the top of the target’s body, where is installed the temperature sensor, was hit by intense beam (106 pps).
Decided to not try to fix the sensor issue because too close from beamtime, run S522 part 2 with lower pressure to increase density and stability.
On Tuesday 31th: The probe return to normal after power cycling. Adding H2 between two beams. Everything is working fine, target is stable for S509.

## Slide 6
LH2 target in 2022
Target ‘’life’’ on 3 weeks
Working conditions: pressure 943/953 mbar
temperature : 20,05/20,12 K
S522 part 2
End of S522 part 1
Gas adding
Begining S509
Begining of S522 part 1

## Slide 7
LH2 target in 2022
Wednesday morning when the beam finishes (8AM):
Pedestal run FOOT;
Bias off FOOT and power off ADC boards;
Warm up the target ( Gilles in remote and me);
Pump the H2;
Target at room temperature and fully secured by Friday.

## Slide 8
Backup
BEAM
How it works
Cryocooler
1st stage (50K)
2nd stage (4,2K)
Condenser/Liqufier
Target
Cryostat under vacuum

## Slide 9
LH2 target in 2022

## Slide 10
Backup