## Slide 1: STT Detector risk’s assessment

## Slide 2: STT detector work packages
Straw Tubes modules
Straw Tracker mechanics
Front-End Electronics
  Analog electronics
  Digital electronics
Gas system
DAQ
Slow Control
Online tracking
Monitoring and calibration
+ Central Frame shared with MVD and target groups
+ Integration shared with all the neighboring detectors

## Slide 3: Straw Tube modules
Basic components have been identified and developed.
No major risks.
Two sites (LNF & JFZ) are equipped with the necessary tools to start production.

## Slide 4: Straw Tracker mechanics
The mechanical layout of the STT is well advanced.
Support structure prototype realized.
Electronics housing and connection worked out: prototypes available.
The proposed solution integrates also the gas distribution.
Open point: electronics design optimization under development
No major risks

## Slide 5: Electronics Development
Basic elements have been identified:
New ASICS for analog readout
New version of TRB (v3) for the Digital part
Two risks have been identified:
TOT will not provide enough resolution;
New ASICS development will take more time
dE/dx using FADC
Delay in STT commissioning

## Slide 6: GAS system
A system to automatize and remote control of the gas flow parameters has been designed, with the possibility to switch to manual/local operation.
– setting the ratio of the two components in the gas mixture;
– quantifying the gas flow;
– setting the gas pressure; – controlling the temperature.
Basic elements have been identified. Prototype are under tests
No major risks
up and down gas pipes.
Gas pipes: steel,4mm 
Fixing element

## Slide 7: DAQ
Central tracker : 4636 straws
Drift time ~ 200 ns
Time measurement: req. electronics resolution ~ 1 ns
sensitivity (threshold) ~ 2 fC
dE/dx for PID: MIP: signal charge 106-108 e-
10% resolution in 24 layers
detector capacitance: ~ 10-15 pF (9 pF/m)
Hit rates up to 800 kHz/channel
Common Clock Distribution
(i.e SODA)
FE
DB
Panda DAQ - network
Developments in agreement with the general requirements of the whole PANDA DAQ. No major risks

## Slide 8: Slow Control
STT parameters to control are:
Gas mixture composition;
Pressure, temperature;
HV, LV
Position monitor
No particular risks have been identified. Everything is under development following PANDA general DCS prescriptions.