Status of the DiRICH Backplane
PHOTONIS
XP85112-S-BA

---
New configuration with SAMTEC plugs nedd a new backplane
 https://www.samtec.com/products/qrm8-052-05.0-l-d-a-k-tr

---
old
Technical drawings all from Andreas Gerhardt

---
new

---
  SMD-Socket (“Buchsenleiste”)
Hole for HV plug
(10 mm dia.)
Dimensions
- HV-divider
- PMT
- plug hole
scale

---
Plug and socket from Lemo catalog 2007
→ found easily on web, but not to buy...
Candidate for socket
5 kV
( HV within FR4 board 30 kV/mm	→ 16 planes: 1.5mm/32 = 47um → 1.4 kV
      → 8 planes: 1.5mm/16 = 94um → 2.8 kV )

---
Alternative for plug and socket:
GSI stockroom

---
Andreas Gerhardt produced a
mock-up to play with.

---
Playboard will be printed in plastic
Tight config
Good
– HV-divider space
– illumination with pulser
Bad
– in case camera goes
through backplane

---
HV - divider
Specs:
derating at high temperatures

---
SMD 2010 = 5x2.5 mm2
0.5 Watt
(500 V 1 mA)
HV-Divider
2kV2 / 1.6 MΩ = 2.5 Watt
Tells this nice
picture the truth???
∆T = 50 degree
No PTFE

---
Emissivity of washers
By hand:
Black 183 deg
Brass 165 deg
Steel 145 deg
Emissivity important
Dull	e=0.95
Half dull	e=0.85
Half shiny	e=0.6
Shiny	e=0.3
T(K) = Tvis / e

---
20 deg
Camera sees
< 40 deg
for non black bodies
For e=0.5
Tobs.=30 deg
Ttrue=(30-20)/0.5 + 20 deg
40 deg

---
Calibration of emissivity
Soldered 2010 0.5 Watt resistor on soldering tip
and measure at ~ 100 degree
Emissivity = 0.85 (DMM and camera show same T)

---
To get dT=30 deg at ambient
T=50 deg one should use
→ 60% of max power specs.
2.5 Watts / 0.6 = 4.2 Watts
Better use 5 resistors (2512/1Watt)

---
Summary
Details of mechanical layout take more time than anticipated
The HV-divider resistors (1.6 Mohm over the plate)
have to withstand 5 Watts